## Slide 1
Training Module 1
The Generic Framework
concept and the
multicriteria assessment
methodology – SBE
Method

## Slide 2: Origin of SBE Method: the Green Building Challenge
Research process started in 1998 coordinated by iiSBE (international initiative for a Sustainable Built Environment)
OBJECTIVE
Develop an open-source transnational methodology for assessing the sustainability of buildings based on the principle of contextualization
RESULT: SBTool

## Slide 3: SBE Method GENERIC FRAMEWORK PRINCIPLE
Generic Framework
A generic multicriteria assessment system for rating the sustainability performance of the built environment.
Not operational, to be used a GF needs to be contextualized.
National / Regional Tools
Operational multicriteria assessment systems.
Derived from the common Generic Framework through a contextualization process.

## Slide 4: SBTool
SBTool Canada
SBTool Japan
SBTool France
SBTool Brazil
SBTool: Generic Framewok at building scale (1998 first version)

## Slide 5: Protocollo ITACA
SBTool CZ
SBTool PT
VERDE

## Slide 6: CONTEXTUALIZATION PROCESS
SBTool
GENERIC FRAMEWORK
CRITERIA SELECTION
PERFORMANCE SCALE
WEIGHTS
CONTEXT
SBTool ITALY

## Slide 7
Design Phase
Self-assessment scores
95
Max. potential
low-level parameters:
129
2
Active low-level
mandatory parameters:
10
Active Weights
Weighted scores
A
8,1%
3,7
37,5%
2,7
39,4%
2,6
4,2%
3,5
5,6%
3,4
F
3,4%
2,8
1,8%
3,3
2,83
.
Self-assessment scores for
ProjectX, BigTown, SomePlace
Whole building basis, All Criteria Focus
Maximum version
Social, Cultural and Perceptual Aspects
SBTool 2019
E Service Quality
Project Information
Relative Performance Results
C+
Assumed life span is 75 years, and monetary units are in EUR
Amortization rate for embodied energy of existing materials is set at 0 %
With current context and building data, the number of active low-level
parameters is:
G Cost and Economic Aspects
W e I g h t e d p r o j e c t s c o r e
The number of active mandatory criteria with a score of less than 3 is:
To see a full list of Issues, Categories and Criteria,
go to the ParametersB worksheet.
Site Regeneration and Development, Urban Design and Infrastructure
B Energy and Resource Consumption
C Environmental Loadings
D Indoor Environmental Quality
5,0
4,0
3,0
2,0
1,0
0,0
A
B
C
F
G
E D
0 = Acceptable Practice; 3 = Good Practice; 5 = Best
Practice
Percent weights of active Issues
A B C
D E F G
SBTool assigns a sustainability score (-1 to +5) to a building.
Municipal Building
Marseille

## Slide 8
GREEN BUILD
ING CHALLENGE
GREEN BUILDING CHALLENGE

## Slide 9
Argentina | University of Buenos Aires | Italy | Environment Park
Austria | Ökologie Institut | Japan | Utsunomiya University
Australia | University of New South Wales | Korea | Korean Institute of Energy Research
Brazil | Unicamp | Netherlands | Novem, DHV
Canada | BCBC | Norway | Norwegian Building Research Institute
Chile | Chilean Chamber of Construction | Poland | NAPE
China | Tsinghua University | South Africa | CSIR
Finland | Motiva | Spain | Ministry of Public Works and Transp.
France | CSTB | Sweden | KTH
Germany |  | USA | Department of Energy
Greece | University of Thessaloniki | Wales | University of Cardiff
Hong Kong | University of Hong Kong | International Framework Committee | 

## Slide 10
US Team contributed in the development of

## Slide 11: SBTool Spain renamed as

## Slide 13
French Team contributed in the development of

## Slide 18
The Japanese Team contributed in the development of

## Slide 20: Modular structure
ISSUE A
ISSUE B
ISSUE C
ISSUE D
ISSUE (N)
Issues represent general themes, recognized as relevant for assessing the sustainability of a building or neighborhood

## Slide 21: Hierarchic levels
Issues: general themes, recognized as relevant for assessing the
sustainability of a building
Categories: particular aspects of areas
Criterion: each assessment entry related to a specific aspect of the category whom the criterion belongs to
Indicator: physical quantity or qualitative scenario that allows to quantify the performance with respect to the assessment criterion. Quantitative indicators have a unit of measure.

## Slide 22: Hierarchic levels
Issue A
Category A.1
Category A.2
Category A.N
Criterion A.1.2
Criterion
A.1.1
Criterion A.2.n
Criterion A.2.2
Criterion
A.2.1
Criterion
A.1.n
Criterion
A.Nn
Criterion
A.N2
Criterion
A.N1
Indicator
Indicator
Indicator
Indicator
Indicator
Indicator
Indicator
Indicator
Indicator

## Slide 23
Notes: New slide

## Slide 24
Key Performance Indicators (KPIs):
A core set of indicators, mandatory in all cases
Considered as minimum requirements for addressing sustainability
Defined and calculated following common standardized procedures
Allow to compare - on a common basis - different buildings, neighbourhoods, or cities among the Mediterranean countries
SMC Key Performance Indicators

## Slide 25
25
SBTool: 8 issues – 25 categories – 80 criteria – 17 KPIs
SBTool – Building scale
Notes: Slightly modified: title row added

## Slide 26: SNTool – Neighbourhood scale
SNTool: 10 issues – 43 categories – 133 criteria – 14 KPIs
A - Use of land and biodiversity | B - Energy | C - Water | D - Solid Waste | E - Environmental quality | F - Transportation and mobility | G - Social Aspects | H - Economy | I - Climate Change: mitigation and adaptation | L - Governance
A1 - Use of land | B1 - Energy infrastructure | C1 - Water infrastructure | D1 - Solid waste collection infrastructure | E1 - Air quality | F1 - Performance of mobility service | G1 - Accessibility (disabled persons) | H1 - Economic performance | I1 - Climate change mitigation | L1 - Urban Planning
A2 - Green urban areas | B2 - Energy consumptions | C2 - Water consumption | D2 - Solid waste management | E2 - Noise | F2 - Green mobility | G2 - Housing | H2 - Employment | I2 - Adaptation to the climatic action: heatwaves and increase of temperature | L2 - Management and community involvement
A3 - Biodiversity and ecosystems | B3 - Renewable energy | C3 - Effluents management |  | E3 - EMF exposure | F3 - Safety in mobility | G3 - Availability of public and private facilities and services | H3 - Innovation | I3 - Adaptation to the climatic action: pluvial flood | L3 - Public buildings operation
 |  |  |  | E4 - Environmental impacts | F4 - Urban morphology and transportation | G4 - Education | H4 - ICT infrastructure | I4 - Adaptation to the climatic action: fluvial and coastal flood | 
 |  |  |  |  |  | G5 - Social inclusion |  | I5 - Adaptation to the climatic action: drought | 
 |  |  |  |  |  | G6 - Safety |  | I6 - Adaptation to the climatic hazard: wildfire | 
 |  |  |  |  |  | G7 - Health |  | I7 - Climatic hazard: wind | 
 |  |  |  |  |  | G8 - Food security |  |  | 
 |  |  |  |  |  | G9 - Culture and Heritage |  |  | 
 |  |  |  |  |  | G10 - Perceptual |  |  | 

## Slide 27: SCTool – City scale
5
SCTool: 10 issues – 39 categories – 99 criteria – 10 KPIs
A - Use of land and biodiversity | B - Energy | C - Water | D - Solid Waste | E - Environmental quality | F - Transportation and mobility | G - Social Aspects | H - Economy | I - Climate Change: mitigation and adaptation | L - Governance
A1 - Use of land | B1 - Energy infrastructure | C1 - Water infrastructure | D1 - Solid waste collection infrastructure | E1 - Air quality | F1 - Performance of mobility service | G1 - Accessibility (disabled persons) | H1 - Economic performance | I1 - Climate change mitigation | L1 - Urban Planning
A2 - Green urban areas | B2 - Energy consumptions | C2 - Water consumption | D2 - Solid waste management | E2 - Noise | F2 - Green mobility | G2 - Housing | H2 - Employment | I2 - Adaptation to the climatic action: heatwaves and increase of temperature | L2 - Management and community involvement
A3 - Biodiversity and ecosystems | B3 - Renewable energy | C3 - Effluents management |  | E3 - EMF exposure | F3 - Safety in mobility | G3 - Availability of public and private facilities and services | H3 - Innovation | I3 - Adaptation to the climatic action: pluvial flood | L3 - Public buildings operation
 |  |  |  |  |  | G4 - Education | H4 - ICT infrastructure | I4 - Adaptation to the climatic action: fluvial and coastal flood | L4 -Equity
 |  |  |  |  |  | G5 - Social inclusion |  | I5 - Adaptation to the climatic action: drought | 
 |  |  |  |  |  | G6 - Safety |  | I6 - Adaptation to the climatic hazard: wildfire | 
 |  |  |  |  |  | G7 - Health |  |  | 
 |  |  |  |  |  | G8 - Food security |  |  | 

## Slide 28: Structure of the tools
E | Social Aspects | 
E1 | Accessibility and safety | 
 | E1.1 | Sidewalks and access to buildings designed for access by physically disabled persons
 | E1.2 | Barrier-Free Accessibility of the District
 | E1.3 | Ease of access to and use of public transport for physically disabled persons
 | E1.4 | Objective/subjective safety measure
E2 | Traffic and mobility services | 
 | E2.1 | Performance of the public transport
 | E2.2 | Availability of car sharing services
 | E2.3 | Measures to limit traffic of cars and trucks passing through the local area
 | E2.4 | Quality of pedestrian and bicycle network
 | E2.5 | Availability of sheltered bicycle parking facilities
E3 | Communication services | 
 | E3.1 | Availability of a broadband communication network
 | E3.2 | Access to a broadband communication network
ISSUE
CATEGORY
CRITERIA
Notes: Title modified

## Slide 29: Criteria and indicators
CRITERION | NAME | INDICATOR | UNIT OF MEASURE
C2.2 | Efficiency in water use | Volume of water supplied minus the volume of utilized water divided by the total volume of water supplied | %
E1.2 | Particulate matter (PM10) concentration | Number of days within a year that PM10 concentration exceeds the daily limit | days/yr
B2.1 | Total final thermal energy consumption for building operations | Aggregated annual total final thermal energy consumption per aggregated indoor useful floor area | kWh/m2/yr
Notes: Title modified

## Slide 30
Notes: New slide

## Slide 31: Criteria description
Notes: New slide replacing «SNTool – Indicators’ description (D3.1.1)»

## Slide 32: SBE Method Assessment Process
Notes: Slide modified

## Slide 33: Assessment process: 3 steps

## Slide 34: 1 – Characterization of criteria
CRITERIA
Assessment of indicators

## Slide 35: SNTool – Indicators’ values
CRITERION NAME
INDICATOR
VALUE
C2.2
Efficiency in water use
Volume of water supplied minus the volume of utilized water divided by the total volume of water supplied
75 %
E1.2
Particulate matter
(PM10)
concentration
Number of days within a year that PM10 concentration exceeds the daily limit
60 days/yr
B2.1
Total final thermal energy consumption for building operations
Aggregated annual total final thermal energy consumption per aggregated indoor useful floor area
90 kWh/m2/yr

## Slide 41: 2 – Normalization (score assignement)

## Slide 42: 2 – Normalization (scoring scale)

## Slide 43: Scoring scale (scaling interval -1,+5)
44
Laws/regulations
Technical standards Scientific literature Statistics data Simulations
ASSOCIATION OF A SCORE TO
THE INDICATOR VALUE

## Slide 44: 2 - Normalization

## Slide 45: Higher is Better
SCORE
INDICATOR’S VALUE
= benchmarks (minimum acceptable performance and best practice)

## Slide 46: Higher is Better
SCORE
INDICATOR’S VALUE
= benchmark (minimum acceptable performance and best practice)

## Slide 47
Higher is Better
45%
1,5
Notes: This slide replace the old example

## Slide 48: Lower is Better
SCORE
INDICATOR’S VALUE
= benchmark

## Slide 49
B1.2 Energia primaria per riscaldamento
Lower is Better
27 Kg CO2 eq/m2
2,7
Notes: This example replace the old one

## Slide 50: Qualitative criterion

## Slide 51: Qualitative criterion
Notes: New added slide

## Slide 52: 3 - Aggregation

## Slide 53: Aggregation
SCORE OF CATEGORIES
OVERALL
SCORE
SCORE OF ISSUES
Notes: This slide replace the old one

## Slide 54
2,1
C3 – Effluents Manag.
C2 – Water Consumption
C1 – Water Infrastructure
D - Waste
A – Use of Land
E – Env. Quality
F – Mobility
C - Water
C1.1
C1.2
C2.1
C2.2
C3.1
C3.2
C3.3
30%
20%
50%
50%
25%
25%
29%
Notes: This slide replace the old

## Slide 55
2,1
C3 – Effluents Manag.
C2 – Water Consumption
C1 – Water Infrastructure
D - Waste
A – Use of Land
E – Env. Quality
F – Mobility
C - Water
C1.1
C1.2
C2.1
C2.2
C3.1
C3.2
C3.3
30%
20%
50%
50%
25%
25%
29%
Notes: This slide replace the old

## Slide 56
Peso dei criteri in una categoria: esempio
Score of Category C3 - Effluents management
Criterion | Score | Weight | Weighted score
C3.1 Water treatment | 1,2 | 0,30 | 0,4
C3.2 Public wastewater | 0,5 | 0,20 | 0,1
C3.3 Household sanitation | 1,3 | 0,50 | 0,7
 |  |  | 1,1
C3 SCORE
1,2
Notes: New slide

## Slide 57
2,1
C3 – Effluents Manag.
C2 – Water Consumption
C1 – Water Infrastructure
D - Waste
A – Use of Land
E – Env. Quality
F – Mobility
C - Water
C1.1
C1.2
C2.1
C2.2
C3.1
C3.2
C3.3
30%
20%
50%
50%
25%
25%
29%

## Slide 58
Peso dei criteri in una categoria: esempio
Score the Issue C - Water
Category | Score | Weight | Weighted score
C1 Water Infrastructure | 1,5 | 0,5 | 0,8
C2 Water Consumption | 0,7 | 0,25 | 0,2
C3 Effluents management | 1,2 | 0,25 | 0,3
 |  |  | 1,2
SCORE C
1,3

## Slide 59
2,1
C3 – Effluents Manag.
C2 – Water Consumption
C1 – Water Infrastructure
D - Waste
A – Use of Land
E – Env. Quality
F – Mobility
C - Water
C1.1
C1.2
C2.1
C2.2
C3.1
C3.2
C3.3
30%
20%
50%
50%
25%
25%
29%

## Slide 60
Peso dei criteri in una categoria: esempio
Final score
Category | Score | Weight | Weighted score
A USE OF LAND | 2,1 | 0,21 | 0,4
C WATER | 1,3 | 0,29 | 0,4
D SOLID WASTE | 2,5 | 0,17 | 0,4
E ENVIRONMENTAL QUALITY | 3,4 | 0,08 | 0,3
F MOBILITY | 2,4 | 0,25 | 0,6
 |  |  | 2,1
FINAL SCORE
2,1

## Slide 62
SBE Method
Contextualisation

## Slide 63: Contextualisation
The process takes place in 3 steps:
Selection of criteria
Benchmarking
Weighting

## Slide 64: Selection of criteria
Selection of issues, categories and criteria to be included in the tool.
KPIs are mandatory.
Recommended number of criteria is 40-50.

## Slide 65
torino
IRBID
BARCELONA
GENOVA
SOUSSE
KPI

## Slide 66
SNTool PASSPORT

## Slide 67
Benchmarking
BENCHMARK 5 – EXCELLENT PERFORMANCE
BENCHMARK 0 – MINIMUM ACCEPTABLE PERFORMANCE

## Slide 68
68
Laws/regulations
Technical standards
Scientific literature
Statistics data
Simulations
ASSOCIATION OF A SCORE TO
THE INDICATOR VALUE
Benchmarking

## Slide 69: Weighting
The process takes place in 3 steps:
Weight of issues
Weights of categories
Weights of criteria

## Slide 70
1,8

## Slide 71
Peso dei criteri in una categoria: esempio
Weight of Issues

## Slide 72
Peso dei criteri in una categoria: esempio
Weight of Issues : priority factors
Issue | Priority
A USE OF LAND | 2
B ENERGY | 3
C WATER | 5
D SOLID WASTE | 2
E ENVIRONMENTAL QUALITY | 3
F MOBILITY | 2
G SOCIAL ASPECTS | 4
H ECONOMY | 4
I CLIMATE CHANGE | 5
J GOVERNANCE | 3
1 = Low priority
5 = High priority

## Slide 73
Peso dei criteri in una categoria: esempio
Weight of Issues
Issue | Priority | Weight | Weight in %
A USE OF LAND | 2 | 2 : 33 = 0,06 | 6%
B ENERGY | 3 | 3 : 33 = 0,09 | 9%
C WATER | 5 | 5 : 33 = 0,15 | 15%
D SOLID WASTE | 2 | 2 : 33 = 0,06 | 6%
E ENVIRONMENTAL QUALITY | 3 | 3 : 33 = 0,09 | 9%
F MOBILITY | 2 | 2 : 33 = 0,06 | 6%
G SOCIAL ASPECTS | 4 | 4 : 33 = 0,12 | 12%
H ECONOMY | 4 | 4: 33 = 0,12 | 12%
I CLIMATE CHANGE | 5 | 5 : 33 = 0,15 | 15%
J GOVERNANCE | 3 | 3 : 33 = 0,09 | 9%
 | 33 |  | 100%

## Slide 74
1,8

## Slide 75
Peso dei criteri in una categoria: esempio
Weight of Categories

## Slide 76
Peso dei criteri in una categoria: esempio
Weight of Categories: priority factor
Category | Priority
C1 Water Infrastructure | 3
C2 Water Consumption | 4
C3 Effluents management | 2
 | 9
1 = Low priority
5 = High priority

## Slide 77
Peso dei criteri in una categoria: esempio
Weight of Categories (C1,C2,C3) in an Issue (C)
Category | Priority | Weight | Weight in %
C1 Water Infrastructure | 3 | 3 : 9 = 0,33 | 33%
C2 Water Consumption | 4 | 4 : 9 = 0,44 | 44%
C3 Effluents management | 2 | 2 : 9 = 0,22 | 22%
 | 9 |  | 100%

## Slide 78
1,8

## Slide 79: Weight of criteria: impact factor
To each criterion it must be assigned an impact factor Pk
I : INTENSITY OF POTENTIAL EFFECT (1-3 POINTS)
(Minor, Moderate, Major)
E : EXTENT OF THE POTENTIAL EFFECT (1-5 POINTS)
(Block, Neighborhood, Disrict, Urban/Region, Global)
D : DURATION OF THE POTENTIAL EFFECTS (1-5 POINTS)
(1-10 years, 3-10 years, 10-30 years, 30-75 years, >75 years)
A: ADJUSTEMENT IN RELATION TO LOCAL PRIORITIES
Pk = I x E x D x A

## Slide 80
Peso dei criteri in una categoria: esempio
Impact factor
Criterion | Intensity | Extent | Duration | Adjustment | Pk
I1.1 Greenhouse gas emissions | 3 | 5 | 5 | 1 | 75
E1.2 Particulate matter concentration (PM10) | 3 | 4 | 2 | 1 | 24
E2.1 Ambient daytime noise conditions | 3 | 2 | 1 | 1,3 | 7,2

## Slide 81
Peso dei criteri in una categoria: esempio
Weights of the criteria in a Category (C2 Water consumption)
Criterion | Impact factor | Weight | Weight in %
C2.1 Total Water Consumption | 31 | 31 : 105 = 0,30 | 30%
C2.2 Efficiency in water use | 25 | 25 : 105 = 0,23 | 23%
C2.3 Consumption of potable water in residential buildings | 22 | 22 : 105 = 0,22 | 21%
C2.6 Re-use of rainwater in residential buildings | 27 | 27 : 105 = 0,26 | 26%
 | 105 |  | 100%

## Slide 82
CASE STUDIES

## Slide 83: Neighborhood “AURORA” – Udine, Italy
land area: 1 km2
Residents: 4.455 origin: military zone
development period: 1950-80
social housing area
333 building
Visual representation of indicators

## Slide 84: SCENARIO OF INTERVENTION
EXPERIMENTAL CITY PROJECT
Major urban rigeneration interventions to be implemented:
energy efficency upgrade of buildings
cycle-route network completion
urban farming

## Slide 85: MAIN OUTCOMES
Yellow line – Diagnosis
Blue line – Targets
Green line – Experimental City’s scenario

## Slide 86: Assessment of “Aurora” neighborhood

## Slide 87: CHECKING THE SUSTAINABILITY VALUE: calculation (SN tool) vs perception (inhabitants)
greening activities
information campaigns
meetings on the ground

## Slide 88: EcoQuartier Parc des Calanques - Francia
-118 ha
-Urban redevelopment area
-11,000 inhabitants

## Slide 89: OVERVIEW OF THE TESTING AREA FEATURES
From urban renewal area to econeighbourhood (EcoQuartier)
Connexion to the rest of the city 1372 social housing renovated
Creation of public equipement : urban parc, theater, neighbourghood house, 2 sport facilities
Keeping up the connection with inhabitants (1st renovation in 2011!)

## Slide 90: Sustainability assessment of the intervention scenario

## Slide 91: ZAC du Bon Lait-Lyon, Francia
Text here
The two main goals of this new neighborhood:
  Conversion of an industrial and urban brownfield
  Creation of a new neighborhood, to add a new district center in the Gerland district
8 ha
1565 dwellings
1 ha of green space
s
75

## Slide 92: Urban and Building Scale Pilots in Barcelona
The EIXAMPLE is a district of Barcelona between the old city and what were once surrounding small towns, constructed in the 19th and early 20th centuries.
The EIXAMPLE is an urbanistic plan
designed by Ildelfons Cerdà

## Slide 93: Urban and Building Scale Pilots in Barcelona
77
Urban scale: ILLA EFICIENT
Building scale:
Agency Housing of Catalonia
Public administration - office
ILLA EFICIENT is the block pilot to design energy refurbishment plan of the Eixample district.

## Slide 94: ILLA EFICIENT – Urban Scale Pilot in Barcelona
9%
5%
Buildings Age
Before 1975
1975 - 2000
2000 -2015
86%

## Slide 95
MAIN OUTCOMES – ILLA EFICIENT
Good performance of the public transport service
Good performance of recycling process
Good performance of solid waste and recycling collection points
STRENGHTS
WEAKNESSES
Non land to development
High residential density
High density of traffic
High noise level

## Slide 96: ILLA EFICIENT Urban scale pilot

## Slide 97
CESBA MED case study in Sant Cugat del Vallès,
Monestir-Sant Francesc Neighborhood Strategic Plan
Key figures of the case study
Surface of the project: 44 ha
Number of inhabitants: 11.060 inhabitants
Cost of the project: 11 M€
Duration: 7 years from 2017 to 2023
Number of housing: 4.270 housing
Size of residential area: 457.929 m²
Size of offices and commerce area: 99.553 m²
Green spaces: 4,7 ha of green space
Water consumption in the area: 4.397.320 m3

## Slide 98: OVERVIEW OF THE TESTING AREA FEATURES
Two scenarios have been considered.
The first scenario aimed to reduce the mobility impact in the area according to the Urban Pedestrian Plan.
The second scenario was focused to reduce the private energy consumption for building operations promoted with subsidies and discounts of municipal taxes for the energy.

## Slide 99: URBAN SCALE MAIN OUTCOMES
The tool allows to graph the current situation and what’s the target in the future.
Different scenarios are easily visualized, and it is a strong tool in the decision-making process.
The municipality has started to implement the scenario 1
Scenario 2 seems to be difficult to be implement because private investment is needed and the result is not far from the current state.
Target
Scenario 1
Scenario 2

## Slide 100
HELLENIC PILOT OVERVIEW
Town Hall
School Complex
Assessment of
Existing neighborhood & two existing municipal buildings
Two retrofit scenarios

## Slide 101: HISTORICAL CENTER OF ANO LIOSSIA MUNICIPALITY OF FYLIS
Neighborhood: 0.271 km2 1320 inhabitants
Area: 360 buildings; 55% residential, 23% mixed use, 22% non-residential
Challenges: - Limited economic resources
Under-privileged, Safety issues, Low income area
Most buildings are old / inefficient
Limited infrastructure networks
Major motorway crossing
Air pollution problems
Inefficient public lighting
Few green areas

## Slide 102: VISION - SCENARIO
Improve the municipality's energy & carbon footprint
Acquire electrical energy & water self-sufficiency
Upgrade historical center; Improve citizens’ life
Reduce unemployment rate and energy poverty of households
Stakeholders: Municipality of Fylis;
Attika Prefecture;
Technical Departments;
Residents

## Slide 103: MAIN OUTCOMES
Data Resources
Audit
Different Departments of the Municipality (e.g. Technical)
Various Studies, Public Lighting plan, Public Transport plan, Maps, Blueprints, Energy & water bills
Weather station, Air pollution station
Statistical Data (Hellenic Statistical Authority)
Hellenic Energy Performance
Certificates (EPC) electronic repository
Dialogue with citizens
Consult with Local Committee Experts

## Slide 104: SNTool PASSPORT

## Slide 105: THANK YOU for your attention
andrea.moro@iisbeitalia.org