## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: C.1.2 - GHG EMISSIONS DURING OPERATION
C.1.2 – GHG EMISSIONS DURING OPERATION | 
ISSUE | CATEGORY
C. Environmental Loadings | C.1 Greenhouse Gas Emissions

## Slide 3: C.1.2 - GHG EMISSIONS DURING OPERATION
Greenhouse gases (GHGs) constitute a group of gases contributing to global warming & climate change. The Kyoto Protocol, an environmental agreement adopted many of the parties to the United Nations Framework Convention on Climate Change (UNFCCC) in 1997 to curb global warming, covers six GHGs: CO2, CH4, N2O, F-gases (HFCs & PFCs) and SF6
Converting them to CO2 equivalents makes it possible to compare them and to determine their individual & total contributions to environmental loadings
BACKGROUND

## Slide 4: C.1.2 - GHG EMISSIONS DURING OPERATION
The Global Warming Potential (GWP) was developed to allow for the comparison of the impact on global warming caused by different gases.
BACKGROUND
Source IPCC
X
For calculating CO2 equivalence, emissions of those gases are valued in terms of CO2 equivalent emissions; By definition,
GWP for CO2 = 1
GWP for methane CH4 = 25 (GWP over 100 years is 25 times that of CO2)
GWP for nitrous oxide N2O = 298 (GWP over 100 years is 298 times that of CO2)
GWP is a relative measure of how much energy can be trapped in the atmosphere over a set time horizon by a mass of gas in comparison with the same mass of carbon dioxide (CO2). A higher GWP means a larger warming effect in that period of time (e.g. 20, 100 years).

## Slide 5: C.1.2 - GHG EMISSIONS DURING OPERATION
BACKGROUND
Thermal energy is delivered to the building in the form of heat/cool from district systems & fuel. It is the energy per 'carrier' supplied to the building, to satisfy uses within the building (e.g. heating, cooling, ventilation, domestic hot water).
The ‘delivered energy’ is metered by the utilities
Fuel combustion in a building (e.g. burning gas for space heating) results to emissions.
District heating/cooling plants may also burn fuels to generate heating/cooling that is transmitted and delivered to buildings.
GHG
GHG
Direct Emissions

## Slide 6: C.1.2 - GHG EMISSIONS DURING OPERATION
BACKGROUND
Source IPCC
The ‘delivered energy’ is metered by the utilities
Electricity from the grid is delivered to the building to satisfy uses within the building (e.g. heating, cooling, ventilation, domestic hot water, lighting, auxiliaries)
Several power plants still burn fossil fuels to generate electricity that is transmitted by the grid and delivered to buildings
GHG
Direct Emissions
Fossil Fuels
42%
The future is green electricity

## Slide 7: C.1.2 - GHG EMISSIONS DURING OPERATION
BACKGROUND
Source IPCC
The ‘delivered energy’ is metered by the utilities
Indirect Emissions
Additional environmental impacts also originate from the extraction and mining of fossil fuels, transport, processing (e.g. refining)
For example, indirect emissions from the upstream production of oil account for about 20% of the total GHG emissions
Source: ARC Financial Corp. “Crude Oil Investing in a Carbon Constrained World”, February 2016.
Ref: Jackie Forrest, www.arcenergyinstitute.com

## Slide 8: C.1.2 - GHG EMISSIONS DURING OPERATION
BACKGROUND
Source IPCC
The GHG intensity for fuels and other forms of energy (e.g. electricity) is expressed in terms of mass of carbon dioxide equivalent per unit of energy of fuel (kgCO2eq/kWh)
Source: IPCC

## Slide 9: C.1.2 - GHG EMISSIONS DURING OPERATION
Description | Unit | Project stage | Data source
CO2 equivalent emissions per internal useful floor area per year | kg CO2 eq./m2/y | Design ____________ Occupancy | Estimation ____________ Estimation
INDICATOR

## Slide 10: C.1.2 - GHG EMISSIONS DURING OPERATION
INTENT
Minimise the total greenhouse gas emissions from buildings’ operations.
-22%
-1265 mil ton CO2 eq.
-20% -40%

## Slide 11: C.1.2 - GHG EMISSIONS DURING OPERATION
BOUNDARY & SCOPE
The assessment boundary is the building.
The scope of the indicator comprises the use stage of the building and includes the emissions related to the following energy end-uses, which are also referred to as technical building services:
heating,
cooling,
ventilation,
domestic hot water,
lighting,
auxiliaries

## Slide 12: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD
Calculations of the contribution of a building to global warming along its life cycle are standardised by ISO 14067. The Life Cycle Assessment (LCA) standard ISO 14040 also provides a main general reference. This is also referred to as a carbon footprint assessment or whole life carbon measurement.

## Slide 13: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – Emission Factors
Emission factors are coefficients which quantify the emissions per unit of energy use.
CO2 emissions are calculated for each energy carrier by multiplying final energy consumption by the corresponding emission.
The emissions reporting unit is kg CO2 equivalent that includes CO2 emissions and other GHGs (such as CH4 and N2O).

## Slide 14: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – Standard Emission Factors (IPCC)
Standard emission factors following IPCC principles, cover all the CO2 emissions that occur due to energy consumption by buildings within the territory of the local authority.
Direct fuel combustion in buildings (e.g. space heating)
Indirect via fuel combustion associated with the generation of electricity or district heat/cold use within the area
The standard emission factors are based on the carbon content of each fuel
Source: Covenant of Mayors - technical annex to the SEAP template
Can use official national/local emission factors, if appropriate

## Slide 15: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – LCA Emission Factors
LCA emission factors take into consideration GHG emissions of CO2 and other gases (CH4 and N2O) and the overall life cycle of the energy carrier, i.e. include emissions that take place outside of the location where the fuel is used
Emissions of the final combustion
Upstream emissions of the supply chain
Can use official national/local emission factors, if appropriate
Source: Covenant of Mayors - technical annex to the SEAP template

## Slide 16: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – Electricity Emission Factors
Emission factors for electricity generation depend on the energy mix for power generation
Electricity that is consumed in a particular municipality generally comes from different plants either inside or outside the municipality
The physical flows of electricity cross the borders and vary depending on the use of renewables, energy market situation, imports/exports etc
Use a national emission factor that reflects the average CO2 eq. emissions related to the national electricity production
Source: www.electricitymap.org

## Slide 17: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – Electricity Emission Factors
Source: Covenant of Mayors - technical annex to the SEAP template
Emission factors for electricity generation depend on the energy mix
National emission factors fluctuate from year to year due to the energy mix that is used in electricity generation
Use a national emission factor that reflects the average CO2 eq. emissions related to the national electricity production
Green electricity

## Slide 18: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – Heat/Cold Emission Factors
Source: Covenant of Mayors - technical annex to the SEAP template
Emission factors for district heat or cold that is sold/distributed as a commodity to end users within the local authority is calculated as follows
If part of the district heat/cold that is produced in the local authority is exported, then the corresponding share of CO2 emissions is deducted in the calculation
If the district heat/cold is imported from a plant situated outside the local authority, then the share of CO2 emissions of this plant that corresponds to the consumption in the territory of the local authority is accounted for in the calculation
Example for heat; similar for cold

## Slide 19: C.1.2 - GHG EMISSIONS DURING OPERATION
The calculation steps for new (design) buildings are the following:
Calculate the internal floor area of the building, [m2]
Calculate the annual quantity of each fuel (e.g. liters of oil, cubic meters of natural gas) delivered to the building for its technical services or used by CHP, if applicable, over a typical year, according to CEN standards that support EPBD. See also B.1.2
The fuels may be used for combustion (e.g. use oil or natural gas for space heating) or CHP to generate useful heat (and electricity, see next)
Use the LCA CO2 eq. emission factors for each fuel to convert energy units to CO2 eq. mass, [kg CO2 eq.]
Calculate the total GHG intensity for all fuels, [kg CO2 eq./m2/yr]
ASSESSMENT METHOD – DESIGN STAGE (Fuels)
Fuels
Efuels =

## Slide 20: C.1.2 - GHG EMISSIONS DURING OPERATION
Calculate the annual electricity delivered to the building to cover the demand for its technical services over a typical year. For more information see indicator B.1.3
Use the LCA CO2 eq. emission factors for electricity to convert energy units to CO2 eq. mass, [kg CO2 eq.]
Calculate the GHG intensity from electricity, [kg CO2 eq./m2/yr]
ASSESSMENT METHOD – DESIGN STAGE (Electricity)
Electricity

## Slide 21: C.1.2 - GHG EMISSIONS DURING OPERATION
Calculate the annual total energy delivered to the building from a district heating/cooling network to cover the demand for its technical services over a typical year, according to CEN standards that support EPBD
Use the LCA CO2 eq. emission factors for district heat or cold to convert energy units to CO2 eq. mass, [kg CO2 eq.]
Calculate the GHG intensity from district heat or cold, [kg CO2 eq./m2/yr]
ASSESSMENT METHOD – DESIGN STAGE (Heat/Cold)
Heat/Cold

## Slide 22: C.1.2 - GHG EMISSIONS DURING OPERATION
Sum all the calculated intensities to calculate the total GHG intensity, [kg CO2 eq./m2/yr]
ASSESSMENT METHOD – DESIGN STAGE (Total)
Total
+
+
=

## Slide 23: C.1.2 - GHG EMISSIONS DURING OPERATION
The calculation steps for existing buildings are the following:
Calculate the buildings’ internal useful floor area (use floor plans or measure), [m2]
Calculate the annual quantity of each fuel (e.g. liters of oil, cubic meters of natural gas) delivered to the building for its technical services, using a 3year average value, from monitoring, bills or utilities. See also B.1.2
Convert the quantity of fuels to thermal energy using their lower heating values, [kWh]
Use the LCA CO2 eq. emission factors for each fuel to convert energy units to CO2 eq. mass, [kg CO2 eq.]
Calculate the total GHG intensity from all fuels, [kg CO2 eq./m2/yr]
ASSESSMENT METHOD – OCCUPANCY STAGE (Fuels)
Efuels =
Fuels

## Slide 24: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – OCCUPANCY STAGE (Electricity)
Calculate the annual electricity delivered to the building to cover the demand for its technical services, using a 3year average value, from monitoring (e.g. BEMS) that provides the necessary data for the specific end-uses. See also B.1.3
Can also use data from electricity bills or utilities; Use a 3year average value; Desegregate data for different end-uses with survey results. See also B.1.3
Use the LCA CO2 eq. emission factors for electricity to convert energy units to CO2 eq. mass, [kg CO2 eq.]
Calculate the GHG intensity from electricity, [kg CO2 eq./m2/yr]
Electricity

## Slide 25: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – OCCUPANCY STAGE (Heat/Cold)
Calculate the annual total energy delivered to the building from a district heating/cooling network to cover the demand for its technical services, using a 3year average value, from bills or utilities, or use the values from indicator B.1.2
Use the LCA CO2 eq. emission factors for district heat/cold to convert energy units to CO2 eq. mass, [kg CO2 eq.]
Calculate the GHG intensity from district heat/cold, [kg CO2 eq./m2/yr]
Heat/Cold

## Slide 26: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – OCCUPANCY STAGE (Total)
Sum all the calculated intensities to calculate the total GHG intensity, [kg CO2 eq./m2/yr]
Total
+
+
=

## Slide 27: C.1.2 - GHG EMISSIONS DURING OPERATION
ASSESSMENT METHOD – OCCUPANCY STAGE
where
Qfuel,i = total quantity of annual fuel consumption of i-th fuel (e.g. m3 for gas or lt for oil)
LHVi = lower heating value of the i-th fuel (e.g. kWhth/m3 or kWhth/lt)
kem,i = LCA CO2 eq. emission factor of the i-th fuel (kg CO2 eq./kWhth)
Qel = total quantity of annual electrical energy from the grid (kWhe)
kem = LCA CO2 eq. emission factor of the electrical energy from the grid (kg CO2 eq./kWhe)
Qdhc = total quantity of annual energy from district heating/cooling (kWhth)
kem,dhc = LCA CO2 eq. emission factor of energy from district heating/cooling (kg CO2eq./kWhth)
Au = useful internal floor area (m2)
Heat/Cold

## Slide 28: C.1.2 - GHG EMISSIONS DURING OPERATION
REFERENCES and STANDARDS
EN 15603 - Energy performance of buildings - Overall energy use and definition of energy ratings
ISO 14067:2013 - Greenhouse gases -- Carbon footprint of products -- Requirements and guidelines for quantification and communication. Geneva: International Organization for Standardization.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en
Directive (EU) 2015/652 laying down calculation methods and reporting requirements pursuant to Directive 98/70/EC of the European Parliament and of the Council relating to the quality of petrol and diesel fuels.
IPCC: 2014. Fifth Assessment Report of the Intergovernmental Panel on Climate Change. Geneva, Switzerland.
JRC: 2013. How to develop a sustainable energy action plan (SEAP) in the Southern Mediterranean Partner Countries, JRC88817. Joint Research Centre, European Commission.

## Slide 29: C.1.2 - GHG EMISSIONS DURING OPERATION
EXAMPLE - DESIGN STAGE

## Slide 30: C.1.2 - GHG EMISSIONS DURING OPERATION
A new office building is designed in Greece with a central HVAC system that is served by high efficiency heat pumps. Electricity is the only energy carrier used in the building.
Available data: The useful internal floor area is 2,995.8 m2. The calculated annual electrical energy use intensity (EUI) for its technical services (i.e. heating, cooling, ventilation, domestic hot water, lighting, auxiliaries) is 85.2 kWhe/m2 useful floor area per year.
Calculate the total LCA GHG intensity, by investigating the option of connecting to two different energy suppliers
    Main national power grid
    Nearby PV field with sufficient capacity to cover the building’s loads

## Slide 31: C.1.2 - GHG EMISSIONS DURING OPERATION
The building’s annual electricity demand for its technical services (i.e. HVAC, domestic hot water, lighting, auxiliaries) is
85.2 kWhe/m2  2995.8 m2 = 255,242.2 kWhe
LCA emission factors for the two options:
1. Connected to main grid: 1.167 kgCO2 eq./kWhe
2. Connected to new Solar PV: 0.02 kgCO2 eq./kWhe
Source: Covenant of Mayors - technical annex to the SEAP template
Use the lower value for a new facility
Step 1
The building’s useful internal floor area is 2,995.8 m2.
Steps 2 - 4
Step 5
The building doesn’t use fuel for its technical services
Step 6

## Slide 32: C.1.2 - GHG EMISSIONS DURING OPERATION
GHG intensity (Electricity)
1. E= = 99.4 kgCO2 eq./m2/y
2. E= = 1.7 kgCO2 eq./m2/y
Since the EUI for electricity was available, one can directly use this data for the calculations
1. E= 85.2  1.167 = 99.4 kgCO2 eq./m2/y
2. E= 85.2  0.02 = 1.7 kgCO2 eq./m2/y
Step 7

## Slide 33: C.1.2 - GHG EMISSIONS DURING OPERATION
Steps 8 - 10
Step 11
The building doesn’t use district heating/cooling network for its technical services
Calculate the total LCA GHG intensity (kg CO2 eq./m2/yr)
1. E= 99.4 kgCO2 eq./m2/y
2. E= 1.7 kgCO2 eq./m2/y

## Slide 34: C.1.2 - GHG EMISSIONS DURING OPERATION
EXAMPLE - OCCUPANCY STAGE

## Slide 35: C.1.2 - GHG EMISSIONS DURING OPERATION
An existing office building located in Athens uses two different energy carriers. The building is connected to the main power grid and has a central heating system using an oil-fired boiler, with exhaust mechanical ventilation. Each office space is equipped with a local split unit heat pump for cooling. Domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Available data: The building manager provided the floor plans and annual energy consumption over several years. The oil quantities correspond to the total fuel orders that were delivered to the building each year. The electricity use data was also extracted from electricity bills that corresponds to the total building electrical energy demand for all end-uses of the building during the corresponding year.
Calculate the total LCA GHG intensity, i.e. CO2 equivalent emissions.
Identify the main source for the annual emissions

## Slide 36: C.1.2 - GHG EMISSIONS DURING OPERATION
 | 2015 | 2016 | 2017
Oil (lt) | 50,500 | 43,900 | 48,100
Electricity (kWhe) | 451,155 | 399,321 | 420,233
Annual quantity of fuels and electricity delivered to the building
Typical floor plan
Floor plans have been verified during a short energy audit of the building and can be used to estimate the building’s useful floor area
Available data

## Slide 37: C.1.2 - GHG EMISSIONS DURING OPERATION
Calculate the building’s useful floor area
Use the available floor plans that have been reviewed and confirmed to comply with the existing building during a short energy audit.
Use internal dimensions. Exclude from the measurement exercise the floor areas not in scope (see Levels)
Useful internal floor area: 4,915.1 m2
Typical floor
Step 1

## Slide 38: C.1.2 - GHG EMISSIONS DURING OPERATION
Calculate the quantity of the various energy carriers for the technical building services
FUELS
OIL
Used for space heating
Assume that the quantity of oil delivered to the building is actually used during the calendar year for its technical services (space heating)
Calculate the three year average: lt
Average annual quantity of fuel: 47,500 lt oil
Step 2

## Slide 39: C.1.2 - GHG EMISSIONS DURING OPERATION
Lower heating value of heating oil LHVoil = 9.9 kWhth/lt (see B1.2)
LCA emission factors for heating oil
LCA GHG intensity from fuels (kg CO2 eq./m2/yr)
kem,oil = 0.305 kg CO2 eq./kWhth
Source: Covenant of Mayors - technical annex to the SEAP template
Step 3
Step 4
Quantity of Fuel: 47,500 lt
9.9 kWh/lt
470,250 kWhth
Calculate the energy content of the fuel (oil)
=
Step 5

## Slide 40: C.1.2 - GHG EMISSIONS DURING OPERATION
ELECTRIRCITY
Calculate the three year average: kWhe
Average annual total electricity from the main grid: 423,570 kWhe
Calculate the electricity used the technical building services in scope using calibrated simulations or use typical breakdown (see B.1.3)
Step 6

## Slide 41: C.1.2 - GHG EMISSIONS DURING OPERATION
Breakdown of electricity demand from energy audit
Technical building services in scope:
Cooling (21.9% ) + Exhaust ventilation, fans (13.2%) + Domestic hot water(2.7%) + Lighting (36.5%) + Auxiliaries, pumps etc (3.8% ) = 78.1% of total electricity
Space heating demand is covered by the fuel of the oil-fired central heating system
Average annual electricity for technical building services from the main grid: 423,570 kWhe  78.1% = 330,808 kWhe

## Slide 42: C.1.2 - GHG EMISSIONS DURING OPERATION
Calculate LCA GHG intensity from electricity (kg CO2 eq./m2/yr)
kem,i = 1.167 kg CO2 eq./kWhe
Source: Covenant of Mayors - technical annex to the SEAP template
Step 7
LCA emission factors for electricity from grid
Step 8
=

## Slide 43: C.1.2 - GHG EMISSIONS DURING OPERATION
Step 12
Step 11
The building doesn’t use district heating/cooling network for its technical services
Step 9
Calculate the total LCA GHG intensity
Contributions to annual emissions
Fuel: 27%
Electricity: 73% Main source of annual emissions (depends on national LCA emission factor)

## Slide 44
EXERCISE

## Slide 45: C.1.2 - GHG EMISSIONS DURING OPERATION
A naturally ventilated office building located in Athens is served by a gas-fired central heating system and is connected to the main power grid. Local heat pumps are used for cooling and domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Available data: The building manager provided the floor plans, monthly fuel and electrical energy consumption from energy bills and monitoring over several years. The electricity data corresponds to the total building electrical energy demand for all its end-uses.
Use the following data to solve the exercise
Calculate the total LCA GHG intensity, i.e. CO2 equivalent emissions.
Identify the main source for the annual emissions

## Slide 46: C.1.2 - GHG EMISSIONS DURING OPERATION
Floor Plans
Useful internal floor area = 416 m2
Available data

## Slide 47: C.1.2 - GHG EMISSIONS DURING OPERATION
Natural Gas Consumption (m3)
 | Month | 2015 | 2016 | 2017
 | January | 686.9 | 809.5 | 959.9
 | February | 713.0 | 868.5 | 1019.0
 | March | 545.1 | 750.0 | 868.5
 | April | 211.1 | 300.6 | 217.7
 | May | 0.0 | 0.0 | 0.0
 | June | 0.0 | 0.0 | 0.0
 | July | 0.0 | 0.0 | 0.0
 | August | 0.0 | 0.0 | 0.0
 | September | 0.0 | 0.0 | 0.0
 | October | 41.1 | 463.4 | 86.4
 | November | 311.4 | 551.8 | 201.9
 | December | 718.2 | 930.7 | 566.1
Available data

## Slide 48: C.1.2 - GHG EMISSIONS DURING OPERATION
 | Month | 2015 | 2016 | 2017
 | January | 3041.1 | 1992.6 | 2811.4
 | February | 2696.0 | 1861.8 | 2494.3
 | March | 2884.7 | 1869.7 | 2582.8
 | April | 2633.4 | 2014.5 | 2317.1
 | May | 2502.5 | 2407.7 | 2475.9
 | June | 3703.5 | 2146.4 | 2438.4
 | July | 4258.1 | 2448.4 | 3164.8
 | August | 4388.8 | 2487.7 | 3299.3
 | September | 2980.2 | 2419.6 | 3138.6
 | October | 2409.9 | 1898.4 | 1916.7
 | November | 2239.1 | 1530.1 | 1960.7
 | December | 2543.1 | 1676.9 | 1749.5
Electricity Consumption (kWhe)
Available data