## Slide 1
Training Module 2
Decision-Making
Process

## Slide 2
Decision-Making phases
2
D4.1.1 Adaptation of CESBA MED generic decision-making methodology to South and East side of MED

## Slide 3
Initiation phase
3
The initiation phase is the first step in the decision-making process to define the optimal retrofitting concept for urban and building scale projects.
The objective is to select the urban area and the buildings for which the retrofitting concept will be defined, collect key information, identify the stakeholders to involve and set the working group (SMC WG) responsible for the decision-making process

## Slide 4
Initiation phase
4

## Slide 5
Initiation phase
In this stage, the municipality must carry out the necessary steps to start the decision-making process. First, the municipality must select the urban area and the building(s) for which the retrofitting concept will be defined.
1.1 Selection of the urban area and the buildings
The physical boundaries of the urban area must be clearly defined, using one or more of the following criteria:
• Geographical proximity
• Property ownership / occupier
• Social and Economic context
• Legal /administrative boundary lines
• Period of construction
• Energy supply infrastructure

## Slide 6
Initiation phase
6
The decision-making methodology is applicable to both small urban areas and neighbourhoods. After setting the physical boundaries of the urban area, the public buildings included in the retrofitting study shall be identified.
1.1 Selection of the urban area and the buildings
The municipality shall provide the rationale behind the selection of the urban area and buildings that will be the objects of the decision-making process.

## Slide 7
Initiation phase
7
The “SMC Team” is the group of experts appointed by the municipality that will manage the whole decision-making process.
A coordinator of the WG shall be appointed.
He/she will be the main responsible for the deployment of the activities and will act as interface with the municipality.
1.2 SMC Team

## Slide 8
Initiation phase
8
The SMC Team shall collect the necessary data to describe the urban area and the building(s), providing the necessary information to start the decision-making process. The climatic profile shall also be described in detailed.
1.3 Collection of data
The information to be collected in the Initiation phase are fully described in D5.2.1 Test Protocol.

## Slide 9
Initiation phase
9
After having set the physical boundaries of the urban area, the municipality shall identify the relevant stakeholders that can contribute to the study.
The identification of the stakeholders can help to refine the sustainability goals and consider multiple approaches to reach them, as the municipality would be able to utilize the stakeholder’s specialized knowledge during the study.
Also, the early engagement of the stakeholders in the project would be helpful to reduce the risk of conflicts in the development of the retrofitting concept.
1.4 Stakeholders identification

## Slide 10
Preparation phase
10
The preparation phase is the beginning of the urban and building retrofitting concepts development.
The preparation phase will provide the necessary information to create a sufficient working basis for the next phases.

## Slide 11
Preparation phase
11
The first step of the preparation phase consists in the contextualization of the SBTool and SNTool generic frameworks (transnational version) to the local conditions and priorities.
The contextualization process consists of (see D3.1.1):
the selection of the assessment criteria
the definition of the criteria’s weights
the definition of the benchmarks for each selected assessment criterion.
2.1 SNTool and SBTool contextualization

## Slide 12
Preparation phase
The selection of criteria determines the environmental, social and economic issues and subjects that will be taken into consideration during the retrofitting concept development. Each assessment criterion in SBTool and SNTool has a specific intent and addresses a specific sustainability subject.
The exclusion of an assessment criterion in the local version of SBTool and SNTool means that it isn’t considered relevant in relation to the local context and priorities.
The value of the weights assigned to the selected criteria reflects the priorities of the municipality in the sustainable retrofitting of the urban area and public buildings.
It is recommended to carry out the selection of criteria and the weight assignment through a participatory approach, as foreseen by the PGS approach.
2.1 SNTool and SBTool contextualization

## Slide 13
Preparation phase
The assessment method associated to each indicator in SNTool and SBTool requires specific information and data. It is necessary to identify, preliminary to the assessment activities, the sources of this information.
The identification of the sources of data can determine the exclusion of a criterion from the local versions of SBTool and SNTool.
For instance, a criterion selected in the previous stage could be later excluded because during the identification of the source of information it has been verified that the data aren’t available or are of poor quality. A valid retrofitting concept can only be defined if it is studied on solid data.
2.2 Data sources identification

## Slide 14
Preparation phase
14
The SMC WG shall define all needed data at building and urban level for the assessment activities. Potential data providers, data sources and most promising strategies must be identified to gather all the needed data.
2.2 Data sources identification
The use of software tools (GIS, energy simulation, cloud-based applications) may accelerate the collection and processing of the data collection process significantly.

## Slide 15
Preparation phase
Data providers may be:
- municipal or regional departments (e.g., urban planning, energy, mobility, green areas, buildings, etc.)
- public agencies (e.g., energy agencies, social housing agencies)
- statistical offices
- building owners / tenants
- certificates (e.g., energy performance, sustainability)
- utilities (e.g. local operators, energy utilities, water utilities)
- publicly accessible free source (e.g. Google Earth, Open Street Map)
- on-site inspection
- databases (e.g., from R&D projects)
2.2 Data sources identification

## Slide 16
16
The PGS approach takes place at this crucial moment: it is recommended to carry out the selection of criteria and the weight assignment through a participatory approach, involving the key stakeholders previously identified.
The selection will determine which sustainability issues will be considered in the preparation of the retrofitting scenarios.
The selection of criteria will be done through:
A Co-Creation Lab
The Collaborative Online Platform
Preparation phase
2.3 Participatory methods in the preparation phase

## Slide 17
2.3 Participatory methods in the preparation phase
A. Co-Creation Lab
Co-creation is the practice of collaborating with different stakeholders to guide the decision-making process while promoting a bottom-up approach. During a facilitated in presence workshop, participants with different roles align and offer diverse insights. Therefore decision-makers can obtain a more interconnected perspective of what a retrofit scenario should include.

## Slide 18
2.3 Participatory methods in the preparation phase
A. Co-Creation Lab
How to facilitate a Co-Creation Lab?
1. Identify the objectives to be achieved.
2. Select the most appropriate activities to achieve the objectives: Brainstorming, prioritization, role playing discussions, prototyping, mapping, among others. Consider also starting with an ice breaker for the participants to get to know each other.
3.Create the participant list, with names, titles and organization based on the role of each stakeholder relevant for the project.
4. Identify a location to carry out the co-creation lab.

## Slide 19
5. Prepare the documents necessary for the participants to be contextualised during the lab.
6. Structure the Session-by-Session plan, with topic, purpose, desired outcomes, time allotment, identification of facilitator or presenter, and participants, necessary materials to develop the selected activities.
7. Send the respective call to participate to the co-creation lab with the location, time, and date details as well as the necessary documents for participants to have all the information.
2.3 Participatory methods in the preparation phase
A. Co-Creation Lab
How to facilitate a Co-Creation Lab?

## Slide 20
Link: https://adhocracy.plus/sustainable_med_cities
B. Collaborative Platform
2.3 Participatory methods in the preparation phase

## Slide 21
Diagnosis phase
21
The diagnosis phase consists in the evaluation of the current condition of the urban area and buildings using a contextualised versions of SNTool/SBTool. It can allow to:
• identify strengths and weaknesses as well as assets that can be leveraged to support interventions
• identify interconnections, benefits, synergies between city systems that can help guide efficient resources use
• explore gaps in awareness and opportunities for action.
The objective of the diagnosis is:
- to set the basis for the definition of the performance targets for the retrofitting project (next phase)
- to identify strengths and weaknesses of the urban area and public buildings in terms of sustainability.

## Slide 22
Diagnosis phase
22

## Slide 23
Diagnosis phase
The key-weaknesses analysis is based on the SNTool assessment’s results, possibly complemented with a soft analysis based on occupant surveys and workshops.
Each criterion has been compared to the benchmark values which allow the municipality in a quick an efficient way to check which urban indicators perform weak and which ones are performing well.
If a criterion shows a result above a certain performance threshold defined by the municipality, the criterion is not relevant for the weaknesses analysis.
SMC Team can rank the criteria according to their reached performance. Using the results of the benchmarking and ranking process, a periodization of the different key-weak points of the urban area is possible.
3.1 Assessing the current state of the urban area

## Slide 24
Diagnosis phase
24
The table represents a simplified output of an urban scale evaluation using SNTool
3.1 Assessing the current state of the urban area
The score associated to each criterion represent the actual level of performance of the urban area, using a scoring scale ranging from:
-1(negative) up to +5(excellent), where 0 represent the minimum acceptable performance

## Slide 25
Diagnosis phase
Ranking criteria.
3.2 Identification of the weaknesses in the urban area
The main sustainability issues (score -1) results to be the availability of green areas (A2.2) and the air pollution (E1.2). The performance concerning the access to waste and recycling collection points (D2.2), and the total final energy consumptions (B2.1) is the minimum acceptable (scores 0,4 and 0,5). The best performance is reached by the public transport system (F1.1)

## Slide 26
Diagnosis phase
26
3.2 Identification of the weaknesses in the urban area
To complement the SNTool evaluation, it is recommended to carry out a survey among the inhabitants of the urban area. The survey can be useful to identify the priorities of inhabitants and issues non quantifiable through the SNTool indicators. Occupant wishes concerning the design or amenities of the neighbourhood infrastructure (e.g. new shopping opportunity or playground in the neighbourhood, more parking space or brighter street lighting, etc.).
To analyse feedback, it is recommended to carry out a workshop by the municipality as part of the PGS approach.
Based on the results of the two-part key weaknesses identification (SNTool + survey) a summary shall be created showing the SNTool assessment results and concurrently the identified non-simulated weaknesses by the municipality.

## Slide 27
Diagnosis phase
3.3 Evaluation of the infrastructures’ current state
in the urban area
The analysis of the current state of the energy and water infrastructures is useful to understand the key weakness and to collect useful information for the next phases of the decision-making process.
The evaluation of the current state of the water infrastructure shall include aspects as:
sufficiency of the water provision in relation to the water demand
drinking water quality
availability and level of water treatment
water losses due to deterioration of the water network.

## Slide 28
Diagnosis phase
28
3.3.1 Evaluation of the energy infrastructures
SMC-WG shall evaluate the current energy infrastructure and renewable energy potential and identify the key weakness in the existing energy infrastructure and systems (heating/cooling networks like pipes, storage systems or heat suppliers).
If in the urban area such components are available, it is necessary to identify and rank the key weakness of these components regarding the energy and cost efficiency.
This step can be skipped in case such systems are not available.
It is also necessary to consider for existing heat networks the energy losses which may appear in operation from pipes and heat exchangers and evaluate them.

## Slide 29
Diagnosis phase
29
3.3.1 Evaluation of the energy infrastructures
Methods that can be used to evaluate the current state of the energy infrastructure:
A. Heating and cooling networks
• Heat demand density map
• Connected heat density
• Heat load profile
• (Heat) duration curve
• Heat grid structure
• Auxiliary power
• Hours of operation
• Fraction of renewable energy in the heating system
• System efficiency

## Slide 30
Diagnosis phase
30
3.3.1 Evaluation of the energy infrastructures
Methods that can be used to evaluate the current state of the energy infrastructure:
B. Electrical demand
• District load profile
• District electricity balance line
C. Inclusion of renewable energy potential
• Solar thermal
• PV Potential
• Wind potential
• Shallow Geothermal
After the current state evaluation, it is possible to start identifying the weak points of the energy infrastructure and systems, prioritizing in the whole perspective.

## Slide 31
Diagnosis phase
31
3.4 Evaluation of the building’s current state
Analogous to the process on urban level, the diagnosis phase on building level also contains a two-part key-weaknesses analysis based on SBTool as well as on occupant
survey. Key-weaknesses of the building can be identified and ranked according to the indicators’ results.
There are on building level again several potential non-simulated weaknesses which cannot be measured or quantified by any indicator (wish of occupants for a different arrangement of the furniture or a more intuitive control of the sun protection in the building).
Key-weaknesses for the non-simulated aspects can be analysed based on the collected feedback from occupant’s surveys and physical workshops in the preparation phase.

## Slide 32
Diagnosis phase
3.5 Diagnosis summary report and SWOT analysis
At the end of the diagnosis phase, the SMC-WG develops a report that summarizes the main findings of the diagnosis phase. The report shall contain the following:
main findings of the diagnosis, including weaknesses at urban and building scale
The report shall contain a SWOT analysis for the urban area, identifying the strengths, weaknesses, available opportunities and possible threats.
recommendations on how to handle the weaknesses in the next phases of the decision-making process.

## Slide 33
33
Diagnosis phase

## Slide 34
34
It is recommended to carry out a survey among the inhabitants of the urban area or building.
To analyse feedback of the different occupants on these non-assessed key-weaknesses using the corresponding tool, it is recommended to carry out a workshop by the municipality as part of the PGS approach.
The communication to the citizens of diagnosis results might be done during a PGS workshop organised in person or using electronic means.
Diagnosis phase
3.6 Diagnosis summary report and SWOT analysis

## Slide 35
Strategic definition phase
35
The main goal of this phase is the definition of the main framework conditions for the later retrofitting design based on the results of the diagnosis phase. The strategic definition therefore serves as pointer for the later design phases by setting meaningful targets for the retrofitting project and by identifying the main constraints and restrictions which may limit the retrofitting design.
This phase allows to:
Build a shared vision to support decision making
Drive improvement in performance by setting a baseline from which to assess change.

## Slide 36
Strategic definition phase

## Slide 37
Strategic definition phase
37
4.1 Sustainability targets
Define clear and measurable targets that should be achieved by the retrofitting concept. Targets must address all fields of sustainability like environment, economy and social aspects.
Targets need to be S.M.A.R.T. which means:
- Specific – target must be clearly defined
- Measurable – targets must be quantifiable
- Attainable – target must be realistic and achievable
- Relevant – are the targets relevant for sustainable urban districts and buildings
- Time-bound – specify when the result(s) can be achieved

## Slide 38
Strategic definition phase
38
4.1 Sustainability targets
SBTool and SNTool are used to set measurable sustainability targets at urban and building scale. For each assessment criteria it must be set a target score. Each target score will correspond to a target value of the indicator.

## Slide 39
Strategic definition phase
39
4.1 Sustainability targets

## Slide 40
Strategic definition phase
40
4.2 Constraints and restrictions
The main constraints that occur in district and building sustainability retrofitting projects can be defined and structured into the following categories:
Legal constraints (e.g. Building Codes, Cultural Heritage Protection)
Technical constraints (e.g. Architecture, Systems)
Financial constraints (e.g.Investment Cost, ROI)
Environmental constraints (e.g. Climatic conditions, urban morphology)
Stakeholder based restrictions
In this stage, the SMC WG must identify the existing constraints and their nature to proceed with the next steps in the decision-making process.

## Slide 41
41
On the results of the diagnosis phase, set meaningful targets for the retrofitting project and identify the main constraints/restrictions which may limit the retrofitting design.
Stakeholders take centre-stage since it is here that the framework conditions for the retrofit design and plans are defined based on the results of the diagnosis phase. This needs to be done in conjunction with stakeholders.
A PGS workshop must be organised to validate the sustainability targets for the urban area and for the public buildings
Strategic definition phase
4.3 Participatory methods in the strategic definition phase

## Slide 42
Retrofit scenario phase
42
Once established a vision for the future of the urban area and identified the sustainability targets that will drive efforts to achieve this vision, it can begin the development of a plan to make this vision a reality.
In this phase, the SMC WG develops alternative possible retrofitting scenarios for the urban area and the buildings that fulfil the defined sustainability targets in the Strategic Definition phase.
The team might come up with number of different scenarios, all of which fulfil the sustainability targets. Therefore, all valid scenarios would then be assessed in the next phase to choose the optimal one.

## Slide 43
Retrofit scenario phase
43

## Slide 44
Retrofit scenario phase
44
A scenario can be defined as a package of retrofitting interventions.
Interventions may comprise changes to a physical asset, such as a new development, technological solution, or other built structure. They can also comprise a soft intervention, such as a process or policy that builds knowledge or empowers skills and leadership. Interventions should promote a holistic, interconnected approach to urban functions and consider the urban area as a system, and they should aim to bridge silos through an inclusive process that acknowledges co-dependencies and interdependencies.
This integrated approach can help new ideas emerge and bring together new opportunities for cross-sectoral innovation. It can maximize synergies, foster efficient use of resources, and build longevity by ensuring that stakeholders and co-owners are engaged and invested in the successful implementation of the effort.
5.1 Development of retrofitting scenarios

## Slide 45
Retrofit scenario phase
45
To achieve performance targets, it is possible to develop alternative scenarios.
In this phase the SMC Working Group, in cooperation with stakeholders, will develop alternative retrofitting scenarios for both the urban area and the buildings. It is important that the scenarios differentiate significantly among each other.
Each scenario is a package of different solutions to improve the sustainability of the urban area as a whole, considering all buildings as connected global system.
A retrofitting scenario is composed of a variety of single interventions in different thematic fields. The main fields among others are energy, water, use of land, resources consumption, climate mitigation and adaptation, mobility, health, socio-cultural conditions.
5.1 Development of retrofitting scenarios

## Slide 46
Retrofit scenario phase
46
The approach proposed is to consider the energy as the priority field.
Urban regeneration interventions in the field of energy retrofitting are influencing the other thematic fields.
5.1 Development of retrofitting scenarios
The energy interventions are the starting point in the preparation of a scenario.
All non-energetic interventions will be then added.

## Slide 47
Retrofit scenario phase
47
To create a retrofitting scenario, the SMC TEAM shall proceed according to the following steps:
A. Selection and optimization of energy interventions at urban level
B. Selection and optimization of energy interventions at building level
C. Selection of non-energy related interventions (water, mobility, use of land,
services, etc.)
D. Identification of business models and financing schemes
E. Validation of the scenario
5.1 Development of retrofitting scenarios

## Slide 48
Retrofit scenario phase
48
The starting point in creating a scenario are the weakness identified in the Diagnosis Phase. The interventions are studied by the SMC Team to improve the sustainability of the urban area and buildings with the objective to achieve the sustainability performance targets established in the Strategic Definition phase.
The process is based on an iterative approach which allows to repeat the evaluation and re-select the package of measures as long as the SMC Team is satisfied with the achieved improvement results. Each iteration step will provide intermediate results by performing calculations and assessments using SBTool and SNTool. The multi-scale approach allows to verify the impact of the urban scale interventions on the buildings and vice-versa.
5.1.1 How to prepare a retrofitting scenario: selection of interventions

## Slide 49
Retrofit scenario phase
49
Automatic optimisation method cannot be used as the existing solutions available, like genetic optimisation algorithms, only allow the optimisation of a limited number of solutions and cannot take fully in account their impact at urban level and in relation to the local context.
As the identification of a package of interventions is a complex task, the SMC Team can follow a structured sequential approach based on three different mechanisms:
- Interventions filtering based on set constraints and restrictions
- Interventions compilation based on diagnosis results (weaknesses)
- Interventions sequence logic of application
5.1.1 How to prepare a retrofitting scenario: selection of interventions

## Slide 50
Retrofit scenario phase
50
After the preparation of a scenario by the SMC Team, the results achieved finally need to be compared with the targets set in the Strategic Definition.
Only if all targets have been reached, then the study about the financing of the scenario can start. If the targets have not been reached the scenario needs to be refined again by further iteration steps as long as needed till all targets have been reached.
For valid scenarios, which have reached all targets, the financing must be determined by considering appropriate business models and financing schemes. This step is needed in order to ensure the financing of the scenario as well as to identify all available useful financing instruments like grants, loans or contracting solutions.
5.1.1 How to prepare a retrofitting scenario: selection of interventions

## Slide 51
Retrofit scenario phase
51
The first step in the optimisation of the intervention package to be conducted by the SMC Team is to ensure that all interventions which may not be suitable to be applied for the building or urban area are identified and excluded.
Interventions cannot be suitable due to the defined constraints or restrictions for a concept which has been set for buildings and the urban area. For example, if cultural heritage protection laws restrict the installation of solar panels on roofs, the SMC Team needs to filter out all interventions which cannot be applied.
To do this at the beginning is important, since the number of possible interventions can be limited to only practicable ones that really can be implemented.
5.1.1.1 Interventions filtering based on set constraints and restrictions

## Slide 52
Retrofit scenario phase
52
The second process to be conducted by the SMC Team in the intervention package optimisation is to capitalize the results the diagnosis phase.
The diagnosis phase provides a result summary in form of a comprehensive list of identified weak points. Based on the identified weak points, the SMC Team can assess the potential for improvements and therefore select most useful retrofitting interventions.
Therefore, the diagnosis’ results guide the SMC Team in the selection of the most effective retrofitting solutions.
5.1.1.2 Interventions compilation based on diagnosis results

## Slide 53
Retrofit scenario phase
53
After the identification of a useful set of interventions it is important to know in which chronological sequence the interventions should be applied. The goal of this optimisation step is to achieve the most efficient retrofitting design.
The three optimisation steps are based on several iterations in which the different useful interventions are applied and the impacts are assessed by the SMC Team. Hence, the SMC Team needs to define for each iteration which interventions will be applied in which iteration step. Therefore, the methodology needs to pretend a chronological sequence how planners must apply the different selected retrofitting interventions to create most effective retrofitting scenarios.
Moreover, in each iteration some interventions may be replaced by other ones more effective. Nevertheless, the proposed sequence of applying the interventions must be seen as a guideline that has to be revised by the SMC Team for each variant.
5.1.1.3 Interventions sequence logic of application

## Slide 54
Retrofit scenario phase
54
Sequence of applying retrofitting interventions in the iteration steps
5.1.1.3 Interventions sequence logic of application

## Slide 55
Retrofit scenario phase
55
To ensure the right chronological sequence to create a complete energy retrofitting concept planners initially should apply interventions from categories in the following order:
Energy consumption reduction
Increasing the efficiency of the energy supply
Inclusion of renewable energy production
5.1.1.3 Interventions sequence logic of application

## Slide 56
Retrofit scenario phase
56
For each scenario, possible business models and financing mechanisms must be identified in order to evaluate which one could be the most suitable for a practical future implementation of the retrofitting interventions. Financing opportunities:
Grants
Loans
Loan Guarantees
Energy Performance Contracting
Co-investment
Embedded revenue contributions
Tax benefits
5.2 Financing mechanisms

## Slide 57
57
SMC WG develops possible alternative for retrofitting scenarios to be applied to the urban area and the buildings that fulfil the defined sustainability targets. Inputs and suggestions from inhabitants, occupants and stakeholders are a valuable contribution in the development of retrofitting interventions. Stakeholders can provide feedback considering their targets and expectations on the prioritization of interventions.
A PGS workshop shall be organised to exchange on the possible retrofitting strategies and scenarios.
Retrofit scenario phase
5.3 Participatory methods in the preparation of retrofit scenarios

## Slide 58
Decision-Making phase
58
The overall goal of this phase is to select the best scenario in terms of energy and cost efficiency as well as the overall sustainability among the ones created in the previous phase.
Only the scenarios which have reached the sustainability targets can be compared in the decision-making phase.
The selected best scenario will then be developed in a retrofitting concept in the next phase.
This phase is articulated in two steps:
- Assessment of scenarios
- Ranking of scenarios

## Slide 59
59
Decision-Making phase

## Slide 60
Decision-Making phase
60
Each scenario foresees a package of interventions to improve the sustainability of an urban area and one or more buildings belonging to it.
In this stage, the main goal is to identify the scenario that allows the urban area and the buildings to reach the higher level of sustainability.
6.1 Assessment of scenarios

## Slide 61
Decision-Making phase
61
The following steps must be accomplished for each scenario:
Urban area
identify the criteria in SNTool that are impacted by the retrofitting interventions
for those criteria, assuming the implementation of the interventions, the value of the indicators bas to be calculated and updated
the new SNTool overall score is updated.
- Building(s)
Identify the criteria in SBTool that are impacted by the retrofitting interventions
for those criteria, assuming the implementation of the interventions, the value of the indicators bas to be calculated and updated
the new SBTool overall score is updated.
6.1 Assessment of scenarios

## Slide 62
Decision-Making phase
62
At the end of the scenarios’ assessment process, the final output are the SBTool and the SNTool scores associated to each of them.
6.1 Assessment of scenarios
At this point, it is possible to proceed with their ranking

## Slide 63
Decision-Making phase
63
The ranking process is articulated in 3 steps:
1. Assignment of a weight to determine the priority levels among the urban area and the buildings
2. Assignment of a global sustainability score to a scenario
3. Ranking of scenarios according to their global sustainability scores
4. Selection of the optimal scenario to be transformed in a retrofitting concept
6.2 Ranking process

## Slide 64
Decision-Making phase
64
Assignment of a weight to determine the priority levels among the urban area and the buildings.
The first step is to assign a weight, expressed as a percentage, to the urban area and the buildings under evaluation. The weight reflects the relative importance among them.
Strong priority has given to the urban area (investments, n. of interventions, n. of people affected, etc.) with regards to the 2 buildings. One of the 2 buildings (A) has a priority (historical building, more deteriorated, bigger, et.) towards the second one (B).
6.2 Ranking process

## Slide 65
Decision-Making phase
65
2. Assignment of a global sustainability score to a scenario.
The overall score of each scenario is calculated as a weighted sum of the SNTool and SNTool scores. Assignment of a weight to determine the priority levels among the urban area and the buildings.
6.2 Ranking process

## Slide 66
Decision-Making phase
66
3. Ranking of scenarios according to their global sustainability scores.
Once that a global sustainability score has been assigned to all the scenarios, it is possible to proceed with their ranking.
6.2 Ranking process

## Slide 67
Decision-Making phase
67
4. Selection of the optimal scenario to be transformed in a retrofitting concept.
To confirm the optimal scenario, it is necessary to consider other 2 aspects: the potential financial mechanism to implement the scenario and the non-simulated aspects.
Financial mechanisms
The final chose should combine the best scenario in terms of performance and financial sustainability. For example, if a scenario may not have reached the first rank but has many advantages in terms of financial mechanisms that are not reflected by the global sustainability score, decision-makers need to bear these aspects in mind.
6.2 Ranking process

## Slide 68
Decision-Making phase
4. Selection of the optimal scenario to be transformed in a retrofitting concept.
Non-simulated aspects
As the ranking result is based on a quantitative method also non-simulated aspects need to be considered in the final decision-making.
For example, if a scenario may not have reached the first rank but has many advantages in terms of qualitative improvements that are not reflected by the global sustainability score, decision-makers need to bear these aspects in mind. Hence, an expert judgement needs to be done to assess the final ranking of the variants beside the global sustainability score. The scenario which has finally been identified as the best ranked one (quantitative and qualitative aspects) is transformed in a retrofitting concept in the next stage.
6.3 Ranking process

## Slide 69
69
Select the best scenario in terms of energy and cost efficiency as well as the overall sustainability among the ones created.
The selected best scenario will then be developed in a retrofitting concept, feedback from occupants and users should be considered before a final decision is made on the best scenario. The opinions of occupants and users should be heavily weighted.
Results should be encapsulated in a summary report, and this is then presented in a PGS meeting.
Decision-Making phase
6.3 Participatory methods in decision-making

## Slide 70
Retrofit concept phase

## Slide 71
Retrofit concept phase
71
The retrofitting concept is a report containing the description of the interventions foreseen by the scenario.
The interventions are illustrated for the urban area and the building(s) and organised following the issues of SBTool and SNTool.
The retrofitting concept shall be considered as the first step or an integrated urban planning and design process. It provides a solid basis to build a valid retrofitting project in future
SMC Team is required to detail the best scenario in a retrofitting concept.

## Slide 72
Retrofit concept phase
72
For each intervention, the information to provide is:
- Description
- Expected results
- Activities/works to implement the intervention
- Timescale
- Budget estimation
- Financial scheme
- Responsible for the implementation
- Partnerships
- Reference stakeholders
- Links with existing or future strategies, plans, programs

## Slide 73
73
SMC Team is required to detail the best scenario in a retrofitting concept.
The retrofitting concept is a report containing the description of the interventions foreseen by the scenario.
During the participatory consultation, the SMC Team will illustrate the interventions foreseen by the scenario.
Retrofit concept phase