## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2
B.1.1 - PRIMARY ENERGY CONSUMPTION | 
ISSUE | CATEGORY
B. Energy & Resource Consumption | B.1 Energy

## Slide 3
BACKGROUND
EU Primary Products
EU Imports
Source: Eurostat
The extraction of energy products from natural sources to a usable form. It occurs within the territory under consideration
Source: Eurostat
Imports cover the amount of energy produced outside and brought into the considered territory for consumption

## Slide 4
Description | Unit | Project stage | Data source
Primary energy consumption per internal useful floor area per year | kWh/m2/y | Design ____________ Occupancy | Estimation ____________ Metering
INDICATOR

## Slide 5
INTENT
Minimize the total primary energy consumption of the building.
NZEB (EPBD 2010/31/ΕΕ, 2018/844)
Nearly Zero Energy Buildings
All new buildings from 2021
Public new buildings from 2019
Clean Energy for All Europeans
New package of measures for providing the stable legislative framework needed to facilitate the clean energy transition towards the creation of the Energy Union
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 6
DESCRIPTION
The indicator provides an understanding of a building's primary energy consumption. Primary energy is defined by Article 2(5) of the Energy Performance of Buildings Directive (EPBD) [1] as 'the energy that has not undergone any conversion in the transformation process, calculated by energy carrier using a primary energy factor'. It is the energy that is required to generate the electricity, heating and cooling used by a building.
This is a calculation of the overall system efficiency of the building; envelope, technical systems (HVAC installation, heat and power generation, domestic hot water supply, built-in lighting and auxiliaries) and energy carriers used.

## Slide 7
The assessment boundary is the building. Energy can be imported or exported through the assessment boundary (the building) from/to on-site, nearby and distant locations.
Inside the assessment boundary, the system losses are taken into account explicitly in the conversion factor applied to the energy carrier, also referred to as a primary energy factor.
BOUNDARY & SCOPE

## Slide 8
The scope of the indicator includes the following energy uses, which are also referred to as technical building services:
heating,
cooling,
ventilation,
domestic hot water,
lighting,
auxiliaries
The energy use is referred to as operational energy consumption.
BOUNDARY & SCOPE

## Slide 9
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790
Possible to use metered or estimated data for the energy use, so that it is feasible to populate this indicator
The source of data must always be clearly declared

## Slide 10
ASSESSMENT METHOD
Can use most national calculation methods that are aligned with the EN standards and are being used for
Building performance assessment or
Issuing Energy Performance Certificates (EPCs)

## Slide 11
ASSESSMENT METHOD - Primary Energy Conversion Factors
Primary (source) energy consumed by a building as measured at the building, converted using primary energy conversion factors to account for the energy consumed in the extraction, processing, and transport of primary fuels (e.g. oil, natural gas); energy losses in thermal combustion in power-generation plants; and energy losses in transmission and distribution to the building
Can use official national/local emission factors, if appropriate

## Slide 12
The calculation steps for new (design) buildings are the following:
Calculate the annual thermal energy use intensity (EUIth) for all energy carriers (see B.1.2) over a typical year according to CEN standards that support EPBD, in kilowatt hours per square meter of useful internal floor area per year, [kWhth/m2/y]
Calculate the annual electrical energy use intensity (EUIe) (see B.1.3) over a typical year according to CEN standards that support EPBD, in kilowatt hours per square meter of useful internal floor area per year, [kWhe/m2/y]
ASSESSMENT METHOD – DESIGN STAGE

## Slide 13
Use national conversion factors to estimate the total primary energy use intensity (PEUI)
ASSESSMENT METHOD – DESIGN STAGE

## Slide 14
ASSESSMENT METHOD – DESIGN STAGE
where
EUIth,i = annual thermal energy use intensity of i-th fuel (kWhth/m2/y) for the gas and/or oil or other fuel delivered to the building for its technical services
Fi = national conversion factor of the i-th fuel
EUId = annual thermal energy use intensity (kWhth/m2/y) used by a district heating/cooling network to generate the heat/cold delivered to the building for its technical services
Fd = national conversion factor for the fuel used by a district heating/cooling network
EUIe = annual electrical energy use intensity (kWhe/m2/y) for the electricity delivered to the building for its technical services (kWhe/m2/y)
Fe = national conversion factor of electricity from the main grid (depends on energy mix of main grid)

## Slide 15
ASSESSMENT METHOD – DESIGN STAGE
National conversion factors
X
=
Fuels (B.1.2)
+
National conversion factor
X
Electricity (B.1.3)
Total primary energy use per building’s useful internal floor area per year
Sum the thermal and the electrical energy use intensity the to calculate the total primary energy use intensity

## Slide 16
The calculation steps for existing buildings are the following:
Calculate the annual thermal energy use intensity (EUIth) for all energy carriers (see B.1.2) by monitoring, energy metering, bills or utilities, using a 3year average, in kilowatt hours per square meter of useful internal floor area per year (kWhth/m2/y)
Calculate the annual electrical energy use intensity (EUIe) (see B.1.3) by monitoring, energy metering, bills or utilities, using a 3year average, in kilowatt hours per square meter of useful internal floor area per year (kWhe/m2/y)
ASSESSMENT METHOD – OCCUPANCY STAGE

## Slide 17
Use national conversion factors to estimate the total primary energy use intensity (PEUI)
ASSESSMENT METHOD – OCCUPANCY STAGE

## Slide 18
ASSESSMENT METHOD – OCCUPANCY STAGE
where
EUIth,i = annual thermal energy use intensity of i-th fuel (kWhth/m2/y) for the gas and/or oil or other fuel delivered to the building for its technical services
Fi = national conversion factor of the i-th fuel
EUId = annual thermal energy use intensity (kWhth/m2/y) used by a district heating/cooling network to generate the heat/cold delivered to the building for its technical services
Fd = national conversion factor for the fuel used by a district heating/cooling network
EUIe = annual electrical energy use intensity (kWhe/m2/y) for the electricity delivered to the building for its technical services (kWhe/m2/y)
Fe = national conversion factor of electricity from the main grid (depends on energy mix of main grid)

## Slide 19
ASSESSMENT METHOD – OCCUPANCY STAGE
National conversion factors
X
=
Fuels (B.1.2)
+
National conversion factor
X
Electricity (B.1.3)
Total primary energy use per building’s useful internal floor area per year
Sum the thermal and the electrical energy use intensity the to calculate the total primary energy use intensity

## Slide 20
EPBD:2018 - Energy Performance of Buildings Directive, 2018/844/EU. Brussels: European Parliament and the Council of the European Union.
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
ASHRAE Standard 100: 2018. Energy Efficiency in Existing Buildings. Atlanta: ASHRAE.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en
REFERENCES and STANDARDS

## Slide 21
REFERENCES and STANDARDS

## Slide 22
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 23
EXAMPLE - DESIGN STAGE

## Slide 24
A new office building is designed in Greece with a central HVAC system that is served by high efficiency heat pumps. Electricity is the only energy carrier used in the building.
Available data: The useful internal floor area is 2995.8 m2. The calculated annual electricity delivered to cover the demand of its technical services (i.e. heating, cooling, ventilation, domestic hot water, lighting, auxiliaries) is 255,242.2 kWhe
Calculate the primary energy consumption (for all delivered energy carriers) per building’s useful internal floor area per year.

## Slide 25
Calculate the annual electrical energy use intensity (kWhe/m2/y) for the technical building services
255,242.2 kWhe

=
Delivered Electricity for technical services
2995.8 m2
85.2 kWhe/m2/y
Useful internal
floor area (m2)
Calculate the annual thermal energy use intensity (kWhth/m2/y) for the technical building services
0 kWhth

=
Delivered Thermal energy for technical services
2995.8 m2
0 kWhth/m2/y
Useful internal
floor area (m2)
Step 1
Step 2

## Slide 26
Calculate the annual primary energy use intensity (kWh/m2/y) for the technical building services
(0 kWhth/m2/y ) + (85.2 kWhe/m2/y  2.1) = 178.9 kWh/m2
Step 3

## Slide 27
EXAMPLE - OCCUPANCY STAGE

## Slide 28
An existing office building located in Athens uses two different energy carriers. The building is connected to the main power grid and has a central heating system using an oil-fired boiler, with exhaust mechanical ventilation. Each office space is equipped with a local split unit heat pump for cooling. Domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Available data: The building manager provided the floor plans and annual energy consumption over several years. The oil quantities correspond to the total fuel orders that were delivered to the building each year. The electricity use data was also extracted from electricity bills that corresponds to the total building electrical energy demand for all end-uses of the building during the corresponding year.
Calculate the primary energy consumption (for all delivered energy carriers) per building’s useful internal floor area per year

## Slide 29
 | 2015 | 2016 | 2017
Oil (lt) | 50,500 | 43,900 | 48,100
Electricity (kWhe) | 451,155 | 399,321 | 420,233
Annual quantity of fuels and electricity delivered to the building
Typical floor plan
Floor plans have been verified during a short energy audit of the building and can be used to estimate the building’s useful floor area
Available data
29

## Slide 30
Thermal Energy (see B.1.2)
Step 1

## Slide 31
Electrical Energy (see B.1.3)
Step 2

## Slide 32
Calculate the annual primary energy use intensity (kWh/m2/y) for the technical building services
(95.7 kWhth/m2/y  1.1)
+
(67.3 kWhe/m2/y  2.1)
= 246.6 kWh/m2
Step 3

## Slide 33
EXERCISE

## Slide 34
A naturally ventilated office building located in Athens uses two different energy carriers. The building is connected to the main power grid and has a central heating system using a gas-fired boiler. Local heat pumps are used for cooling and domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Available data: The building manager provided the floor plans, monthly fuel and electrical energy consumption from energy bills and monitoring over several years. The electricity data corresponds to the total building electrical energy demand for all its end-uses.
Use the following data to solve the exercise
Calculate the primary energy consumption (for all delivered energy carriers) per building’s useful internal floor area per year

## Slide 35
Floor Plans
Useful internal floor area = 416 m2
Available data

## Slide 36
Natural Gas Consumption (m3)
 | Month | 2015 | 2016 | 2017
 | January | 686.9 | 809.5 | 959.9
 | February | 713.0 | 868.5 | 1019.0
 | March | 545.1 | 750.0 | 868.5
 | April | 211.1 | 300.6 | 217.7
 | May | 0.0 | 0.0 | 0.0
 | June | 0.0 | 0.0 | 0.0
 | July | 0.0 | 0.0 | 0.0
 | August | 0.0 | 0.0 | 0.0
 | September | 0.0 | 0.0 | 0.0
 | October | 41.1 | 463.4 | 86.4
 | November | 311.4 | 551.8 | 201.9
 | December | 718.2 | 930.7 | 566.1
Available data

## Slide 37
 | Month | 2015 | 2016 | 2017
 | January | 3041.1 | 1992.6 | 2811.4
 | February | 2696.0 | 1861.8 | 2494.3
 | March | 2884.7 | 1869.7 | 2582.8
 | April | 2633.4 | 2014.5 | 2317.1
 | May | 2502.5 | 2407.7 | 2475.9
 | June | 3703.5 | 2146.4 | 2438.4
 | July | 4258.1 | 2448.4 | 3164.8
 | August | 4388.8 | 2487.7 | 3299.3
 | September | 2980.2 | 2419.6 | 3138.6
 | October | 2409.9 | 1898.4 | 1916.7
 | November | 2239.1 | 1530.1 | 1960.7
 | December | 2543.1 | 1676.9 | 1749.5
Electricity Consumption (kWhe)
Available data