## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
B.1.3 – ELECTRICAL ENERGY CONSUMPTION | 
ISSUE | CATEGORY
B. Energy and Resource Consumption | B.1. Energy

## Slide 3: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
EU Services Sector
EU Residential Sector
Source: Eurostat
ELECTRICITY
48%
Source: Eurostat
ELECTRICITY
24%
BACKGROUND

## Slide 4: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
INDICATOR
Description | Unit | Project stage | Data source
Electrical energy consumption per internal useful floor area per year | kWh/m2/y | Design ____________ Occupancy | Estimation ____________ Metering

## Slide 5: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
INTENT
Minimize the total electrical energy consumption of the building.
NZEB (EPBD 2018/844)
Nearly Zero Energy Buildings
All new buildings from 2021
Public new buildings from 2019
Clean Energy for All Europeans
New package of measures for providing the stable legislative framework needed to facilitate the clean energy transition towards the creation of the Energy Union
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 6: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
DESCRIPTION
The indicator provides an understanding of a building's electricity consumption.
This is in general responsible for the majority of life cycle energy use for buildings constructed before 2000.
Electricity is delivered from the main grid to the building to satisfy uses within the building (heating, cooling, ventilation, domestic hot water, built-in lighting, auxiliaries). The ‘delivered energy’ is generally the one metered by the utilities.

## Slide 7: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
BOUNDARY & SCOPE
The assessment boundary is the building.
The scope of the indicator includes the following energy end-uses, which are also referred to as technical building services:
heating
cooling
ventilation
domestic hot water
lighting
auxiliaries
The energy use is re referred to as operational energy consumption.

## Slide 8: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
The actual annual electricity use of a building is also available from electricity bills or utilities. Average over longer periods (e.g. 3year records).
BOUNDARY & SCOPE
The main challenge is that the breakdown for the different building technical services and other end-uses (e.g. plug loads) is not evident.
Desegregation for different end-uses is facilitated by BEMS, if available for buildings in operation, or calibrated building simulations.
Technical services
(space heating, DHW, cooling, lighting, auxiliaries)
In scope
Plug loads, Cooking etc
(appliances, office equipment etc)
x
NOT
In scope

## Slide 9: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Source: JRC
Residential
The actual annual electricity use of a building is also available from electricity bills or utilities. Average over longer periods (e.g. 3year records).
BOUNDARY & SCOPE
Utility bills include the total electricity demand for the building’s technical services (in scope here) and plug loads, cooking etc (not in scope here).
Desegregate electricity demand for different end-uses with calibrated building simulations or use survey results from an energy audit.
Source: Eurostat
Commercial

## Slide 10: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
BOUNDARY & SCOPE
The actual electricity use of a building can be monitored. If available, BEMS or BMS can provide valuable data with a breakdown of the actual electricity use of the different technical installations.
Building energy management system (BEMS) control & monitor energy use of the various technical installations for heating, cooling, ventilation, lighting, plug loads etc, and indoor environmental conditions.
Building management system (BMS) may additionally include other functions (e.g. safety, access, lifts, fire security).
Actual energy use data from at least 12 consecutive months is necessary.
It is preferable to average over longer records (e.g. three year data) in order to remove the effects of varying weather conditions and average out other inherent fluctuations in the building occupancy.

## Slide 11: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790
Possible to use metered or estimated data for the energy use, so that it is feasible to populate this indicator
The source of data must always be clearly declared

## Slide 12: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD
Can use most national calculation methods that are aligned with the EN standards and are being used for
Building performance assessment or
Issuing Energy Performance Certificates (EPCs)

## Slide 13: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
The calculation steps for new (design) buildings are the following:
Calculate the annual electricity from the grid delivered to the building to cover the demand for its technical services over a typical year, according to CEN standards that support EPBD
Calculate the internal useful floor area within the building
Calculate the electrical energy use intensity in kilowatt hours per square meter of useful internal useful floor area per year (kWhe/m2/y)
ASSESSMENT METHOD – DESIGN STAGE

## Slide 14: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD – OCCUPANCY STAGE
The calculation steps for existing buildings are the following:
Calculate the annual electricity from the grid delivered to the building to cover the demand for its technical services by metering, using a 3year average value
Can also use data from electricity bills or utilities; desegregate data for different end-uses with survey results; Use a 3year average value
Calculate the internal useful floor area within the building (use floor plans or measure)
Calculate the electrical energy use intensity in kilowatt hours per square meter of useful internal useful floor area per year (kWhe/m2/y)

## Slide 15: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
EPBD:2018 - Energy Performance of Buildings Directive, 2018/844/EU. Brussels: European Parliament and the Council of the European Union.
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en
REFERENCES and STANDARDS

## Slide 16: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 17: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
EXAMPLE - DESIGN STAGE

## Slide 18: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
A new office building is designed in Greece with a central HVAC system that is served by high efficiency heat pumps. Electricity is the only energy carrier used in the building.
Available data: The useful internal floor area is 2,995.8 m2. The calculated annual electricity delivered to cover the demand of its technical services (i.e. heating, cooling, ventilation, domestic hot water, lighting, auxiliaries) is 255,242.2 kWhe
Calculate the electrical energy consumption (for the building’s technical services) per building’s useful internal floor area per year (i.e. final electrical energy use intensity).

## Slide 19: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Calculate the annual electrical energy use intensity (kWhe/m2/y)
255,242.2 kWhe

=
Delivered Electricity for technical services
2995.8 m2
85.2 kWhe/m2/y
Useful internal
floor area (m2)
Step 1
Step 2
Step 3
The annual electricity delivered to the building is 255,242.2 kWhe
The building’s useful internal floor area is 2,995.8 m2

## Slide 20: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
EXAMPLE - OCCUPANCY STAGE

## Slide 21: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
An existing office building located in Athens is connected to the main power grid and it is served by an oil-fired boiler for central space heating, exhaust mechanical ventilation and local split unit heat pumps for cooling. Domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Available data: The building manager provided the floor plans and annual electricity bills over several years. The electricity data corresponds to the total building demand for all end-uses of the building during the corresponding year.
Calculate the electrical energy consumption (for the building’s technical services) per building’s useful internal floor area per year (i.e. final electrical energy use intensity).

## Slide 22: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
 | 2015 | 2016 | 2017
Electricity (kWhe) | 451,155 | 399,321 | 420,233
Annual electricity delivered to the building (obtained from electricity bills)
Typical floor plan
Floor plans have been verified during a short energy audit of the building and can be used to estimate the building’s useful floor area
Available data

## Slide 23: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Calculate the average annual electricity for the technical building services
Calculate the three year average: kWhe
Average annual total electricity from the main grid: 423,570 kWhe
Calculate the electricity used the technical building services in scope using calibrated simulations or use typical breakdown
Step 1

## Slide 24: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Calculate the average annual electricity for the technical building services
Breakdown of electricity demand from energy audit
Technical building services in scope:
Cooling (21.9% ) + Exhaust ventilation, fans (13.2%) + Domestic hot water(2.7%) + Lighting (36.5%) + Auxiliaries, pumps etc (3.8% ) = 78.1% of total electricity
Space heating demand is covered by the fuel of the oil-fired central heating system
Average annual electricity for technical building services from the main grid: 423,570 kWhe  78.1% = 330,808 kWhe

## Slide 25: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Calculate the building’s useful floor area
Use the available floor plans that have been reviewed and confirmed to comply with the existing building during a short energy audit.
Use internal dimensions. Exclude from the measurement exercise the floor areas not in scope (see Levels)
Useful internal floor area: 4,915.1 m2
Typical floor
Step 2

## Slide 26: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Calculate the annual electrical energy use intensity (kWhe/m2/y) for the technical building services
330,808 kWhe

=
Delivered Electricity for technical services
4,915.1 m2
67.3 kWhe/m2/y
Useful internal
floor area (m2)
Step 3

## Slide 27: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
EXERCISE

## Slide 28: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
A building located in Athens is centrally air-conditioned with energy efficient HVAC installations.
Available data: The building manager provided the floor plans and annual energy consumption over several years. The data was extracted from electricity bills that corresponds to the total building electrical energy demand for all its end-uses during the corresponding year.
Use the following data to solve the exercise
Calculate the electrical energy consumption (for the building’s technical services) per building’s useful internal floor area per year (i.e. final electrical energy use intensity).

## Slide 29: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
Floor Plans
Useful internal floor area = 416 m2
Available data

## Slide 30: B.1.3 – ELECTRICAL ENERGY CONSUMPTION
 | Month | 2015 | 2016 | 2017
 | January | 6082.3 | 3985.2 | 5622.7
 | February | 5392.1 | 3723.6 | 4988.5
 | March | 5769.3 | 3739.4 | 5165.6
 | April | 5266.8 | 4028.9 | 4634.2
 | May | 5004.9 | 4815.5 | 4951.8
 | June | 6985.0 | 5366.0 | 5015.9
 | July | 7976.3 | 6121.1 | 5999.4
 | August | 8111.5 | 6219.3 | 6023.2
 | September | 6622.7 | 5376.9 | 6974.8
 | October | 5355.3 | 4218.6 | 4259.4
 | November | 4975.9 | 3400.3 | 4357.2
 | December | 5651.4 | 3726.4 | 4373.7
Electricity Consumption (kWhe)
Available data