## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION | 
ISSUE | CATEGORY
B. Energy & Resource Consumption | B.1 Energy
RED: Renewable Energy Directive 2018/2001
New package of 8 different legislative proposals for
«Clean Energy for All Europeans package»
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 3: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
BACKGROUND (All RES for all uses)
EU Services Sector
EU Residential Sector
Source: Eurostat
RES
16%
Source: Eurostat
RES
3%

## Slide 4: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
BACKGROUND
Source: Eurostat
Renewables
30%

## Slide 5: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Description | Unit | Project stage | Data source
Share of renewable energy in final electrical energy consumption | % | Design ____________ Occupancy | Estimation ____________ Metering
INDICATOR

## Slide 6: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
INTENT
Maximize the use of renewable energy sources.
Photovoltaics
(BIPV-Building Integrated Photovoltaics)
Wind turbines

## Slide 7: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
DESCRIPTION
This indicator assesses the share of renewable energy in final electrical energy consumptions and thus, the degree to which renewable fuels have substituted fossil fuels and therefore contributed to the decarburization of the Mediterranean space economy.
It also quantifies the progress towards the Europe 2020 & 2030 targets for renewable energies.

## Slide 8: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
BOUNDARY & SCOPE
The assessment boundary is the building.
The scope of the indicator includes the following energy uses, which are also referred to as technical building services:
heating,
cooling,
ventilation,
domestic hot water,
lighting,
auxiliaries
In a life cycle approach, their energy use is referred to as operational energy consumption

## Slide 9: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
BOUNDARY & SCOPE
According to the Renewables Energy Directive (RED 2018), energy from renewable sources means energy from renewable non-fossil sources, namely wind, solar, aerothermal, geothermal, hydrothermal and ocean energy, hydropower, biomass, landfill gas, sewage treatment plant gas and biogases. Heat pumps enabling the use of aerothermal, geothermal or hydrothermal heat at a useful temperature level need electricity or other auxiliary energy to function. The energy used to drive heat pumps should therefore be deducted from the total usable heat. Only heat pumps for which SPF > 1,15 * 1/η shall be taken into account.

## Slide 10: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of the Energy Performance of Buildings Directive (EPBD) across the EU
The CEN standards series that currently forms the basis for most national calculation methods includes EN 15603 that collates the results from EN 13790
In case of existing buildings, the share of renewable energy in total final electric energy consumption should be evaluated by energy metering
Simulations may provide accurate data
Possible to use metered or estimated data for the energy use, so that it is feasible to populate this indicator
The source of data must always be clearly declared

## Slide 11: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD
The actual electricity produced & used on-site from renewable sources (e.g. solar using PV, wind using turbines) is usually monitored (measured) by dedicated power or smart meters.
Actual energy use data from at least 12 consecutive months is necessary.
It is preferable to average over longer records (e.g. three year data) in order to remove the effects of varying weather conditions and average out other inherent fluctuations in the building occupancy.
From Main Grid
From PV

## Slide 12: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD
The actual electricity use from the main power grid can also be monitored. If available, BEMS or BMS can provide valuable data with a breakdown of the actual electricity use of the different technical installations.
Building energy management system (BEMS) control & monitor energy use of the various technical installations and indoor environmental conditions.
Building management system (BMS) may additionally include other functions (e.g. safety, access, lifts, fire security).
The actual annual electricity use of a building is also available from electricity bills or utilities. Average over longer periods (e.g. 3year records).
Utility bills include the total electricity demand for the building’s technical services (in scope here) and plug loads, cooking etc (not in scope here).
Desegregate electricity demand for different end-uses with calibrated building simulations or use survey results from an energy audit.
See also B.1.3

## Slide 13: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD
Performance of RES depends on type of system, efficiency, location (e.g. solar availability ) etc
For example, electricity production from PVs
Annual average output
Greece: 1100 to 1500 kWh/kWp/year
Thessaloniki: 1150 to 1250 kWhe/kWp/year
Athens: 1300 to 1400 kWhe/kWp/year
Crete: 1350 to 1500 kWhe/kWp/year

## Slide 14: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
The calculation steps new (design) buildings are the following:
Calculate the electricity produced & used on-site from renewable sources (e.g. solar using PV, wind using turbines) to cover the demand for its technical services over a typical year, according to CEN standards that support EPBD, [kWh]
ASSESSMENT METHOD – DESIGN STAGE

## Slide 15: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Calculate the annual electricity delivered to the building from the main power grid, [kWh]
Sum the electrical energy from RES and the electricity delivered to the building from the main power grid, to calculate the total final electrical energy (RES & conventional)[kWh]
ASSESSMENT METHOD – DESIGN STAGE
See also B.1.3 for design stage

## Slide 16: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Total Electrical Energy (kWhe,T)
Electricity from RES (kWhe,RES)
ASSESSMENT METHOD – DESIGN STAGE
=
______
Calculate the percentage ratio of the amount of electricity produced from renewable sources to the total final electrical energy (RES & conventional), [%]

## Slide 17: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD – OCCUPANCY STAGE
The calculation steps for existing buildings are the following:
Calculate the electricity produced & used on-site from renewable sources (e.g. solar using PV, wind using turbines) to cover the demand for its technical services, using a 3year average, from monitored data or calculations, [kWh]

## Slide 18: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
ASSESSMENT METHOD – OCCUPANCY STAGE
Measure the annual electricity delivered to the building from the main power grid, [kWh]
Sum the electrical energy from RES and the electricity delivered to the building from the main power grid, to calculate the total final electrical energy (RES & conventional)[kWh]
See also B.1.3 for design stage

## Slide 19: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Total Electrical Energy (kWhe,T)
Electricity from RES (kWhe,RES)
ASSESSMENT METHOD – OCCUPANCY STAGE
=
______
Calculate the percentage ratio of the amount of electricity produced from renewable sources to the total final electrical energy (RES & conventional), [%]

## Slide 20: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
REFERENCES and STANDARDS
RED 2018. Directive (EU) 2018/2001 of the European Parliament and of the Council of 11 December 2018 on the promotion of the use of energy from renewable sources (recast). Brussels: European Commission. http://data.europa.eu/eli/dir/2018/2001/oj
2013/114/EU: Commission Decision of 1 March 2013
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en

## Slide 21: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 22: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
EXAMPLE - DESIGN STAGE

## Slide 23: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
A new office building is designed in Greece with a central HVAC system that is served by high efficiency heat pumps. Electricity is the only energy carrier used in the building. In addition, building integrated photovoltaics (30 kWp) are used to deliver electricity for the building’s technical services.
Available data: The useful internal floor area is 2,995.8 m2. The calculated annual electricity from the main grid delivered to cover the demand of its technical services (i.e. heating, cooling, ventilation, domestic hot water, lighting, auxiliaries) is 215,071.8 kWhe,Grid. Simulations for the specific type of PVs, location, orientation etc, have provided an estimate of the annual electricity production from renewables of 40,170.4 kWhe,RES
Calculate the percentage ratio of the amount of electricity produced from renewable sources to the total final electrical energy use from the main grid.

## Slide 24: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
The calculated annual electricity delivered to the building is 215,071.8 kWhe,Grid
Step 1
The calculated annual electricity production from renewables is 40,170.4 kWhe,RES
Step 2
Step 3
Calculate the total electrical energy (RES & conventional)
40,170.4 kWhe,RES + 215,071.8 kWhe,Grid = 255,242.2 kWhe,t

## Slide 25: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Step 4
Calculate the percentage ratio
15.7 % RES Electrical
255,242.2
Total Electrical Energy (kWhe,TOTAL)
40,170.4
Electricity from RES (kWhe,RES)
=
______
x
100

## Slide 26: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
EXAMPLE - OCCUPANCY STAGE

## Slide 27: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
An existing office building located in Athens is connected to the main power grid and it is served by an oil-fired boiler for central space heating, exhaust mechanical ventilation and local split unit heat pumps for cooling. Domestic hot water is served with local electric continuous-flow (tankless) water heaters. In addition, building integrated photovoltaics (70 kWp) are used to deliver electricity for the building’s technical services.
Available data: The building manager provided the annual electricity bills that corresponds to the total electricity purchased from the main grid to cover the demand for all end-uses of the building, and the electricity produced from the PVs for the corresponding year.
Calculate the percentage ratio of the amount of electricity produced from renewable sources to the total final electrical energy use from the main grid.

## Slide 28: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
 | 2015 | 2016 | 2017
Electricity from main grid (kWhe,Grid) | 372,651 | 305,095 | 326,502
Electricity from RES (kWhe,RES) | 78,504 | 94,226 | 93,731
Annual electricity delivered to the building (obtained from electricity bills (kWhe,Grid) that is purchased from the main grid and the annual electricity produced from the PVs (kWhe,RES)
Available data

## Slide 29: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Calculate the average annual electricity from the PVs for the technical building services
Calculate the three year average: kWhe,RES
Average annual total electricity from the PVs: 88,820 kWhe,RES
Step 1

## Slide 30: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Calculate the average annual electricity from the grid for the technical building services
Calculate the three year average
kWhe,Grid
Average annual total electricity from the main grid: 334,749 kWhe,Grid
Calculate the electricity used by the technical building services in scope using calibrated simulations or use typical breakdown
Step 2
See B.1.3

## Slide 31: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
Calculate the average annual electricity from the grid for the technical building services
Breakdown of electricity demand from energy audit
Technical building services in scope:
Cooling (21.9% ) + Exhaust ventilation, fans (13.2%) + Domestic hot water(2.7%) + Lighting (36.5%) + Auxiliaries, pumps etc (3.8% ) = 78.1% of total electricity
Space heating demand is covered by the fuel of the oil-fired central heating system
Average annual electricity for technical building services from the main grid: 334,749 kWhe,Grid  78.1% = 261,439 kWhe, Grid
See B.1.3

## Slide 32: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
350,259
Total Electrical Energy (kWhe,TOTAL)
88,820
Electricity from RES (kWhe,RES)
=
______
25%
% RES Electrical
Step 4
Calculate the percentage ratio
Step 3
Calculate the total electrical energy (RES & conventional)
88,820 kWhe,RES + 261,439 kWhe,Grid = 350,259 kWhe,t
x
100

## Slide 33: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
EXERCISE

## Slide 34: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
A new hospital building is designed that is served by a central HVAC system. It will be connected to the power grid.
The design team considers the installation of:
Building integrated photovoltaics to deliver electricity for the building’s technical services.
Available data: For the initial design, the calculated monthly final electrical energy used by the technical building services in scope over a typical year. For the alternative design, the calculated annual electrical energy produced from the photovoltaics is 304,500kWhe,RES
Use the following data to solve the exercise
Calculate the percentage ratio of the amount of electricity produced from renewable sources to the total final electrical energy use from the main grid.

## Slide 35: B.1.5 - ENERGY FROM RENEWABLE SOURCES IN TOTAL ELECTRICAL ENERGY CONSUMPTION
 | Month | Typical year
 | January | 166051
 | February | 136356
 | March | 155240
 | April | 148506
 | May | 159599
 | June | 190353
 | July | 236246
 | August | 224114
 | September | 195751
 | October | 156604
 | November | 147153
 | December | 152552
Electricity consumption (kWhe,Grid)
Total = 304,500kWhe,RES
Available data
Electrical energy produced from PV