## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
B.1.6 – Embodied Non-Renewable Primary Energy | 
ISSUE | CATEGORY
B. Energy & Resource Consumption | B.1 Energy

## Slide 3
INDICATOR
Description | Unit | Project stage | Data source
Embodied primary non-renewable energy per internal useful floor area | MJ/m2 | Design ____________ Occupation | Estimation ____________ Not applicable
B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
The indicator is only applicable at design stage.
In case of new construction, the indicator must be calculated taking in account all the materials used for the building construction.
In case of an existing building, the indicator must be calculated taking in account only the materials used for its renovation and not the ones pre-existent.

## Slide 4: B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
INTENT
Promote the use of construction materials with a low embodied energy.

## Slide 5
DESCRIPTION
This indicator measures the embodied non-renewable primary energy of materials used for the building construction. The embodied energy is the energy consumed by all the processes associated with the production of construction materials, from the raw materials supply to manufacturing (cradle-to-gate) energy used for the acquisition of raw materials, processing, manufacturing and assembling building construction materials at the factory gate.
Cradle to Gate: energy used for the acquisition of raw materials, processing, manufacturing and assembling building construction materials at the factory gate.
B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY

## Slide 6: B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
BOUNDARY & SCOPE
The assessment boundary is the building
The scope comprises the product stage of the building i.e. from raw material supply to manufacturing. The scope encompasses the building materials excluding the technical installations. All the elements of the construction are taken in account: foundations, bearing structure, envelope, slabs.

## Slide 7: B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
BOUNDARY & SCOPE
The minimum scope of the indicator includes the following building parts and elements:

## Slide 8
ASSESSMENT METHOD
To calculate the value of the indicator, it is necessary to compile a Bill of Materials (BoM) that is a mass-based inventory of the different materials (kg) that compose a building. The BoM is organized according to main elements composing a building
The starting point is the Bill of Quantities (BoQ) specifying the elements of a building (e.g. foundations, columns). The BoQ includes different categories of elements, which can have different functional performance characteristics. BoM differs from a BoQ in that it describes the different materials (e.g. concrete, steel, aluminium) that are contained in the various building elements. Once the BoM has been compiled, it is possible to calculate the value of the indicator.
B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
A BoQ includes the building elements accounting for at least 99% of the mass of the building.

## Slide 9
ASSESSMENT METHOD
The calculation steps are the following:
  Identify the basic composition of each building element. A breakdown of its constituent materials has to be carried out. The mass of each constituent material has to be estimated
  Aggregate by material. The mass for each constituent material should thereafter be aggregated to obtain the total mass for each type of material, [kg].
  Calculate the embodied primary energy of each material by multiplying the specific mass (i.e. kg) with its corresponding embodied energy coefficient, [MJ/kg].
  Sum the embodied energy of all materials to calculate the total embodied energy of the building, [MJ]
  Calculate the total useful internal floor area, [m2]
  Calculate the indicator’s value as: total embodied energy of the building (step 4) / total useful internal floor area (step 5), [MJ/ m2].
B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
MJ/m2

## Slide 10: B.1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
REFERENCES and STANDARDS
ISO 14040/44, EN 15804 (Sustainability of construction works. Environmental product declarations. Core rules for the product category of construction products)
EN 15978 “Sustainability of construction works - Assessment of environmental performance of buildings - Calculation method”

## Slide 11: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
EXAMPLE

## Slide 12: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
MATERIAL TYPE (Major components) | APPROXIMATE WEIGHT (kg) From BoQ | EMBODIED ENERGY INTENSITY (MJ/kg) From BoM | EMBODIED ENERGY (MJ)
Floors - concrete |  |  | 
17.5 Mpa concrete in floor slab with lightweight cladding | 53,184 | 1.0 | 53,184
Concrete masonry foundation | 1,312 | 0.94 | 1,233
Reinforcing steel for slab on ground and foundation | 789 | 8.9 | 7,022
Vinyl flooring | 2,049 | 8.0 | 16,392
Steps 1 -3
Calculate the embodied primary non-renewable energy per internal useful floor area of a single family house of 195 m2

## Slide 13: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
MATERIAL TYPE (Major components) | APPROXIMATE WEIGHT (kg) From BoQ | EMBODIED ENERGY INTENSITY (MJ/kg) From BoM | EMBODIED ENERGY (MJ)
Windows and glazing |  |  | 
Aluminium window joinery – factory coated | 288 | 34.3 | 9,878
Float glass | 450 | 15.9 | 7,155
Wall cladding |  |  | 
Brick veneer | 13,780 | 6.7 | 92,326
Fibre-cement sheet | 2,940 | 9.4 | 27,636
Steps 1 -3

## Slide 14: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
Calculate the total embodied energy of the building
+ 16,392 + 9,878 + 7,155 + 92,326 + 27,636) = 214, 826 MJ
Step 4
Step 5
Step 6
Internal useful floor area: 195 m2
197, 847 MJ

=
Total embodied energy
195 m2
1,101.7 MJ/m2
internal useful
floor area
Calculate the total embodied primary non-renewable energy per internal useful floor area

## Slide 15: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
EXERCISE

## Slide 16: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
MATERIAL TYPE (Major components) | APPROXIMATE WEIGHT (kg) From BoQ | EMBODIED ENERGY INTENSITY (MJ/kg) From BoM | EMBODIED ENERGY (MJ)
Floors - concrete |  |  | 
17.5 Mpa concrete in floor slab with lightweight cladding | 53,184 | 1.0 | 
Concrete masonry foundation | 1,312 | 0.94 | 
Reinforcing steel for slab on ground and foundation | 789 | 8.9 | 
Vinyl flooring | 2,103 | 8.0 | 
Steps 1 -3
Calculate the embodied primary non-renewable energy per internal useful floor area of a building with 200 m2 internal floor area

## Slide 17: B1.6 – EMBODIED NON-RENEWABLE PRIMARY ENERGY
MATERIAL TYPE (Major components) | APPROXIMATE WEIGHT (kg) From BoQ | EMBODIED ENERGY INTENSITY (MJ/kg) From BoM | EMBODIED ENERGY (MJ)
Windows and glazing |  |  | 
Aluminium window joinery – factory coated | 296 | 34.3 | 
Float glass | 462 | 15.9 | 
Wall cladding |  |  | 
Brick veneer | 14,133 | 6.7 | 
Fibre-cement sheet | 3,015 | 9.4 | 
Steps 1 -3