## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: B.3.4 – RECYCLED MATERIALS
B.3.4 – RECYCLED MATERIALS | 
ISSUE | CATEGORY
B. Energy & Resource Consumption | B.3 Materials

## Slide 3
INDICATOR
Description | Unit | Project stage | Data source
Weight of recycled materials on total weight of materials. | % | Design ____________ Occupation | Estimation ____________ Not-Applicable
B.3.4 – RECYCLED MATERIALS
The indicator is only applicable at design stage.
In case of new construction, the indicator must be calculated taking in account all the materials used for the building construction.
In case of renovation of an existing building, the indicator must be calculated taking in account only the materials used for its renovation and not the ones pre-existent.

## Slide 4: B.3.4 – RECYCLED MATERIALS
INTENT
Reduce the environmental impact of construction materials.

## Slide 5
DESCRIPTION
This indicator assesses the amount of recycled materials used in the building with regards to the total amount of building materials. The use of recycled materials allows to reduce the use and depletion of new materials.
B.3.4 – RECYCLED MATERIALS

## Slide 6: B.3.4 – RECYCLED MATERIALS
BOUNDARY & SCOPE
The assessment boundary is the building.
The scope encompasses the building materials excluding the technical installations. All the elements of the construction are taken in account: foundations, load bearing structure, envelope, slabs.
It is possible to take in account both the post-consumer and pre-consumer recycled content of a material. The pre-consumer content is included in the calculation only if it isn’t reused in the same industrial process.

## Slide 7: B.3.4 – RECYCLED MATERIALS
BOUNDARY & SCOPE
The following building parts and elements are included in the calculations:

## Slide 8
ASSESSMENT METHOD
To calculate the value of the indicator it is necessary to compile a Bill of Materials (BoM) that is a mass-based inventory of the different materials (kg) that compose a building. The BoM is organised according to main elements that a building is composed of.
The starting point is the Bill of Quantities (BoQ) that specifies the elements of a building (e.g. foundations, columns). The BoQ comprises different categories of elements, which can have different functional performance characteristics. A BoM differs from a BoQ in that it describes the different materials (e.g. wood, steel, aluminium) that are contained in the various building elements. Once the BoM has been compiled, it is possible to calculate the value of the indicator.
B.3.4 – RECYCLED MATERIALS

## Slide 9
ASSESSMENT METHOD
The calculation steps are the following: :
  Identify the basic composition of each building element. A breakdown of its constituent materials has to elaborated. The mass of each constituent material has to be estimated
  Aggregation by material: the mass of all constituent material should thereafter be aggregated to obtain the total mass of materials used in the building
  Identify the recycled content of each constituent material (in mass)
  Aggregation by material: the recycled mass of all constituent materials should thereafter be aggregated to obtain the total recycled mass of materials used in the building
  The indicator’s value is calculated as the percentage ratio of total recycled mass of materials (step 4) to the total mass of materials (step 2), [%]
B.3.4 – RECYCLED MATERIALS

## Slide 10
B.3.4 – RECYCLED MATERIALS
REFERENCES and STANDARDS
EN ISO 14021 (Environmental labels and declarations - Self-declared environmental claims - Type II environmental labelling).

## Slide 11: B.3.4 – RECYCLED MATERIALS
EXAMPLE

## Slide 12: B.3.4 – RECYCLED MATERIALS
From the Bill of Quantities and Bill of Materials, it resulted that a 1½ storey house of 195 m2 weighs approximately 45,000 kg. The total amount of recyclable materials in the house is approximately 25,000 kg.
Calculate the percentage ratio of total recycled mass of materials to the total mass of materials

## Slide 13: B.3.4 – RECYCLED MATERIALS
Steps 1 - 2
Steps 3 - 4
Step 5
Total mass of materials used in the building : 45,000 kg
Total recycled mass of materials used in the building : 25,000 kg
Calculate the percentage ratio of total recycled mass of materials to the total mass of materials
45,000 (kg)
25,000 (kg)
=
______
x

## Slide 14: B.3.4 – RECYCLED MATERIALS
EXERCISE

## Slide 15: B.3.4 – RECYCLED MATERIALS
From the Bill of Quantities and Bill of Materials, it resulted that a 200 m2 1½ storey house weighs approximately 50,000 kg. The total amount of recyclable materials in the house is approximately 15,000 kg.
Calculate the percentage ratio of total recycled mass of materials to the total mass of materials