## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
B.4.3 POTABLE WATER CONSUMPTION FOR INDOOR USES | 
ISSUE | CATEGORY
B. Energy & Resource Consumption | B.4 Use of potable water, stormwater and greywater

## Slide 3: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
BACKGROUND
The Mediterranean region holds only 3% of global water resources but hosts over 50% of the world's water poor populations, around 180 million people
In the Middle East and North Africa region, 60% of the population live in areas of high or very high water-stress, compared to the global average of 35%.
Source: https://ufmsecretariat.org/wp-content/uploads/2018/01/water-report-2017.pdf
Annual natural renewable water resources per capita in the Main Mediterranean
Source: https://www.medecc.org/scientific-basis-of-water-food-energy-part-of-the-medecc-report/

## Slide 4: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
INDICATOR
Description | Unit | Project stage | Data source
Potable water consumption per occupant per year | m3/occupant/year | Design ____________ Occupation | Estimation ____________ Metering
To perform the calculation, it is possible to use metered or estimated data.
In case of existing buildings, the water consumptions should be evaluated using data from metering. The metered consumptions have to be estimated taking the average value over 3 years period bills.
The source of data must always be clearly declared

## Slide 5: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
INTENT
Make efficient use of water resources.

## Slide 6: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
DESCRIPTION
This indicator estimates or measures the water consumption of sanitary fittings/devices and water consuming appliances of a building.
It can be applied to new, renovated or existing buildings in order to understand, and ultimately decrease, the water consumption.

## Slide 7: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
BOUNDARY & SCOPE
The assessment boundary is the building.
The indicator includes the use of potable water for :
- drinking water
- water for sanitation
- water for cleaning
- domestic hot water
Water consumption for watering is not taken into account

## Slide 8: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
ASSESSMENT METHOD
To perform the calculations, it is possible to use actual or estimated data. In case of existing buildings, the actual potable water consumptions should be evaluated using data from metering. It is preferable to consider actual data from longer records (e.g. three year data) or at least 12 consecutive months.
In case of estimated data, the number of sanitary devices/fittings (i.e. toilets, taps and showers) and water using appliances (i.e dishwashers and washing machines) should be taken into account for the calculations. Consumption rates for different sanitary devices and fittings are determined through specific data from suppliers or libraries. The specific usage factors have to be established. The number of days that the building is expected to be occupied per year has to be defined by the user.
The source of data must always be clearly declared

## Slide 9
ASSESSMENT METHOD – METERED DATA
Collect actual data of annual potable water consumption and calculate the average annual total potable water consumption of the building, [m3]. **
It is preferable to consider actual data from longer records (e.g. three year data) or at least 12 consecutive months.
Define the number of building’s occupants.
Calculate the indicator’s value as: annual total potable water consumption (step 1) / number of occupants (step 2), [m3 /occupant].
B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
** Garden watering should be extracted. Default annual water consumption for garden watering is estimated between 0.3-1 m3/m2 garden area

## Slide 10: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
ASSESSMENT METHOD – ESTIMATED DATA
The calculation steps are the following:
Define all the sanitary devices/fittings (i.e. toilets, taps and showers) and the water using equipment (i.e. washing machines, dishwashers, water cooled cooling tower) of the building
Determine the typical consumption rates for different sanitary devices and fittings, through specific data from suppliers or libraries
Define typical usage factors for each sanitary device and equipment
Define the annual number of days that the building is occupied

## Slide 11: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
ASSESSMENT METHOD – ESTIMATED DATA
The principle of the per occupant water consumption calculation for taps and showers is as follows:
The exact same principle applies for calculations for toilets (except that flushes are used instead of minutes).

## Slide 12: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
ASSESSMENT METHOD – ESTIMATED DATA
For cleaning, the basis of the calculation is as follows:

## Slide 13: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
ASSESSMENT METHOD – ESTIMATED DATA
Typical water consumption rates
Toilet flushing : 9 Lt
Bath : 150 Lt
Shower: 15 Lt/min
Washing hands, face, teeth : 10-15 Lt/min
Washing machine : 150 Lt
Dishwasher: 50 Lt
Washing fruits/vegetables : 15 Lt/min
Washing dishes 150 Lt/day

## Slide 14: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
ASSESSMENT METHOD – ESTIMATED DATA
ANSI/ASHRAE/ICC/USGBC/IES Standard 189.1-2017
https://www.ashrae.org/technical-resources/bookstore/standard-189-1
Minimum requirements of water consumption in «Green Buildings»

## Slide 15
ASSESSMENT METHOD – ESTIMATED DATA
Calculate the annual total potable water consumption of the building, [m3].
Define the number of building’s occupants
Calculate the indicator’s value as: annual total potable water consumption (step 5) / number of occupants (step 6), [m3 /occupant].
B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
m3 /occupant

## Slide 16: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
REFERENCES and STANDARDS
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en

## Slide 17: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
EXAMPLE

## Slide 18: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
An existing building has 100 occupants and a floor area of 1000m2. The building is occupied 350 days a year
Available data: The floor area, the number of occupants, the number of sanitary devices and water using equipment, the consumption rates and the typical usage factors
Calculate the annual potable water consumption per occupant

## Slide 19: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
20 taps, 6 liters per minute, 3 minutes per occupant per day
3 showers, 6 liters per minute, 5 minutes per shower. Each shower used 10 times a day
10 toilets, average flush 3 Liters. Each toilet used 20 times a day
100 cleans per year and use of 0,01L/m²
Available data
Steps 1 -4

## Slide 20: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
Annual consumption for taps
10taps * [ 6L/min * 3min/occupant * (350/365)] * 0,001 = 0.36 m3/occupant
Annual consumption for showers
3showers * [10times/day * 6L/min * 3min/shower * (350/365)] * 0,001 = 0.86 m3/occupant
Annual consumption for toilets
10toilets * [20flushes/day * 3L/flush * (350/365)] * 0,001 = 0.58 m3/occupant
Annual consumption for cleaning
100cleans * [0,01L/m² * 1000m²] * 0,001 = 1.00 m3/occupant
Annual total consumption = 2.8 m3/occupant
Calculate the annual total potable water consumption of the
building
Steps 5 -7

## Slide 21: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
EXERCISE

## Slide 22: B.4.3 – POTABLE WATER CONSUMPTION FOR INDOOR USES
An existing building has 75 occupants and a floor area of 800m2. The building is occupied 330 days a year
Available data:
8 toilets, with average flush: 3 Liters. Each toilets used 20 times a day
10 taps with 6 liters per minute, 2 minutes per occupant per day
No showers
50 cleans per year and use of 0,02L/m²
Calculate the annual potable water consumption per occupant