## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: C.1.1 – EMBODIED GHG EMISSIONS
C.1.1 – EMBODIED GHG EMISSIONS | 
ISSUE | CATEGORY
C. Environmental Loadings | C.1 Greenhouse Gas Emissions

## Slide 3
BACKGROUND
Embodied greenhouse gas emissions is the amount of greenhouse gas (GHG) emissions that are generated by all the processes associated with the production of construction materials, from the acquisition of raw materials to manufacturing and assembling building construction materials at the factory gate (cradle-to-gate).
C.1.1 – EMBODIED GHG EMISSIONS
Embodied greenhouse gas emissions is the emissions footprint of a building before it becomes operational

## Slide 4
BACKGROUND
Most of the life cycle impacts (over 90%) refer to the cradle-to-gate and CO2 emissions.
Transportation to the building site accounts for about 7% more, while some recurrent amounts will also be added during maintenance and replacement of some elements, as needed.
The final demolition at the end of a building’s lifetime may account for about 1% of the life cycle impacts, depending on waste management.
C.1.1 – EMBODIED GHG EMISSIONS

## Slide 5
BACKGROUND
The metric used for Embodied greenhouse gas emissions is the global warming potential (GWP) quantified in kilograms of CO2 equivalent (kgCO2eq) and then normalized per unit floor area (kgCO2eq/m2).
The “equivalent” (eq) mass of CO2 is used to express the equivalent impacts of all GHG gases, including the dominant contributor of CO2 emissions
GWP of CO2=1 (by definition)
GWP for methane CH4 = 25 (GWP over 100 years is 25 times that of CO2)
GWP for nitrous oxide N2O = 298 (GWP over 100 years is 298 times that of CO2)
C.1.1 – EMBODIED GHG EMISSIONS

## Slide 6
INDICATOR
Description | Unit | Project stage | Data source
Embodied greenhouse gas emissions per internal useful floor area | kg CO2eq/m2 | Design ____________ Occupation | Estimation ____________ Not applicable
C.1.1 – EMBODIED GHG EMISSIONS
The indicator is only applicable at design stage.
In case of new construction, the indicator must be calculated taking in account all the materials used for the building construction.
In case of an existing renovated building, the indicator must be calculated taking in account only the materials used for its renovation and not the ones pre-existent.

## Slide 7: C.1.1 – EMBODIED GHG EMISSIONS
INTENT
Promote the use of construction materials and processes with low embodied greenhouse gas emissions.

## Slide 8: C.1.1 – EMBODIED GHG EMISSIONS
BOUNDARY & SCOPE
The assessment boundary is the building
The scope comprises the product stage of the building i.e. from raw material supply to manufacturing. The scope encompasses the building materials excluding the technical installations. All the elements of the construction are taken in account: foundations, bearing structure, envelope, slabs.

## Slide 9: C.1.1 – EMBODIED GHG EMISSIONS
BOUNDARY & SCOPE
The minimum scope of the indicator includes the following building parts and elements:

## Slide 10
C.1.1 – EMBODIED GHG EMISSIONS
ASSESSMENT METHOD
To calculate the value of the indicator it is necessary to compile a Bill of Materials (BoM) that is a mass-based inventory of the different materials (kg) that compose a building. The BoM is organized according to main elements composing a building
The starting point is the Bill of Quantities (BoQ) specifying the elements of a building (e.g. foundations, columns). The BoQ includes different categories of elements, which can have different functional performance characteristics. BoM differs from a BoQ in that it describes the different materials (e.g. concrete, steel, aluminium) that are contained in the various building elements.
A BoQ includes the building elements accounting for at least 99% of the mass of the building.

## Slide 11
C.1.1 – EMBODIED GHG EMISSIONS
ASSESSMENT METHOD
The calculation steps are the following:
  Identify the basic composition of each building element. A breakdown of its constituent materials has to be carried out. The mass of each material has to be estimated
  Aggregate by material. The mass for each constituent material should thereafter be aggregated to obtain the total mass for each type of material, [kg].
  Calculate the embodied greenhouse gas emissions of each material by multiplying the specific mass (i.e. kg) with its corresponding GHG emissions coefficient, [kgCO2/kg].
  Sum the embodied carbon of all materials to calculate the total embodied GHG emissions of the building, [kg CO2]
  Calculate the total useful internal floor area, [m2]
  Calculate the indicator’s value as: total embodied GHG emissions of the building (step 4) / total useful internal floor area (step 5), [kgCO2/ m2].
kgCO2/ m2

## Slide 12
C.1.1 – EMBODIED GHG EMISSIONS
ASSESSMENT METHOD
For emissions coefficient use national coefficients, if available. or international data bases, for example, (ICE Database).
The coefficients are quantified in kilograms of CO2 equivalent (kgCO2eq) per unit mass (kg) of the material or sometimes also expressed per unit area of material (kgCO2eq/m2)

## Slide 13: C.1.1 – EMBODIED GHG EMISSIONS
REFERENCES and STANDARDS
EN 15978 “Sustainability of construction works - Assessment of environmental performance of buildings - Calculation method”
European Platform on Life Cycle Assessment, European Commission. https://eplca.jrc.ec.europa.eu/?page_id=86
ICE Database, Inventory of Carbon and Energy, Circular Ecology. https://circularecology.com/embodied-carbon-footprint-database.html
IEA Evaluation of Embodied Energy and CO2eq for Building Construction (Annex 57), International Energy Agency. http://www.iea-ebc.org/Data/publications/EBC_Annex_57_Results_Overview.pdf
ISO 14040/44, EN 15804 (Sustainability of construction works. Environmental product declarations. Core rules for the product category of construction products)

## Slide 14: C.1.1 – EMBODIED GHG EMISSIONS
EXAMPLE

## Slide 15: C.1.1 – EMBODIED GHG EMISSIONS
Calculate the embodied GHG emissions per internal useful floor area
of a house of 195 m2
Steps 1 -3
MATERIAL TYPE | APPROXIMATE WEIGHT (kg) From BoQ | EMBODIED EMISSIONS (kgCO2eq/kg) From BoM | EMBODIED EMISSIONS (kgCO2eq)
Floors - concrete |  |  | 
17.5 Mpa concrete in floor slab with lightweight cladding | 53,184 | 0.124 | 6,595
Concrete masonry foundation | 1,312 | 0.136 | 178
Reinforcing steel for slab on ground and foundation | 789 | 1.99 | 1,570
Vinyl flooring | 2,049 | 3.19 | 6,536

## Slide 16: C.1.1 – EMBODIED GHG EMISSIONS
Steps 1 -3
MATERIAL TYPE | APPROXIMATE WEIGHT (kg) From BOQ | EMBODIED EMISSIONS INTENSITY (kgCO2eq/kg) From BOM | EMBODIED EMISSIONS (kgCO2eq)
Windows and glazing |  |  | 
Aluminium window joinery – factory coated | 144 288 | 9.16 | 2,638
Float glass | 450 | 0.91 | 409
Wall cladding |  |  | 
Brick veneer | 13,780 | 0.21 | 2,894
Fibre-cement sheet | 2,940 | 0.554 | 1,629

## Slide 17: B1.6 – EMBODIED GHG EMISSIONS
Calculate the total embodied GHG emissions of the building
+ 1,570 + 6,536 + 2,638 + 409 + 2,894 + 1,629 ) = 27,449 kgCO2eq
Step 4
Step 5
Step 6
Internal useful floor area: 195 m2
27,449 kgCO2eq

=
Total embodied GHG emissions
195 m2
115.1 kgCO2eq /m2
internal useful
floor area
Calculate the total embodied GHG emissions per internal useful floor area

## Slide 18: C.1.1 – EMBODIED GHG EMISSIONS
EXERCISE

## Slide 19: C.1.1 – EMBODIED GHG EMISSIONS
Calculate the embodied GHG emissions per internal useful floor area
of a new building of 200 m2
Steps 1 -3
MATERIAL TYPE | APPROXIMATE WEIGHT (kg) From BoQ | EMBODIED EMISSIONS (kgCO2eq/kg) From BoM | EMBODIED EMISSIONS (kgCO2eq)
Floors - concrete |  |  | 
17.5 Mpa concrete in floor slab with lightweight cladding | 54,547 | 0.124 | 
Concrete masonry foundation | 1345 | 0.136 | 
Reinforcing steel for slab on ground and foundation | 810 | 1.99 | 
Vinyl flooring | 2,103 | 3.19 | 

## Slide 20: C.1.1 – EMBODIED GHG EMISSIONS
Steps 1 -3
MATERIAL TYPE | APPROXIMATE WEIGHT (kg) From BOQ | EMBODIED EMISSIONS INTENSITY (kgCO2eq/kg) From BOM | EMBODIED EMISSIONS (kgCO2eq)
Windows and glazing |  |  | 
Aluminium window joinery – factory coated | 296 | 9.16 | 
Float glass | 462 | 0.91 | 
Wall cladding |  |  | 
Brick veneer | 14,133 | 0.21 | 
Fibre-cement sheet | 3,015 | 0.554 |