## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: D.1.2 TVOC CONCENTRATION
D.1.2 - TVOC CONCENTRATION | 
ISSUE | CATEGORY
D. Indoor Environmental Quality | D.1 Indoor Air Quality and Ventilation

## Slide 3: D.1.2 TVOC CONCENTRATION
BACKGROUND
Volatile organic compounds (VOC) means any compound of carbon, excluding carbon monoxide, carbon dioxide, carbonic acid, metallic carbides or carbonates, and ammonium carbonate, which participates in atmospheric photochemical reactions.
VOCs are the main source for poor indoor air quality, which can affect a person’s daily life.
VOCs are suspected to be one of the major causes of Sick-Building Syndrome (SBS)

## Slide 4: D.1.2 TVOC CONCENTRATION
BACKGROUND
TVOCs Effects |  | 
Personal Comfort | Perception of Cleanliness | Health
Elevated TVOC levels can cause headaches and irritation Some individuals, particularly children, have greater sensitivity | Bad odors and stale air can be perceived as a lack of cleanliness and make people feel uncomfortable People can lose the ability to perceive scents if frequently exposed to odors | Some TVOCs are carcinogens (e.g. formaldehyde) Some TVOCs are irritants at normal levels (e.g. toluene)
Source: https://www.renesas.com/us/en/document/whp/overview-tvoc-and-indoor-air-quality

## Slide 5: D.1.2 ΤVOC CONCENTRATION
According to empirical data from field measurements
Source: P. Wargocki, On the quest for indices defining indoor air quality. What is a reasonable approach?, webinar on IAQ - indoor air quality and IAQ metrics, Air infiltration and Ventilation Centre - AIVC, 2017.
https://www.aivc.org/sites/default/files/05_Wargocki_2017_AIVC_Workshop_Brussels.pdf
Common TVOC concentration in buildings is lower than 1.0μg/m3
Maximum concentration should not exceed 300mg/m3
1 PPM = 1,000 microgram per meter cubed
Maximum concentration for different categories:
100mg/m3 for Alkanes
50mg/m3 for Aromatics
30mg/m3 for Terpene
20mg/m3for Esteres
30mg/m3 for Halocarbons
50mg/m3 for Carboxyls
BACKGROUND

## Slide 6: D.1.2 ΤVOC CONCENTRATION
INDICATOR
Description | Unit | Project stage | Data source
TVOC concentration in indoor air | μg/ m3 | Design ____________ Occupancy | Not applicable ____________ Measurements
The indicator is only applicable in a post completion phase of a building, prior to occupation

## Slide 7: D.1.2 TVOC CONCENTRATION
INTENT
Facilitate the assessment of indoor air quality.

## Slide 8: D.1.2 ΤVOC CONCENTRATION
DESCRIPTION
This indicator measures one of the most significant potential hazards to human health that can impact indoor air, the Total Volatile Organic Compounds (TVOC).
In an air tight, modern building, the most significant direct emissions sources related to building construction material & products and other building finish materials may originate from:
- paints and varnishes,
- textile furnishings,
- floor coverings,
- associated adhesives and sealants, and
- finish materials that incorporate particle board

## Slide 9: D.1.2 ΤVOC CONCENTRATION
BOUNDARY & SCOPE
The boundary is the building.
The instruments to be utilised for the measurement may vary in relation to what pollutant is necessary to assess, in most cases VOCs detectors are used, located on tripod at a height of 1.5 metres.
It is recommended to perform the measurement for a period sufficient to establish the TVOCs concentration level trend (not less than a week).

## Slide 10: D.1.2 ΤVOC CONCENTRATION
BOUNDARY & SCOPE
TVOCs concentration levels must be measured in all spaces with characteristic functions (e.g. office spaces, meeting room, cafeteria), different orientations (e.g. on the side of a façade facing the street), and floors (e.g. first, middle and last floor). The indicator value for the building is then calculated as a weighted average of the corresponding measurements
For each pollutant measured, the quantitative increase of the indoor air value in relation to the external air value has to be checked.

## Slide 11: D.1.2 ΤVOC CONCENTRATION
ASSESSMENT METHOD – POST COMPLETION/ IN-USE PHASE
The calculation steps are the following:
Calculate the TVOC concentration in each selected characteristic space, [μg/ m3]
Calculate the internal floor area of each characteristic space, [m2]
Calculate the total internal floor area of all selected characteristic spaces, [m2]
Sum the products of the measured TVOC concentrations in each characteristic space multiplied by the corresponding floor area
Calculate the weighted value of the TVOC concentration for the building as the ratio of the sum of products of the TVOC concentration (step 4) to the total internal floor area of the selected characteristic spaces (step 3), [μg/ m3].
.

## Slide 12: D.1.2 ΤVOC CONCENTRATION
REFERENCES and STANDARDS
Level(s) (the European framework for sustainable buildings) indicator 4.1: Indoor air quality. Document developed by European Commission - Joint Research Centre, January 2021.
EN 16516: construction products: Assessment of release of dangerous substances - Determination of emissions into indoor air.
ISO 16000-6:2021 - Indoor air — Part 6: Determination of organic compounds (VVOC, VOC, SVOC) in indoorand test chamber air by active sampling on sorbent tubes, thermal desorption and gas chromatography using MS or MS FID
CEN 15251 (Indoor environmental input parameters for design and assessment of energy performance of buildings addressing indoor air quality, thermal environment, lighting and acoustics)
EN 16798-1:2017 - Energy performance of buildings - Part 1: Indoor environmental input parameters for design and assessment of energy performance of buildings addressing indoor air quality, thermal environment, lighting and acoustics - Module M1-6 (revision of EN 15251). Brussels: European Committee for Standardization.
C. Laffarfue, C. Reinhard, S. Mason , Harmonization of VOC emissions testing in Europe – the new Standard CEN/TS 16516, International Society of Indoor Air Quality and Climate
.

## Slide 13: D.1.2 ΤVOC CONCENTRATION
ASHRAE Standard 189.1 - Design of High-Performance Green Buildings. https://www.ashrae.org/technical-resources/standards-and-guidelines/read-only-versions-of-ashrae-standards
REFERENCES and STANDARDS

## Slide 14: D.1.2 TVOC CONCENTRATION
EXAMPLE

## Slide 15: D.1.2 TVOC CONCENTRATION
In an existing building with an internal floor area of 500m2, measurements of TVOCs concentrations were carried out in six main spaces (S1-6).
Available data:
Calculate the TVOC concentration in indoor air
 | S1 | S2 | S3 | S4 | S5 | S6
Floor Area (m2) | 55 | 60 | 70 | 45 | 60 | 55
TVOC (μg/m3) | 58.36 | 72.00 | 93.40 | 52.13 | 67.14 | 89.11
Steps 1 - 2

## Slide 16: D.1.2 TVOC CONCENTRATION
Step 5
Sum the products of the measured TVOC concentrations in each characteristic space multiplied by the corresponding floor area
((55*58.36) + (60*72.00) + (70*93.40) + (45*52.13) + (60*67.14) + (55*89.11)) = 25,343.1 (μg/m3) m2
Calculate the average TVOC concentration in indoor air
345 (m2)
25,343.1 ((μg/m3) m2)
=
______
Step 3
Step 4
Calculate the total internal floor area of all selected spaces : 345 m2

## Slide 17: D.1.2 TVOC CONCENTRATION
EXERCISE

## Slide 18: D.1.2 TVOC CONCENTRATION
In an existing building, measurements of TVOCs concentrations were carried out in two main spaces (S1-2).
Available data:
Calculate the TVOC concentration in indoor air
 | S1 | S2
Floor Area (m2) | 89 | 14
TVOC (μg/m3) | 32.7 | 31.8
S1
S2
Source: D’Amico, A.; Pini, A.; Zazzini, S.; D’Alessandro, D.; Leuzzi, G.; Currà, E. Modelling VOC Emissions from Building Materials for Healthy Building Design. Sustainability 2021, 13, 184. https://dx.doi.org/10.3390/ su13010184