## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: D.3.1 – DAYLIGHT
BACKGROUND
Daylight factor (DF) is a daylight availability metric that expresses the amount of daylight available inside a room (on a work plane) compared to the amount of unobstructed daylight available outside under overcast sky conditions
For example: If the available amount of daylight at a point in a room is 180 lux, and outdoor is 20000 lux then, daylight factor at that point is 0.9 %
Source: https://www.velux.com/what-we-do/research-and-knowledge/deic-basic-book/daylight/daylight-calculations-and-measurements

## Slide 3: D.3.1 – DAYLIGHT
BACKGROUND
Daylight Factor depends on:
Area of glazing: the greater the area of the glazings in a room, the higher the DF.
Orientation of glazing: the more angled the window (e.g. roof lights) the more daylight could be let inside that room. This is simply due to a wider view range of skylight to the sky.
Sill height: higher sill heights, especially in rooms with higher depths guarantee higher levels of daylight.
Depth of room: deeper rooms (where the distance between windows and distant walls is great), are subjects of lesser DF.
Outside obstacles: outdoor buildings and other features are considered as obstacles to the clear sky view from the windows. Window location, area and sill height can be set to minimize the obscured view.
Reflectivity of fabrics: brighter floors, ceilings and internal walls reflect more light and increase DF
Visible Light Transmittance of glazing: indoor daylight level contribution of a clear window is more than that of the tinted window
Source: Mardaljevic, J., Andersen, M., Roy, N., Christoffersen, J. (2012) Daylighting, Artificial Lighting and Non-Visual Effects Study for a Residential Building

## Slide 4: D.3.1 – DAYLIGHT
BACKGROUND
The higher the DF, the more daylight is available in the room.
Rooms with an average DF of 2% or more can be considered daylit, but electric lighting may still be needed to perform visual tasks.
A room will appear strongly daylit when the average DF is 5% or more, in which case electric lighting will most likely not be used during daytime. (Source: CIBSE (2002) Code for Lighting, Oxford: Chartered Institution of Building Services Engineers)

## Slide 5: D.3.1 – DAYLIGHT
D.3.1 – DAYLIGHT | 
ISSUE | CATEGORY
D. Indoor Environmental Quality | D.3 Daylighting and Illumination

## Slide 6: D.3.1 – DAYLIGHT
INDICATOR
Description | Unit | Project stage | Data source
Mean Daylight Factor | % | Design ____________ Occupation | Estimation ____________ Measurement

## Slide 7: D.3.1 – DAYLIGHT
INTENT
Ensure an adequate level of daylighting in all primary occupied spaces.

## Slide 8: D.3.1 – DAYLIGHT
The assessment boundary is the building
The indicator must be calculated in all spaces with characteristic functions of the building (e.g. office spaces, meeting room, cafeteria), different orientations (e.g. on the side of a façade facing the street), and floors (e.g. first, middle and last floor). The indicator value for the building is then calculated as a weighted average of the corresponding measurements
BOUNDARY & SCOPE

## Slide 9: D.3.1 – DAYLIGHT
ASSESSMENT METHOD - DESIGN PHASE
Method 1) Calculation method using daylight factors on the reference plane.
The calculation steps are :
Identify the grid of points on the plane
Predict the daylight factors across the plane
Calculate the target daylight factor DT and DTM
Ensure that the daylight factors equal or exceed the target values (DTM and DT).

## Slide 10: D.3.1 – DAYLIGHT
ASSESSMENT METHOD - DESIGN PHASE
Method 2) Calculation method using climatic data for the given site and an adequate time step.
The calculation steps are :
Simulate illuminance values on the reference plane based on hourly internal daylight illuminance values
Ensure that the targeted illuminance levels are achieved or exceeded
The daylight provision is calculated in new and under major renovation buildings accordingly to EN 17037. Paragraph 5.1.3 fully describes the two possible calculation methods. Annex A gives values for target illuminances and minimum target illuminances to be achieved. Annex B describes recommendations for the daylight calculations

## Slide 11: D.3.1 – DAYLIGHT
ASSESSMENT METHOD – POST COMPLETION & OCCUPANCY PHASE
The calculation steps for existing buildings are :
Identify several measuring points in each selected space of the building
Conduct the measurements with a luxmeter
At the same time measure the external values (best in overcast conditions with no direct solar radiation). In addition to the luxmeter and if necessary, a shadow ring could be used.
Calculate the average daylight factor in each selected space, making a ratio between the average indoor values measured and the average outdoor values, [%]

## Slide 12: D.3.1 – DAYLIGHT
ASSESSMENT METHOD – POST COMPLETION & OCCUPANCY PHASE
Calculate the internal floor area of each space, [m2]
Calculate the total internal floor area of the selected spaces , [m2]
Sum the average daylight factor in each space multiplied by the corresponding area to calculate the weighted daylight factor
Calculate the indicator’s value as the ratio of the weighted daylight factor to the total internal floor area of the selected spaces, [%]
In case of the in-use building, some adjusting must be adopted to obtain an accurate measurement (curtains drawn, obstruction resulting from the furniture, absence of occupants, etc.).
%

## Slide 13: D.3.1 – DAYLIGHT
EN 17037 – Daylighting in buildings, paragraph 5.1.2 Criteria for daylight provision and paragraph 5.1.3 Daylight Provision Calculation Methods
REFERENCES

## Slide 14: D.3.1 – DAYLIGHT
EXAMPLE

## Slide 15: D.3.1 – DAYLIGHT
Calculate the Mean Daylight Factor of the building
In an office building, a series of simulations were carried out, for five (5) typical rooms, for the Daylight Factor
 | Office 1 | Office 2 | Office 3 | Office 4 | Office 5
Area (m2) | 14.3 | 16.3 | 25.0 | 23.7 | 33.0
Average DF (%) | 4.1 | 3.6 | 2.6 | 3.1 | 3.9
Office 1 | Office 2 | Office 3 | Office 4 | Office 5
Steps 1 - 5
DF
Source: K. Mantzourani et al 2020 IOP Conf. Ser.: Earth Environ. Sci. 410 012099

## Slide 16: D.3.1 – DAYLIGHT
Step 7
Sum the products of the Daylight Factor in each space multiplied by the corresponding floor area
((4.1 *14.3) + (3.6 *16.3) + (2.6 *25.0) + (3.1 *23.7) +(3.9 *33.0)) = 384.5 % m2
Step 6
Calculate the total internal floor area of all selected spaces: 112.3 m2
Step 8
Calculate the mean Daylight Factor
=
112.3 (m2)
384.5 (% m2)
______

## Slide 17: D.3.1 – DAYLIGHT
EXERCISE

## Slide 18: D.3.1 – DAYLIGHT
Calculate the Mean Daylight Factor of the building
8.8%
8.9%
8.6%
5.6%
2.7%
4.0%
2.8%
2.6%
4.0%
2.1%
Source: C. Carletti, G. Cellai, L. Pierangioli, F. Sciurpi, S. Secchi, The influence of daylighting in buildings with parameters nZEB: application to the case study for an office in Tuscany Mediterranean area. AiCARR 50th International Congress; Beyond NZEB Buildings, 10-11 May 2017, Matera, Italy
In an office building, the average DF was measured in ten rooms