## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: G.1.4 ENERGY COST
G.1.4 USE STAGE ENERGY COST | 
ISSUE | CATEGORY
G. Cost and Economic Aspects | G.1 Cost and Economics
Fuels
Electricity

## Slide 3: G.1.4 ENERGY COST
INDICATOR
Description | Unit | Project stage | Data source
Annual energy cost per useful internal floor area | €/m2/yr | Design ____________ Occupation | Estimation ____________ Energy bills

## Slide 4: G.1.4 ENERGY COST
INTENT
Optimize the operating cost of buildings to reflect the potential for long term performance.

## Slide 5: G.1.4 ENERGY COST
DESCRIPTION
The focus of the indicator is on the costs of thermal and electric energy during operation for all uses.
Internal thermal conditions and environmental quality is a priority

## Slide 6: G.1.4 ENERGY COST
The assessment boundary is the building
The scope of the indicator includes the following energy uses, also referred to as end-uses and technical building services of the building :
heating,
cooling,
ventilation,
domestic hot water,
lighting,
auxiliaries,
appliances,
elevators
cooking appliances
Data from Β.1.2 & Β.1.3 should be used with caution
BOUNDARY & SCOPE

## Slide 7: G.1.4 ENERGY COST
ASSESSMENT METHOD
Reporting can be based on estimated performance at the design stage and after monitoring of performance during normal building occupancy. This means they can be used by a range of project actors, including during the design stage, to estimate future performance and performance following occupation so as to check how the building is actually performing against projected short, medium and long-term cost schedules.
In case of existing buildings, the total annual cost of actual thermal and electrical energy use from energy bills should be calculated taking the average energy cost over 3 years period.

## Slide 8: G.1.4 ENERGY COST
ASSESSMENT METHOD – DESIGN STAGE
The calculation steps for new (design) buildings are the following:
Calculate the annual energy use per energy source for all technical building services taken into account, in kilowatt hours per year (kWh/y).
Calculate the useful internal floor area of the building, in square meters (m2)
Calculate the annual operational enegy cost for each energy source, in € per useful internal floor area of the building (€/m2/y).
Calculate the annual total operational energy cost for all energy sources, in € per useful internal floor area of the building (€/m2/y)
Calculations take into account all technical servises of the building

## Slide 9: G.1.4 ENERGY COST
ASSESSMENT METHOD – OCCUPANCY STAGE
The calculation steps for existing buildings are the following:
Calculate the annual energy cost for the thermal and electrical energy use of the building, based on bills, using a 3year average or at least one whole year, in €
Calculate the useful internal floor area of the building, in square meters (m2)
Calculate the annual operational enery cost, per useful internal floor area of the building (€/m2/y).
Calculations take into account all technical servises of the building

## Slide 10: G.1.4 ENERGY COST
Level(s) Part 1-2 – Beta version. Brussels: European Commission.
http://ec.europa.eu/environment/eussd/buildings.htm
REFERENCES

## Slide 11: G.1.4 ENERGY COST
EXAMPLE

## Slide 12: G.1.4 ENERGY COST
An existing office building located in Athens is connected to the main power grid and it is served by an oil-fired boiler for central space heating, exhaust mechanical ventilation and local split unit heat pumps for cooling. Domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Available data: The building manager provided the floor plans, the annual fuel oil and electricity bills over several years, the operation hours, the number of employees and the number of visitors. The oil quantities correspond to the total fuel orders that were delivered to the building during the corresponding year. The electricity data corresponds to the total building demand for all end-uses of the building during the corresponding year.
Calculate the annual total energy cost per building’s useful internal floor area. Which data are not necessary for the calculations?

## Slide 13: G.1.4 ENERGY COST
 | 2015 | 2016 | 2017
Oil (€) | 18123 | 22204 | 21138
Electricity (€) | 8214 | 11548 | 10256
Annual cost of fuel (oil) and electricity delivered to the building
Typical floor plan
Floor plans have been verified during a short energy audit of the building and can be used to estimate the building’s useful floor area
Available data
Annual Operation days: 201
Number of employees : 8
Annual number of visitors: ~ 2.000
useful internal floor area
1242 m2

## Slide 14: G.1.4 ENERGY COST
Annual energy cost
Average annual energy cost for fuel oil : = 20.488 €
Average annual energy cost for electricity: = 10.006 €
Annual total energy cost per building’s useful internal floor area
= 24.55 €/m2/yr
Step 1
Step 2
Useful internal floor area : 1242 m2
Step 3

## Slide 15: G.1.4 ENERGY COST
Not necessary information for the energy cost calculations:
Annual Operation days
Number of employees
Annual number of visitors

## Slide 16: G.1.4 ENERGY COST
EXERCISE

## Slide 17: G.1.4 ENERGY COST
An existing office building located in Athens is connected to the main power grid and it is served by a natural gas-fired boiler for central space heating and local split unit heat pumps for cooling. The building does not have mechanical ventilation. Domestic hot water is served with local electric continuous-flow (tankless) water heaters.
Διαθέσιμα δεδομένα: The building manager provided the floor plans, monthly fuel and electrical energy consumption over three consecutive years. The electricity data corresponds to the total building electrical energy demand for all its end-uses.
Use the following data to solve the exercise
Calculate the annual total energy cost per building’s useful internal floor area. Which data are not necessary for the calculations?

## Slide 18: G.1.4 ENERGY COST
Floor Plans
Useful internal floor area = 416 m2
Available data

## Slide 19: G.1.4 ENERGY COST
Natural Gas Consumption (m3)
 | Month | 2015 | 2016 | 2017
 | January | 686.9 | 809.5 | 959.9
 | February | 713.0 | 868.5 | 1019.0
 | March | 545.1 | 750.0 | 868.5
 | April | 211.1 | 300.6 | 217.7
 | May | 0.0 | 0.0 | 0.0
 | June | 0.0 | 0.0 | 0.0
 | July | 0.0 | 0.0 | 0.0
 | August | 0.0 | 0.0 | 0.0
 | September | 0.0 | 0.0 | 0.0
 | October | 41.1 | 463.4 | 86.4
 | November | 311.4 | 551.8 | 201.9
 | December | 718.2 | 930.7 | 566.1
Available data
Average cost for natural gas : 0.055 €/kWh

## Slide 20: G.1.4 ENERGY COST
 | Month | 2015 | 2016 | 2017
 | January | 3041.1 | 1992.6 | 2811.4
 | February | 2696.0 | 1861.8 | 2494.3
 | March | 2884.7 | 1869.7 | 2582.8
 | April | 2633.4 | 2014.5 | 2317.1
 | May | 2502.5 | 2407.7 | 2475.9
 | June | 3703.5 | 2146.4 | 2438.4
 | July | 4258.1 | 2448.4 | 3164.8
 | August | 4388.8 | 2487.7 | 3299.3
 | September | 2980.2 | 2419.6 | 3138.6
 | October | 2409.9 | 1898.4 | 1916.7
 | November | 2239.1 | 1530.1 | 1960.7
 | December | 2543.1 | 1676.9 | 1749.5
Electricity Consumption (kWhe)
Available data
Average cost for electricity : 0.10153 €/kWh