## Slide 1
Training Module 3
Calculating the assessment
criteria of
SBTool – Building Scale

## Slide 2: H.1.2 – HEAT ISLAND EFFECT
H.1.2 – HEAT ISLAND EFFECT | 
ISSUE | CATEGORY
H. Adaptation to Climate Change | H.1 Climatic action: increase of temperature
Source: https://hdgbuildingmaterials.com/products/solar-reflectance-index-hdg-primer/

## Slide 3
INDICATOR
Description | Unit | Project stage | Data source
Mean Solar Reflectance Index of paved surfaces and roofs in the area | - | Design ____________ Occupation | Estimation ____________ Estimation
H.1.2 – HEAT ISLAND EFFECT
The area for the calculation of the indicator is the gross area of the building lot.

## Slide 4: H.1.2 – HEAT ISLAND EFFECT
INTENT
Reduce the heat island effect in order to reduce the discomfort at ground level during summer

## Slide 5
H.1.2 – HEAT ISLAND EFFECT
DESCRIPTION
The Solar Reflectance Index (SRi) is a measure of the constructed surface's ability to reflect solar heat.
Source: Cool Roof Rating Council. https://coolroofs.org/documents/CRRC-SRI-Document_2022-07-12.pdf
SRi values vary from 0 (i.e. for materials that absorb all incident solar radiation like a black body) to 100 (i.e. for materials that reflect all the incident solar radiation). Because of the way SRi is defined, very hot materials can have slightly negative SRi values, while very cool materials can have values exceeding 100.

## Slide 6
DESCRIPTION
SRi can be used as an indicator of how hot materials are likely to become when solar radiation is incident on their surface. The lower the SRi, the hotter a material is likely to become in the sunshine.
Typical SRi values
Grey concrete: 35
White concrete: 86
Standard white paint: 100
Standard black paint: 5
New asphalt: 0
H.1.2 – HEAT ISLAND EFFECT
Source: Green Building Council of Australia Green Star – Design and As Built April 2014 - DRAFT
Asphalt, concrete, and other building materials fade or darken with age, increasing or decreasing SRi. SRi of lighter materials (like concrete) decreases with age as the surface darkens and the SRi of darker materials (like asphalt or black concrete) will increase with age as the color of the surface lightens

## Slide 7: H.1.2 – HEAT ISLAND EFFECT
BOUNDARY & SCOPE
The assessment boundary is the building lot.
The minimum scope of the indicator includes all horizontal surfaces (roofs included) of the building envelope and the building lot

## Slide 8: H.1.2 – HEAT ISLAND EFFECT
ASSESSMENT METHOD
The calculation steps are the following:
Identify all the horizontal surfaces and roofs in the building and the lot area
Calculate the area of each surface per cover material, [m2]
Calculate the total area per cover material of horizontal paved surfaces and roofs, [m2]
Calculate the total area of all horizontal surfaces and roofs, [m2]
Multiply the total area per cover material with the corresponding SRi, [m2]
Sum the products of SRi multiplied by area, [m2]
Calculate the indicator’s value as: sum of products of SRi multiplied by area (step 6) / total area of all horizontal surfaces and roofs (step 4)

## Slide 9: H.1.2 – HEAT ISLAND EFFECT
REFERENCES and STANDARDS
ASTM E 1980 – Standard Practice for Calculating Solar Reflectance Index of Horizontal and Low-Sloped Opaque Surfaces
Lawrence Berkeley National Laboratory, Heat Island Group. Cool Roofing Materials Database https://heatisland.lbl.gov/resources/cool-roofing-materials-database
Urban Heat Island Gold Standard and Urban Heat Island Atlas https://link.springer.com/chapter/10.1007/978-3-319-10425-6_2
Fonte V.C. Sharma, Solar Properties of Some Buildings Elements in Energy 1989 vol. 14 p.80 5-10. http://coolroofs.org/products/results

## Slide 10: H.1.2 – HEAT ISLAND EFFECT
EXAMPLE

## Slide 11: H.1.2 – HEAT ISLAND EFFECT
Calculate the mean Solar Reflectance Index of horizontal and roof
surfaces
An existing small one-storey building, with floor area of 120m2 is located within a lot of surface area of 600m2. Τhe building has a flat roof covered with gray asphaltic membrane. The outdoor space is partly covered by natural stone tiles (40%) and vegetation (60%).

## Slide 12: H.1.2 – HEAT ISLAND EFFECT
Step 4
Step 5
Total area of all horizontal surfaces and roofs : 600m2
Weighed area per cover material of horizontal paved surfaces and roofs
Material | Area | SRi | Area x SRi
Asphaltic Membrane, Grey | 120 m2 | 7 1 | 840 m2
Limestone, Grey | 192 m2 | 54 2 | 10368 m2
1 Source : https://coolroofs.org/directory/roof?product_type_id=11&orderBy=product_type&page=1&product_color_id=
2 Source : https://hdgbuildingmaterials.com/products/solar-reflectance-index-hdg-primer/
Step 6
Sum the products of the Sri multiplied by the corresponding floor area
(840+ 10368 ) = 11208 m2

## Slide 13: H.1.2 – HEAT ISLAND EFFECT
Step 7
Calculate the mean SRi
=
600 m2
11208 m2
______

## Slide 14: H.1.2 – HEAT ISLAND EFFECT
EXERCISE

## Slide 15: H.1.2 – HEAT ISLAND EFFECT
Calculate the mean Solar Reflectance Index of horizontal and roof
surfaces over the total plot area
An existing residential building is located within a lot of surface area of 500m2. Τhe building has a tilted roof, with a total surface of 175m2, covered with tiles and a flat roof, with a total surface of 50m2 covered with pavement tiles. The outdoor space is partly covered by natural pavement tiles (75%) and vegetation (25%).