## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM | 
ISSUE | CATEGORY
F. Transportation and Mobility | F.2. Performance of Mobility Service

## Slide 3: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
BACKGROUND

## Slide 4: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
BACKGROUND
Most urban areas are serviced by a public transportation service, but the quality of service, including the density of the route network, scheduling to suit the needs of the local population and affordable fares, vary widely.
Public Transport includes metro, bus, minibus and tram. On average, bus is the dominant mode of transport with a 63% share, followed by bus, metro and suburban rail.
https://cms.uitp.org/wp/wp-content/uploads/2020/08/UITP_Statistic-Brief_national-PT-stats.pdf

## Slide 5: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
INDICATOR
Indicator | Unit | Data source
Percentage of inhabitants that are within 400 meters walking distance of at least one public transportation service stop | % | Metered data
For the calculation of the indicator the following are considered:
- only residents of the neighborhood and not working people in the area
- a stop must have a daily total service frequency of at least 20 trips
The calculation of walking distance between building entrance and transport stop can be performed by in situ measurements of by using maps.

## Slide 6: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
INTENT
Estimate the performance of the public / municipal transportation system

## Slide 7: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
In the calculation the followings should be considered:
Bus
metro
tram
suburban rail
BOUNDARY & SCOPE
The assessment boundary includes the whole neighborhood.

## Slide 8: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
The calculation steps are the following:
Locate the public/municipal transport stops with daily frequency of at least 20 trips, that serve the residential buildings of the neighborhood
Locate all the residential buildings in the neighborhood with a walking distance from their entrance to at least one of the located stops up to 400 meters
Calculate the occupants of the selected buildings
Calculate the total population of the neighborhood
Calculate the indicator’s value as the percentage ratio of the occupants of the selected buildings (step 3) to the total population of the neighborhood, [%]
ASSESSMENT METHOD
%

## Slide 9: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
REFERENCES and STANDARDS
Global Platform for Sustainable Cities – Urban Sustainability Framework. https://www.thegpsc.org/
UNECE - Collection Methodology for Key Performance Indicators for Smart Sustainable Cities
https://www.ncl.ac.uk/media/wwwnclacuk/ceser/files/Understanding%20Cities.pdf
https://unhabitat.org/planning-and-design-for-sustainable-urban-mobility-global-report-on-human-settlements-2013/
http://www.eltis.org/discover/news/interreg-presents-good-practice-sustainable-urban-mobility-and-sumps
Notes: MARINA

## Slide 10: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
EXAMPLE

## Slide 11: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
In an existing neighborhood, there are 16 residential buildings with a total of 614 residents, 10 single houses with three-member families and 5 single houses with four-member families. There is one public school, one supermarket and one pharmacy line and one pharmacy, as shown in the figure below.
Available data: The walking distance of each building from the stops
Calculate the percentage of inhabitants that are within 500 meters
walking distance of at least one public transportation stop.
Transport | Frequency | Line
Municipal | Every hour Monday to Friday: 6:30 – 20:30 Saturday: 8:00 – 18:30 | 
Public | Monday to Friday: 5:30 – 24:00 every 15min Weekend: 6:30 – 24:00 every 30 min | 
Neighborhood

## Slide 12: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
All residential buildings are within 500 meters walking distance of at least one public transportation stop, with daily total service frequency of at least 20 trips.
Available data
Steps 1 -2
Calculate
walking distances

## Slide 13: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
Step 3
Calculate the number of residents in the selected residential buildings in the neighborhood
(10 * 3 + 5 * 4 + 614) = 664 residents
Step 4
Calculate the total number of residents in all residential buildings in the neighborhood
Step 5
Calculate the percentage of inhabitants that are within 500 meters
walking distance of at least one public transportation stop
(10 * 3 + 5 * 4 + 614) = 664 residents
664 residents
664 residents
100 %
100

## Slide 14: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
EXERCISE

## Slide 15: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
In an existing neighborhood, there are 2 public transport stops. Consider four-member families in each building.
Available data: The walking distance of each building from the stops
Transport | Frequency | Line
Public | Monday to Friday: 5:30 – 24:00 every 15min Weekend: 6:30 – 24:00 every 30 min | 
Calculate the percentage of inhabitants that are within 500 meters
walking distance of at least one public transportation stop.

## Slide 16: F.1.1 – PERFORMANCE OF THE PUBLIC TRANSPORT SYSTEM
Available data
NEIGHBORHOOD
https://www.google.com/maps