## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
G3.1: AVAILABILITY AND PROXIMITY OF KEY SERVICES | 
ISSUE | CATEGORY
G. Social Aspects | G.3 Availability of public and private facilities and services

## Slide 3
BACKGROUND
Convenient locations of key services for access by local residents (e.g. schools, sports facilities, supermarket, community buildings, etc.) is a major factor in reducing the use of private vehicles and in ensuring that residents can obtain access to the services they need.
G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES

## Slide 4
INDICATOR
G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
Indicator | Unit | Data source
Percentage of inhabitants that are within 800 meters walking distance of at least 3 key services. | % | Metered data
For the calculations, only residents of the neighborhood are considered and not working people in the area
The calculation of walking distance between building entrance and key service can be performed by in situ measurements or by using maps.

## Slide 5: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
INTENT
Determine the accessibility of local residents to key services (e.g. schools, sports facilities, supermarket, community buildings, etc.)

## Slide 6: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
Key Services include the following categories :
1. Education (schools, kindergartens, nurseries, education centers, etc.)
2. Health center (hospitals, medical wards, medical centers, etc.)
3. Law enforcement services (police station, etc.)
4. Sport facilities
5. Food shops
6. Bank
7. Post office
8. Pharmacy
9. Shopping center
10. Culture and leisure facilities
BOUNDARY & SCOPE
The assessment boundary includes the whole neighborhood.
At least three categories should be selected.
Only one key service from each category should be considered.
Private services can be considered

## Slide 7
ASSESSMENT METHOD
The calculation steps are the following:
Locate the key services in the neighborhood
Locate all the residential buildings in the neighborhood with a walking distance from their entrance to at least three key services up to 800 meters.
Calculate the residents number of the selected buildings.
Calculate the total residents in the neighborhood
Calculate the indicator’s value as the percentage of the residents number of the selected buildings (step 3) to the total residents in the neighborhood (step 4), [%]
G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
%

## Slide 8: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
REFERENCES and STANDARDS
Global Platform for Sustainable Cities, World Bank. 2018. “Urban Sustainability Framework.” 1st ed. Washington, DC: World Bank

## Slide 9: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
EXAMPLE

## Slide 10: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
In an existing neighborhood (market with the white line), there are 16 residential buildings with a total of 212 residents and 15 single houses with three-member families.
Calculate the percentage of inhabitants that are within 800 meters
walking distance of at least three key services.
There is one school, one supermarket and one pharmacy in the neighborhood, as shown in the figure.
Available data: The walking distance of each building from the services

## Slide 11: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
All residential buildings are within 800 meters walking distance from the three key services.
Available data
Steps 1 -2
School
Supermarket
Pharmacy

## Slide 12: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
Step 3
Calculate the number of residents in the selected residential buildings in the neighborhood
(15 * 3 + 212) = 257 residents
Step 4
Calculate the total number of residents in all residential buildings in the neighborhood
Step 5
Calculate the percentage of inhabitants that are within 800 meters
walking distance of at least three key services
(15 * 3 + 212) = 257 residents
257 residents
257 residents
100 %
100

## Slide 13: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
EXERCISE

## Slide 14: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
In an existing neighborhood there are 57 residential buildings with a total of 157 residents. Nearby there are the following key services:
School
Health center
Bank
Sports facility
Food market
Shopping center
Calculate the percentage of inhabitants that are within 800 meters
walking distance of at least three key services.

## Slide 15: G.3.1 - AVAILABILITY AND PROXIMITY OF KEY SERVICES
School
Sports
Facilities
Food market
Bank
Health Centre
Residential Area
Shopping Centre