## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: I.3.3 – PERMEABILITY OF LAND
I.3.3 – PERMEABILITY OF LAND | 
ISSUE | CATEGORY
I. CLIMATE CHANGE: Mitigation and Adaptation | I.3 Adaptation to the climatic action: pluvial flood

## Slide 3: I.3.3 – PERMEABILITY OF LAND
BACKGROUND
Soil sealing is the permanent covering of an area of land and its soil by impermeable artificial material, such as asphalt and concrete
Most common surfaces, from most to less permeable(1) lawn, (2) gravel turf, (3) plastic and (4) concrete grass grids, (5) water-bound surfaces, (6) permeable concrete pavements, (7) porous asphalt, (8) common pavement (impermeable asphalt).
Other types of permeable and semipermeable surfaces

## Slide 4: I.3.3 – PERMEABILITY OF LAND
BACKGROUND
Urban areas amounted to 4.1 % (176000 km²), 4.3% (186 000 km²) and 4.4% (192000 km²) of the EU territory in 1990, 2000 and 2006 respectively.
The total soil sealed surface area in 2006 was estimated to be about 2.3% of the EU’s territory, with an average of 200 m² per citizen.
Member States with high shares of sealed surfaces (exceeding 5% of the national territory) are Malta, the Netherlands, Belgium, Germany, and Luxembourg. High sealing rates exist across most of the Mediterranean coast, which experienced a 10% increase in soil sealing during the 1990s alone.
Source: EU Final Report. Overview of best practices for limiting soil sealing or mitigating its effects in EU-27. April 2011
Share of sealed surface per region

## Slide 5: I.3.3 – PERMEABILITY OF LAND
BACKGROUND
Main impacts of soil sealing
Water resources. A fully functioning soil can store as much as 3750 tonnes of water per hectare (almost 400 mm of precipitation). Sealing reduces the amount of rainfall that can be absorbed by the soil
Above and belowground biodiversity. Scientists estimate that at least a quarter of species on the planet live in soils
Global carbon cycle. There are about 70-75 billion tonnes of organic carbon in European soils. Most topsoil, which normally contains about half of the organic carbon in mineral soils, is normally stripped off during building activities. As a consequence, the removed soil lose a significant percentage of its organic carbon stock due to enhanced mineralisation and re-use
Reduction in evapotranspiration and vegetation cover, contributing to changing local weather patterns, becoming a key issue in arid climates such as the Mediterranean

## Slide 6: I.3.3 – PERMEABILITY OF LAND
Permeability of land is the capacity to transmit water to the soil. It is a very important issue connected to the water recharging of aquifers and the reduction of effluents.
BACKGROUND

## Slide 7: I.3.3 – PERMEABILITY OF LAND
BACKGROUND
Comparison of benefits and
limitations of most common
Permeable surfaces
in relation
to asphalt
Source: Prokop, G., H. Jobstmann, and A. Schönbauer. 2011. Report on best practices for limiting soil sealing and mitigating its effects. Study contracted by the European Commission, DG Environment, Technical Report-2011-50, Brussels, Belgium, 231 pp

## Slide 8: I.3.3 – PERMEABILITY OF LAND
INDICATOR
Indicator | Unit | Data source
Share of the urban area that is permeable to water | % | Thematic map – Geographic Information System.

## Slide 9: I.3.3 – PERMEABILITY OF LAND
INTENT
Improve the land permeability in order to reduce its impact on the hydrological cycle

## Slide 10: I.3.3 – PERMEABILITY OF LAND
BOUNDARY & SCOPE
The assessment boundary includes the whole neighborhood.
Reference permeability coefficients:
Grass = 1
Gravel = 0.9
Sand = 0.9
Plastic gratings filled with land/grass = 0.8
Concrete gratings leaning on the grass = 0.6
Concrete gratings leaning on gravel = 0.6
Interlocking elements leaning on sand = 0.3
Interlocking elements leaning on gravel = 0.3
Interlocking elements leaning on concrete pavement = 0
Continuous pavements leaning on concrete = 0
Asphalt = 0

## Slide 11: I.3.3 – PERMEABILITY OF LAND
The calculation steps are the following:
Calculate the total surface area of the neighborhood, , [m2]
ASSESSMENT METHOD
Calculate the area of the various surfaces, , with different coverings or occupied by constructions in the urban area (i.e green areas, surfaces paved with asphalt, surfaces occupied by buildings, etc.). Include all the surfaces in the neighborhood so that:

## Slide 12: I.3.3 – PERMEABILITY OF LAND
ASSESSMENT METHOD
Calculate the weighted surface of the neighborhood, considering the permeability coefficients (αi) of the various surfaces(Ai)
Calculate the indicator’s value as the percentage ratio of the of the weighted surfaceof the neighborhood (step 3) to total surface area of the neighborhood (step 1), [%]
%
Notes: MARINA

## Slide 13: I.3.3 – PERMEABILITY OF LAND
Guidelines on best practice to limit mitigate or compensate soil sealing, European Union, 2012
http://ec.europa.eu/environment/soil/pdf/guidelines/pub/soil_en.pdf
REFERENCES and STANDARDS

## Slide 14: I.3.3 – PERMEABILITY OF LAND
EXAMPLE

## Slide 15: I.3.3 – PERMEABILITY OF LAND
In an existing neighborhood, of total surface of 400873m2, the different land covering materials were defined.
Calculate the share of the urban area that is permeable to water

## Slide 16: I.3.3 – PERMEABILITY OF LAND
Available data
Steps 1,2
Materials | Surface area (m2) | Permeability coefficient
Total area | 400873 | 
Buildings | 190765 | 0
Asphalt | 35134 | 0
Tiles on pavements | 13320 | 0
Tiles on squares | 5847 | 0
Interlocking elements leaning on gravel | 2605 | 0.3
Grass | 153202 | 1

## Slide 17: I.3.3 – PERMEABILITY OF LAND
Step 3
Calculate the weighted surface of the neighborhood
(190765*0 + 35134*0+ 13320*0 + 5847*0 + 2605*0.3 + 153202*1) = 153984 m2
Step 4
Calculate the total emissions of CO2 eq. related to building operations, for all the buildings in the neighborhood
Total number of inhabitants
Weighted surface of the neighborhood
153984 m2
400873 m2
38.4 %
100

## Slide 18: I.3.3 – PERMEABILITY OF LAND
EXERCISE

## Slide 19: I.3.3 – PERMEABILITY OF LAND
In an existing neighborhood, shown in the map below, perform measurements of the various land covering materials.
Calculate the share of the urban area that is permeable to water