## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
B.2.4 - TOTAL FINAL ELECTRIC ENERGY CONSUMPTION FOR BUILDING OPERATIONS | 
ISSUE | CATEGORY
B. Energy | B.2. Energy Consumption
See also Β.1.3 of Building Scale

## Slide 3
BACKGROUND
EU Services Sector
EU Residential Sector
Source: Eurostat
ELECTRICITY
48%
Source: Eurostat
ELECTRICITY
24%

## Slide 4: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
Electricity is delivered from the main grid to the building to satisfy uses within the building (heating, cooling, ventilation, domestic hot water, built-in lighting, auxiliaries). The ‘delivered energy’ is generally the one metered by the utilities.

## Slide 5: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INDICATOR
Indicator | Unit | Data source
Aggregated annual total final electric energy consumption per aggregated indoor useful floor area | kWh/m2/year | Metered or estimated data
For the evaluation of the actual performance of the urban area it is preferable to use metered data.
If metered data aren’t available, estimated data shall be used.
Estimated data are used for evaluating retrofit scenarios in planning and decision-making processes
The source of data must always be clearly declared.

## Slide 6: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INTENT
Estimate and minimize electrical energy consumption for all buildings in the neighborhood.
NZEB (EPBD 2010/31/ΕΕ, 2018/844)
Nearly Zero Energy Buildings
All new buildings from 2021
Public new buildings from 2019
Clean Energy for All Europeans
New package of measures for providing the stable legislative framework needed to facilitate the clean energy transition towards the creation of the Energy Union
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 7: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
7
DESCRIPTION
The indicator provides an understanding of the final electricity consumption for all the existing buildings in the neighborhood
Use stage energy consumptions are in general responsible for the majority of life cycle energy use in the case of buildings constructed before the turn of the millennium.

## Slide 8: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In the calculation of the final thermal energy consumption, the following energy uses should be considered:
heating,
cooling,
mechanical ventilation,
domestic hot water,
lighting
auxiliaries
BOUNDARY & SCOPE
The assessment boundary includes all buildings in the neighborhood.
Energy use is referred to as operational energy consumption

## Slide 9: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790

## Slide 10: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Actual annual electricity use of a building
can be monitored. Actual energy use data from at least 12 consecutive months is necessary
can be available from electricity bills or utilities. Average over longer periods (e.g. 3year records)
Utility bills include the total electricity use for the building’s end uses. The main challenge is that the breakdown for the different end-uses (e.g. plug loads, cooking, etc, which are not in scope here) is not evident.
Building energy management system (BEMS) or Building management system (BMS), if available, provide valuable data with a breakdown of the actual electricity use of the different technical installations.

## Slide 11: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Residential
Desegregate electricity use for different end-uses with calibrated building simulations or use survey results from an energy audit.
Source: Eurostat
Commercial

## Slide 12: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The calculation steps are the following:
For each building in the neighborhood collect data for the electricity consumption, in kilowatt hours [kWhe].
For each building in the neighborhood calculate the average annual electricity consumption, for the energy uses taken into account [kWhe/yr]
For each building in the neighborhood calculate the indoor useful area, in square meters [m2]
ASSESSMENT METHOD – USE OF METERED DATA
Can use data from monitoring or from electricity bills or utilities, for a 3years-period. If needed, desegregate collected data for different end-uses with survey results
Highly recommended assessment method!
Data available from energy performance certificate, energy audit report, building/usage permit or other documentation of a building

## Slide 13: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD – USE OF METERED DATA
Highly recommended assessment method!
Sum the average annual electricity consumption of each building up to an aggregated total annual final electrical energy consumption [kWhe/yr]
Sum the indoor useful area of each building in the area up to an aggregated total indoor useful area [m2]
Calculate the indicator’s value as: aggregated total annual final electrical energy consumption (step 4) / aggregated indoor useful area (step 5), [kWhe/m2/yr]

## Slide 14: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The calculation steps are the following:
For each building in the neighborhood calculate the annual electricity use for the energy uses taken into account, in kilowatt hours [kWhe/year].
ASSESSMENT METHOD – USE OF ESTIMATED DATA
Calculations should be over a typical year, according to CEN standards that support EPBD
For each building in the neighborhood calculate the indoor useful area, in square meters [m2]
Sum the annual final electric energy consumption of each building up to an aggregated total annual final electrical energy consumption [kWhe/yr]
Sum the indoor useful area of each building in the area up to an aggregated total indoor useful area [m2]
Calculate the indicator’s value as: aggregated total annual final electrical energy consumption (step 3) / aggregated indoor useful area (step 4), [kWhe/m2/yr]

## Slide 15: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EPBD:2018 - Energy Performance of Buildings Directive, 2018/844/EU. Brussels: European Parliament and the Council of the European Union. https://eur-lex.europa.eu/legal-content/EN/TXT/PDF/?uri=CELEX:32018L0844&from=EL
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
ASHRAE Standard 100: 2018. Energy Efficiency in Existing Buildings. Atlanta: ASHRAE.
ASHRAE GreenGuide (5th ed.), Design, Construction and Operation of Sustainable Buildings, T. Lawrence, A.K. Darwich, J.K. Means, D. Macauley (Editors), 504 p., Atlanta: ASHRAE, 2018. https://www.ashrae.org/technical-resources/bookstore/ashrae-greenguide-the-design-construction-and-operation-of-sustainable-buildings
Handbook of Energy Efficiency in Buildings (1st ed.), Umberto Desideri and Francesco Asdrubali (Editors), 836 p., ISBN 978-0128128176, Butterworth-Heinemann, 2018. https://www.elsevier.com/books/handbook-of-energy-efficiency-in-buildings/desideri/978-0-12-812817-6
REFERENCES and STANDARDS

## Slide 16: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 17: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
ASHRAE Standard 189.1 - Design of High-Performance Green Buildings. https://www.ashrae.org/technical-resources/standards-and-guidelines/read-only-versions-of-ashrae-standards

## Slide 18: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXAMPLE

## Slide 19: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 5 small residential buildings, 15 single houses, one office building and one junior school. All buildings are connected to the main electricity grid and most of them to the central natural gas network.
Available data: The useful internal floor area and the calculated average annual electrical energy consumption of all buildings in the neighborhood
Calculate the total final electrical energy consumption per total
useful internal floor area (i.e. final electrical energy use intensity).

## Slide 20: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
For single houses and residential buildings the internal floor area and the annual electrical energy consumption are given as a total aggreggated value for all the buildings within the category
Available data
 | Useful internal floor area (m2) | Calculated annual electrical energy consumption (kWhe) | HVAC systems (heating, cooling, domestic hot water)
Office | 1045 | 125086 | Central HP for heating, cooling and domestic hot water.
School | 1847 | 51347 | Central natural gas boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water.
Single houses (15) | 1805 | 92596 | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling.
Residential buildings (5) | 3322 | 148161 | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling
Steps 1 -2

## Slide 21: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 3
Calculate the total annual elecgrical energy consumption for all the buildings in the neighborhood
(125086 + 51347 + 92596 + 148161) = 41719 kWhe
Step 4
Calculate the total indoor useful floor area for all the buildings in the neighborhood
(1045 + 1847 + 1805 + 3322) = 8109 m2
Step 5
Calculate the annual total final electrical energy consumption per total useful internal floor area
Total Indoor Useful Floor Area
417.19 kWhe

=
Total Electrical energy
8109 m2
51.5 kWhe/m2/y

## Slide 22: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXERCISE

## Slide 23: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 22 single houses, one kindergarten and one junior school. All buildings are connected to the main electricity grid and all of them are equipped with central boilers (natural gas or fuel oil).
Available data: The useful internal floor area and the calculated annual electrical energy consumption of all buildings in the neighborhood
Calculate the annual total final electrical energy consumption per total useful internal floor area (i.e. final electrical energy use intensity).

## Slide 24: B.2.4 - TOTAL FINAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Available data
 | Useful internal floor area (m2) | Calculated annual electrical energy consumption (kWhe) | HVAC systems (heating, cooling, domestic hot water)
Kindergarten | 456 | 6567 | Central fuel oil boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water.
School | 2151 | 86255 | Central natural gas boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water
Single houses (22) | 2530 | 122199 | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling.
For single houses the internal floor area and the annual electrical energy consumption are given as a total aggreggated value for all the buildings