## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS | 
ISSUE | CATEGORY
B. Energy | B.2. Energy Consumption
See also Β.1.1 of Building Scale

## Slide 3: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
EU Primary Products
EU Imports
Source: Eurostat
The extraction of energy products from natural sources to a usable form. It occurs within the territory under consideration
Source: Eurostat
Imports cover the amount of energy produced outside and brought into the considered territory for consumption

## Slide 4: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
Primary energy is defined by Article 2(5) of the Energy Performance of Buildings Directive (EPBD) as 'the energy that has not undergone any conversion in the transformation process, calculated by energy carrier using a primary energy factor.
It is the energy that is required to generate the electricity, heating and cooling used by a building.

## Slide 5: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
5
BACKGROUND
Thermal and
electrical energy
Coal, Peat coal
Oil
Gas
Nuclear en.
Sun
Wind
Water
Geothermal en.
Wood …
Electrical energy
District heat
Petroleum products
Gas
Wood pellets
Briquetts
Coke …
Primary Energy
Secondary Energy
Primary Energy
Energy DELIVERED to Building
Energy Losses
Conversion
Storage
Distribution
Building Energy Needs
Heating
Cooling
Domestic hot water
Ventilation
Auxiliaries
Lighting
Secondary Energy
Energy Losses
Conversion
Storage
Distribution
Energy Losses
Conversion
Storage
Distribution

## Slide 6: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INDICATOR
Indicator | Unit | Data source
Aggregated annual total primary energy consumption per aggregated indoor useful floor area | kWh/m2/year | Calculations

## Slide 7: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INTENT
Estimate and minimize primary energy consumption for all buildings in the neighbourhood.
NZEB (EPBD 2010/31/ΕΕ, 2018/844)
Nearly Zero Energy Buildings
All new buildings from 2021
Public new buildings from 2019
Clean Energy for All Europeans
New package of measures for providing the stable legislative framework needed to facilitate the clean energy transition towards the creation of the Energy Union
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 8: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790

## Slide 9: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BOUNDARY & SCOPE
The assessment boundary includes all buildings in the neighborhood.
In the calculation of the primary energy consumption, the following energy uses should be considered:
heating,
cooling,
mechanical ventilation,
domestic hot water,
lighting
auxiliaries
Energy use is referred to as operational energy consumption

## Slide 10: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD - Primary Energy Conversion Factors
Primary energy consumed by a building as measured at the building, converted using primary energy conversion factors
Can use official national/local emission factors, if appropriate

## Slide 11: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The calculation steps are the following:
For each building in the neighborhood calculate the average annual thermal energy consumption per fuel or district heat/cold, for the energy uses taken into account (see B.2.1) over a typical year according to CEN standards that support EPBD, in kilowatt hours (kWhth/y)
For each building in the neighborhood calculate the average annual electrical energy consumption (see B.1.3) over a typical year according to CEN standards that support EPBD, in kilowatt hours (kWhe/y)
Sum the average annual thermal energy consumption per fuel or district heat/cold for all the buildings in the neighborhood
Sum the average annual electrical energy consumption for all the buildings in the neighborhood
ASSESSMENT METHOD

## Slide 12: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Use national conversion factors per fuel, district heat/cold and electricity to estimate the total primary energy consumption (PEU) for all buildings of the neighborhood

## Slide 13: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
where
EUth,i = annual thermal energy consumption of i-th fuel (kWhth/y) delivered to all buildings of the neighborhood
Fi = national conversion factor of the i-th fuel
EUd = annual thermal energy consumption (kWhth/y) used by a district heating/cooling network to generate the heat/cold delivered to all buildings of the neighborhood
Fd = national conversion factor for the fuel used by a district heating/cooling network
EUe = annual electrical energy consumption (kWhe/y) for the electricity delivered to all buildings of the neighborhood
Fe = national conversion factor of electricity from the main grid (depends on energy mix of main grid)

## Slide 14: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
For each building in the neighborhood calculate the indoor useful area, in square meters [m2]
Sum the indoor useful area of each building in the area up to an aggregated total indoor useful area, in square meters [m2]
Calculate the indicator’s value as: total primary energy consumption (PEU) (step 5) / aggregated indoor useful area (step 7), [kWh/m2/year]
ASSESSMENT METHOD – USE OF ESTIMATED DATA

## Slide 15: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
EPBD:2018 - Energy Performance of Buildings Directive, 2018/844/EU. Brussels: European Parliament and the Council of the European Union
EN ISO 13790 Energy performance of buildings – Calculation of energy use for space heating and cooling
EN 15316-2-1 Space heating emission systems
EN 15316-2-3 Space heating distribution systems
EN 15316-3-1 Domestic hot water systems, characterisation of needs
EN 15316-3-2 Domestic hot water systems, distribution
EN 15316-3-3 Domestic hot water systems, generation
EN 15316-4-1 Space heating generation systems, combustion systems (boilers)
EN 15316-4-2 Space heating generation systems, heat pump systems
EN 15316-4-3 Space heating generation systems, thermal solar systems
Notes: MARINA

## Slide 16: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
EN 15316-4-4 Space heating generation systems, building-integrated cogeneration systems
EN 15316-4-5 Space heating generation systems, the performance and quality of district heating and large volume systems
EN 15316-4-7 Space heating generation systems, biomass combustion systems
EN 15603 Energy performance of buildings – Overall energy use and definition of energy ratings
Level(s) Part 1-2 – Beta version. Brussels: European Commission
https://environment.ec.europa.eu/topics/circular-economy/levels_en
Notes: MARINA

## Slide 17: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 18: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXAMPLE

## Slide 19: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 5 small residential buildings, 15 single houses, one office building and one junior school. All buildings are connected to the main electricity grid and most of them to the central natural gas network.
Available data: The useful internal floor area and the calculated annual thermal and electrical energy consumption of all buildings in the neighborhood
Calculate the annual total primary energy consumption per total
useful internal floor area (i.e. primary energy use intensity).

## Slide 20: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
For single houses and residential buildings the internal floor area,the annual thermal and electrical energy consumption are given as a total aggreggated value for all the buildings within the category
Available data
 | Useful internal floor area (m2) | Calculated annual thermal energy consumption (kWhth) | Calculated annual electrical energy consumption (kWhth) | HVAC systems (heating, cooling, domestic hot water)
Office | 1045 |  | 125086 | Central HP for heating, cooling and domestic hot water.
School | 1847 | 59452 | 51347 | Central natural gas boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water.
Single houses (15) | 1805 | 202521 | 92596 | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling.
Residential buildings (5) | 3322 | 291007 | 148161 | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling
Steps 1, 2, 6

## Slide 21: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 3
Calculate the average annual thermal energy consumption per fuel or district heat/cold for all the buildings in the neighborhood
Natural Gas
(0+59452+202521+291007) = 552980 kWhth
Step 4
Calculate the average annual electrical consumption for all the buildings in the neighborhood
Electricity
(125086 + 51347 + 92596 + 148161) = 417190 kWhe

## Slide 22: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 5
Calculate the average annual thermal energy consumption per fuel or district heat/cold for all the buildings in the neighborhood
National conversion factor
X
=
Fuels –
Natural Gas
+
National conversion factor
X
Electricity
Total primary energy consumption
417190 kWhe 2.9
X
552980 kWhth 1.05
X
1790480
kWh

## Slide 23: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 7
Step 8
Calculate the total indoor useful floor area for all the buildings in the neighborhood
(1045+1847+1805+3322) = 8109 m2
Calculate the annual primary energy demand per total useful internal floor area
Total Indoor Useful Floor Area
1790480 kWh

=
Primary energy
8109 m2
221 kWh/m2/y

## Slide 24: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXERCISE

## Slide 25: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 22 single houses, one kindergarten and one junior school. All buildings are connected to the main electricity grid and all of them are equipped with central boilers (natural gas or fuel oil).
Available data: The useful internal floor area and the calculated annual thermal energy consumption of all buildings in the neighborhood
Calculate the annual total primary energy consumption per total
useful internal floor area (i.e. primary energy use intensity).

## Slide 26: B.2.7 – TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Available data
 | Useful internal floor area (m2) | Calculated annual electricity consumption (kWhe) | Calculated annual thermal energy consumption (kWhth) | HVAC systems (heating, cooling, domestic hot water)
Kindergarten | 456 | 6.567 | 52.470 (fuel oil ) | Central fuel oil boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water.
School | 2.151 | 86.255 | 112.929 (natural gas) | Central natural gas boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water
Single houses (22) | 2.530 | 122.199 | 311.443 (natural gas) | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling.
For single houses the internal floor area, the annual electricity and thermal energy consumption are given as a total aggreggated value for all the buildings