## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
See also Β.1.4 of Building Scale
B.3.1 - SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDINGS OPERATION | 
ISSUE | CATEGORY
B. Energy | B.3 Renewable energy
Solar energy Biomass energy Thermal heat from the air-ground-water Geothermal energy

## Slide 3
BACKGROUND (All RES for all uses)
EU Services Sector
EU Residential Sector
Source: Eurostat
RES
16%
Source: Eurostat
RES
3%

## Slide 4: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
The annual thermal energy produced & used on-site from renewable sources is determined in relation to each energy carrier (fuel) that may replace.
For example,
Use solar thermal collectors to produce hot water that is then used for space heating instead of an oil-fired boiler.

## Slide 5: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND – Thermal solar systems
Common practice
DHW: 1 m2 of flat plate collector per person
Space heating: 1 m2 of flat plate collector for a thermal load of 700 W
Domestic Hot Water (DHW)
Space Heating
Solar COMBI Systems
Solar Collectors
Heat Storage
Heat Distribution
Heat Dissipation
Auxiliary (backup)

## Slide 6: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Europe: 5% of total thermal solar systems
Austria (40%), Switzerland (35%), Netherlands (20%), Denmark (15%), France (5%)
National Regulations in many European countries there are minimum requirements in new buildings, for the use of solar collectors for domestic hot water (DWH) and space heating (SH)
BACKGROUND – Thermal solar systems
Domestic Hot Water (DHW)
Space Heating
Solar COMBI Systems
Greece: 60% of DWH
Ireland: 10kWh/m2 floor area from RES
Portugal: 1m2 of solar collector/user for DWH
Spain: 30-70% of DWH
Switzerland: 20% of SH

## Slide 7: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
Common practice
Solar collector area: 3.6 m2/kWc
Auxiliary energy use: 0.255 kWhe/kWhc
Solar Collectors
Heat Storage
Heat Distribution
Heat-driven Cooling Unit
Cold Storage (optional)
Air Conditioning System
Cold Distribution
Auxiliary (backup)
+
COMBI-PLUS
Solar Cooling
DHW
Space Heating
Solar COMBI Systems

## Slide 8: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The actual thermal energy produced & used on-site from renewable sources or delivered to a building can be monitored. If available, BEMS or BMS can provide valuable data with a breakdown of the actual thermal energy use of the different technical installations.
Building energy management system (BEMS) control & monitor energy use of the various technical installations for heating, cooling, ventilation, lighting, plug loads etc, and indoor environmental conditions.
Building management system (BMS) may additionally include other functions (e.g. safety, access, lifts, fire security).
Actual energy use data from at least 12 consecutive months is necessary.
It is preferable to consider longer records (e.g. three year data) in order to remove the effects of varying weather conditions and average out other inherent fluctuations in the building occupancy.
BACKGROUND – BEMS/BMS

## Slide 9: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INDICATOR
Indicator | Unit | Data source
Total consumption of final thermal energy generated from renewable sources on-site divided by total final thermal energy consumption | % | Estimated or metered data
For the evaluation of the actual performance of the urban area it is preferable to use metered data.
If metered data aren’t available, estimated data shall be used.
Estimated data are used for evaluating retrofit scenarios in planning and decision-making processes
The source of data must always be clearly declared.

## Slide 10: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INTENT
Maximize the use of renewable energy sources.
Ground source
Water source
Wood chips
Wood pellets
RED: Renewable Energy Directive 2018/2001
New package of 8 different legislative proposals for
«Clean Energy for All Europeans package»
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 11: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
11
DESCRIPTION
The indicator assesses the share of renewable thermal energy in final thermal energy consumptions and, by implication, the degree to which renewable fuels have substituted fossil and/or nuclear fuels and therefore contributed to the decarbonisation of the Mediterranean area economy.
It also shows what is the progress towards Europe 2020 and 2030 target for renewable energies.

## Slide 12: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790
Glazed flat plate
(60-90°C)
Evacuated tube
(80-120°C)
Unglazed
(25-50oC)
Concentrating
(95-160°C)
PV driven
Water source HP
(Closed loop)
PV driven
Ground source HP
(horizontal loop)
PV driven
Air source HP
(High SSER)
Wood pellets
Wood chips

## Slide 13: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In the calculation of the final thermal energy consumption, the following energy uses should be considered:
heating
cooling
mechanical ventilation
domestic hot water
BOUNDARY & SCOPE
The assessment boundary includes all buildings in the neighborhood.
Energy use is referred to as operational energy consumption

## Slide 14: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BOUNDARY & SCOPE
According to the Renewables Energy Directive (RED 2018), energy from renewable sources means energy from renewable non-fossil sources, namely wind, solar, aerothermal, geothermal, hydrothermal and ocean energy, hydropower, biomass, landfill gas, sewage treatment plant gas and biogases.
Heat pumps enabling the use of aerothermal, geothermal or hydrothermal heat at a useful temperature level need electricity or other auxiliary energy to function. The energy used to drive heat pumps should therefore be deducted from the total usable heat. Only heat pumps for which SPF > 1,15 * 1/η shall be taken into account.

## Slide 15: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The calculation steps are the following:
For each building in the neighborhood calculate the average annual thermal energy produced & used on-site from renewable sources (e.g. solar collectors, PV driven HPs, biomass) to cover the demand for the energy uses taken into account, using a 3year average value from monitored data(if available), or calculations (as described in B.1.4 – Energy from renewable sources in total thermal energy consumption)
For each building in the neighborhood calculate the average annual thermal energy delivered (e.g. oil, natural gas, district heating) to the building to cover the energy uses taken into account, from monitored / metered data or calculations (as described in B.1.2 - Thermal energy consumption)
ASSESSMENT METHOD

## Slide 16: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Sum the annual thermal energy produced & used on-site from renewable sources of each building up to an aggregated total thermal energy from RES, [kWhth,RES/yr]
Sum the annual thermal energy of each building up to an aggregated total thermal energy (RES & conventional), [kWhth/yr]
Calculate the indicator’s value as the percentage ratio of the amount of total thermal energy from RES (step 3) to the total final thermal energy (RES & conventional) (step 4), [%]

## Slide 17: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
RED 2018. Directive (EU) 2018/2001 of the European Parliament and of the Council of 11 December 2018 on the promotion of the use of energy from renewable sources (recast). Brussels: European Commission. http://data.europa.eu/eli/dir/2018/2001/oj
2013/114/EU: Commission Decision of 1 March 2013
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en

## Slide 18: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 19: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
Solar Engineering of Thermal Processes (4th ed.), John A. Duffie, William A. Beckman, 944 p., ISBN: 978-0-470-87366-3, Wiley, 2013. https://www.wiley.com/en-us/Solar+Engineering+of+Thermal+Processes%2C+4th+Edition-p-9780470873663
Solar Cooling Handbook, A Gudie to Solar Assisted Cooling and Dehumidification Processes, Hans-Martin Henning, Mario Motta, Daniel Mugnier (Editors), 368 p., ISBN 978-3990434383, Ambra Verlag, 2013.
ASHRAE GreenGuide (5th ed.), Design, Construction and Operation of Sustainable Buildings, T. Lawrence, A.K. Darwich, J.K. Means, D. Macauley (Editors), 504 p., Atlanta: ASHRAE, 2018. https://www.ashrae.org/technical-resources/bookstore/ashrae-greenguide-the-design-construction-and-operation-of-sustainable-buildings
Handbook of Energy Efficiency in Buildings (1st ed.), Umberto Desideri and Francesco Asdrubali (Editors), 836 p., ISBN 978-0128128176, Butterworth-Heinemann, 2018. https://www.elsevier.com/books/handbook-of-energy-efficiency-in-buildings/desideri/978-0-12-812817-6

## Slide 20: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXAMPLE

## Slide 21: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 20 single houses, one sports hall and one junior school. All buildings are connected to the central natural gas network. The sports hall and some of the houses have solar collectors for DHW, while the school has a central biomass boiler for space heating.
Available data: The total renewable energy on-site and the total thermal energy consumption of all buildings in the neighborhood
Calculate the percentage ratio of renewable energy on-site in total
final thermal energy consumption for building operations.

## Slide 22: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
For single houses the annual thermal energy consumption and the thermal energy from RES are given as a total aggreggated value for all the buildings within the category
Available data
 | Calculated annual thermal energy consumption (kWhth) | Calculated annual thermal energy consumption from RES (kWhth,RES) | HVAC systems (heating, cooling, domestic hot water)
Sports hall | 108100 | 30900 | Central natural gas boiler for heating. Central HP for cooling. Solar collectors for domestic hot water.
School |  | 46432 | Central biomass boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water.
Single houses (20) | 295324 | 21411 | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling. Solar collectors for domestic hot water.
Steps 1 -2

## Slide 23: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 3
Calculate total thermal energy produced & used on-site from renewable sources for all the buildings in the neighborhood
(30900+46432+21411) = 98743 kWhth,RES
Step 4
Calculate the total annual final thermal energy consumption for all the buildings in the neighborhood
(108100+0+295324) = 403324 kWhth
Step 5
Calculate the total annual total final thermal energy (RES & conventional) for all the buildings in the neighborhood
(98743 + 403324) = 502067 kWh

## Slide 24: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 6
Calculate the percentage ratio of the total renewable energy on-site to the total final thermal energy consumption from RES and conventional
98743 kWhth,RES
Total Thermal Energy (RES)
502067 kWh
19.7 %
Total Thermal Energy (RES & Conventional)
100

## Slide 25: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXERCISE

## Slide 26: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 22 single houses, one kindergarten and one junior school. All buildings are equipped with central boilers (natural gas or fuel oil). Domestic hot water is covered by solar collectors in some houses, in the kindergarten and in the school.
Available data: The total renewable energy on-site and the total thermal energy consumption of all buildings in the neighborhood
Calculate the percentage ratio of renewable energy on-site in total
final thermal energy consumption for buildings operation.

## Slide 27: B.3.1 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL FINAL THERMAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Available data
 | Calculated annual thermal energy consumption (kWhth) | Calculated annual thermal energy consumption from RES (kWhth,RES) | HVAC systems (heating, cooling, domestic hot water)
Kindergarten | 52470 (fuel oil) | 6297 | Central fuel oil boiler for space heating. Local HP for space cooling. Solar collectors for domestic hot water.
School | 112929 (natural gas) | 4616 | Central natural gas boiler for space heating. Local HP for space cooling. Solar collectors for domestic hot water
Single houses (22) | 382765 (fuel oil & natural gas) | 32621 | Central boiler (natural gas & fuel oil) for space heating and domestic hot water. Local HP for space cooling. Solar collectors for domestic hot water
For single houses the annual thermal energy consumption and the thermal energy from RES are given as a total aggreggated value for all the buildings within the category