## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
See also Β.1.5 of Building Scale
B.3.4 - SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDINGS OPERATION | 
ISSUE | CATEGORY
B. Energy | B.3 Renewable energy
RED: Renewable Energy Directive 2018/2001
New package of 8 different legislative proposals for
«Clean Energy for All Europeans package»
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 3: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND (All RES for all uses)
EU Services Sector
EU Residential Sector
Source: Eurostat
RES
16%
Source: Eurostat
RES
3%

## Slide 4: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
Source: Eurostat
Renewables
30%

## Slide 5: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND
Performance of RES depends on type of system, efficiency, location (e.g. solar availability ) etc
For example, electricity production from PVs
Annual average output
Greece: 1100 to 1500 kWh/kWp/year
Thessaloniki: 1150 to 1250 kWhe/kWp/year
Athens: 1300 to 1400 kWhe/kWp/year
Crete: 1350 to 1500 kWhe/kWp/year

## Slide 6: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INDICATOR
Indicator | Unit | Data source
Total consumption of final electrical energy generated from renewable sources on-site divided by total final electrical energy consumption | % | Estimated or metered data
For the evaluation of the actual performance of the urban area it is preferable to use metered data.
If metered data aren’t available, estimated data shall be used.
Estimated data are used for evaluating retrofit scenarios in planning and decision-making processes
The source of data must always be clearly declared.

## Slide 7: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INTENT
Maximize the use of renewable energy sources.

## Slide 8: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
8
DESCRIPTION
The indicator assesses the share of renewable electrical energy in final electrical energy consumptions and, by implication, the degree to which renewable fuels have substituted fossil and/or nuclear fuels and therefore contributed to the decarbonisation of the Mediterranean area economy
It also shows what is the progress towards Europe 2020 and 2030 target for renewable energies.

## Slide 9: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790

## Slide 10: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In the calculation of the final thermal energy consumption, the following energy uses should be considered:
heating,
cooling,
ventilation,
domestic hot water,
lighting,
auxiliaries
BOUNDARY & SCOPE
The assessment boundary includes all buildings in the neighborhood.
Energy use is referred to as operational energy consumption

## Slide 11: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BOUNDARY & SCOPE
According to the Renewables Energy Directive (RED 2018), energy from renewable sources means energy from renewable non-fossil sources, namely wind, solar, aerothermal, geothermal, hydrothermal and ocean energy, hydropower, biomass, landfill gas, sewage treatment plant gas and biogases.
Heat pumps enabling the use of aerothermal, geothermal or hydrothermal heat at a useful temperature level need electricity or other auxiliary energy to function. The energy used to drive heat pumps should therefore be deducted from the total usable heat. Only heat pumps for which SPF > 1,15 * 1/η shall be taken into account.

## Slide 12: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The actual electricity produced & used on-site from renewable sources (e.g. solar using PV, wind using turbines) is usually monitored (measured) by dedicated power or smart meters.
Actual energy use data from at least 12 consecutive months is necessary.
It is preferable to average over longer records (e.g. three year data) in order to remove the effects of varying weather conditions and average out other inherent fluctuations in the building occupancy.
From Main Grid
From PV

## Slide 13: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The actual electricity use from the main power grid can also be monitored. If available, BEMS or BMS can provide valuable data with a breakdown of the actual electricity use of the different technical installations.
Building energy management system (BEMS) control & monitor energy use of the various technical installations and indoor environmental conditions.
Building management system (BMS) may additionally include other functions (e.g. safety, access, lifts, fire security).
The actual annual electricity use of a building is also available from electricity bills or utilities. Average over longer periods (e.g. 3year records).
Utility bills include the total electricity demand for the building’s technical services (in scope here) and plug loads, cooking etc (not in scope here).
Desegregate electricity demand for different end-uses with calibrated building simulations or use survey results from an energy audit.
For more information see indicator B.1.5

## Slide 14: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The calculation steps are the following:
For each building in the neighborhood calculate the average annual electricity produced & used on-site from renewable sources (e.g. solar using PV, wind using turbines) to cover the demand for the energy uses taken into account, using a 3year average value (if available), from monitored data or calculations (as described in B.1.5 – Energy from renewable sources in total electrical energy consumption)
ASSESSMENT METHOD
For each building in the neighborhood calculate the average annual electricity delivered to the building from the main power grid, to cover the energy uses taken into account, from monitored / metered data or calculations (as described in B.1.3 - Electrical energy consumption)

## Slide 15: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Sum the annual electricity produced & used on-site from renewable sources of each building up to an aggregated total electrical energy from RES [kWhe,RES/yr]
Sum the annual electrical energy consumption of each building up to an aggregated total electrical energy consumption (RES & grid), [kWhe/yr]
Calculate the indicator’s value as the percentage ratio of the amount of total electrical energy from RES (step 3) to the total electrical energy consumption (RES & grid) (step 4), [%]

## Slide 16: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
RED 2018. Directive (EU) 2018/2001 of the European Parliament and of the Council of 11 December 2018 on the promotion of the use of energy from renewable sources (recast). Brussels: European Commission. http://data.europa.eu/eli/dir/2018/2001/oj
2013/114/EU: Commission Decision of 1 March 2013
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en

## Slide 17: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 18: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
Solar Cooling Handbook, A Gudie to Solar Assisted Cooling and Dehumidification Processes, Hans-Martin Henning, Mario Motta, Daniel Mugnier (Editors), 368 p., ISBN 978-3990434383, Ambra Verlag, 2013.
ASHRAE GreenGuide (5th ed.), Design, Construction and Operation of Sustainable Buildings, T. Lawrence, A.K. Darwich, J.K. Means, D. Macauley (Editors), 504 p., Atlanta: ASHRAE, 2018. https://www.ashrae.org/technical-resources/bookstore/ashrae-greenguide-the-design-construction-and-operation-of-sustainable-buildings
Handbook of Energy Efficiency in Buildings (1st ed.), Umberto Desideri and Francesco Asdrubali (Editors), 836 p., ISBN 978-0128128176, Butterworth-Heinemann, 2018. https://www.elsevier.com/books/handbook-of-energy-efficiency-in-buildings/desideri/978-0-12-812817-6

## Slide 19: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXAMPLE

## Slide 20: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 20 single houses, one sports hall and one junior school. All buildings are connected to the main electricity grid. The sports hall has PV panels integrated on its envelope to cover partially cooling and lighting demands.
Available data: The total renewable energy on-site and the total electrical energy consumption of all buildings in the neighborhood
Calculate the percentage ratio of renewable energy on-site in total
electrical energy consumption for buildings operation.

## Slide 21: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
For single houses the annual electrical energy consumption and the electrical energy from RES are given as a total aggreggated value for all the buildings within the category
Available data
 | Calculated annual electrical energy consumption from grid (kWhe) | Calculated annual electrical energy consumption from RES (kWhth,RES) | HVAC systems (heating, cooling, domestic hot water)
Sports hall | 45564 | 12605 | Central natural gas boiler for heating. Central HP for cooling. Solar collectors for domestic hot water.
School | 51347 |  | Central biomass boiler for space heating. Local HP for space cooling. Electric heaters for domestic hot water.
Single houses (20) | 128466 |  | Central natural gas boiler for space heating and domestic hot water. Local HP for space cooling. Solar collectors for domestic hot water.
Steps 1 -2

## Slide 22: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 3
Calculate total electrical energy produced & used on-site from renewable sources for all the buildings in the neighborhood
(12605+0+0) = 12605 kWhe,RES
Step 4
Calculate the total annual electrical energy consumption from the grid for all the buildings in the neighborhood
(45564+51347+128466) = 225377 kWhe
Step 5
Calculate the annual total electrical energy consumption (RES & Grid)
(225377 + 12605) = 237982 kWh

## Slide 23: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 6
Calculate the percentage ratio of electrical energy consumption from RES to the total electrical energy from RES and grid
12605 kWhe,RES
Total Electrical Energy from RES
237982 kWh
5.6 %
Total Electrical Energy (RES & Grid)
100

## Slide 24: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXERCISE

## Slide 25: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 22 single houses, one kindergarten and one junior school. All buildings are connected to the main electricity grid. The kindergarten and some of the houses have PV panels integrated on their envelope to cover partially cooling and lighting demands.
Available data: The total renewable energy on-site and the total electrical energy consumption of all buildings in the neighborhood
Calculate the percentage ratio of renewable energy on-site in total
electrical energy consumption for building operations.

## Slide 26: B.3.4 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL ELECTRICAL ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Available data
 | Calculated annual electrical energy consumption from grid (kWhe) | Calculated annual electrical energy consumption from RES (kWhe,RES) | HVAC systems (heating, cooling, domestic hot water)
Kindergarten | 45564 | 12600 | Central fuel oil boiler for space heating. Local HP for space cooling. Solar collectors for domestic hot water. PV panels (cooling and lighting)
School | 51347 |  | Central natural gas boiler for space heating. Local HP for space cooling. Solar collectors for domestic hot water
Single houses (22) | 128466 | 66230 | Central boiler (natural gas & fuel oil) for space heating and domestic hot water. Local HP for space cooling. Solar collectors for domestic hot water. PV panels
For single houses the annual electrical energy consumption and the electrical energy from RES are given as a total aggreggated value for all the buildings within the category