## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDINGS OPERATION | 
ISSUE | CATEGORY
B. Energy | B.3 Renewable energy
RED: Renewable Energy Directive 2009/28
New package of 8 different legislative proposals for
«Clean Energy for All Europeans package»
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 3: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BACKGROUND (All RES for all uses)
EU Primary Products
EU Imports
Source: Eurostat
The extraction of energy products from natural sources to a usable form. It occurs within the territory under consideration
Source: Eurostat
Imports cover the amount of energy produced outside and brought into the considered territory for consumption

## Slide 4: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INDICATOR
Indicator | Unit | Data source
Total consumption of primary energy generated from renewable sources on-site divided by total primary energy consumption | % | Estimated or metered data
For the evaluation of the actual performance of the urban area it is preferable to use metered data.
If metered data aren’t available, estimated data shall be used.
Estimated data are used for evaluating retrofit scenarios in planning and decision-making processes
The source of data must always be clearly declared.

## Slide 5: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
INTENT
Maximize the use of renewable energy sources.

## Slide 6: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
DESCRIPTION
The indicator assesses the share of renewable energy in primary energy consumption of the buildings and, by implication, the degree to which renewable fuels have substituted fossil and/or nuclear fuels and therefore contributed to the decarbonisation of the Mediterranean area economy
It also shows what is the progress towards Europe 2020 and 2030 target for renewable energies.

## Slide 7: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT
The calculation method is provided by the CEN standards series that support implementation of EPBD across the EU
The CEN standards series that currently forms the basis for most of national calculation methods includes EN 15603 that collates the results from EN ISO 13790

## Slide 8: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In the calculation of the final thermal energy consumption, the following energy uses should be considered:
heating,
cooling,
ventilation,
domestic hot water,
lighting,
auxiliaries
BOUNDARY & SCOPE
The assessment boundary includes all buildings in the neighborhood.
Energy use is referred to as operational energy consumption

## Slide 9: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
BOUNDARY & SCOPE
According to the Renewables Energy Directive (RED 2018), energy from renewable sources means energy from renewable non-fossil sources, namely wind, solar, aerothermal, geothermal, hydrothermal and ocean energy, hydropower, biomass, landfill gas, sewage treatment plant gas and biogases.
Heat pumps enabling the use of aerothermal, geothermal or hydrothermal heat at a useful temperature level need electricity or other auxiliary energy to function. The energy used to drive heat pumps should therefore be deducted from the total usable heat. Only heat pumps for which SPF > 1,15 * 1/η shall be taken into account.

## Slide 10: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The actual electricity produced & used on-site from renewable sources (e.g. solar using PV, wind using turbines) is usually monitored (measured) by dedicated power or smart meters.
Actual energy use data from at least 12 consecutive months is necessary.
It is preferable to average over longer records (e.g. three year data) in order to remove the effects of varying weather conditions and average out other inherent fluctuations in the building occupancy.
From Main Grid
From PV

## Slide 11: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
The actual electricity use from the main power grid can also be monitored. If available, BEMS or BMS can provide valuable data with a breakdown of the actual electricity use of the different technical installations.
Building energy management system (BEMS) control & monitor energy use of the various technical installations and indoor environmental conditions.
Building management system (BMS) may additionally include other functions (e.g. safety, access, lifts, fire security).
The actual annual electricity use of a building is also available from electricity bills or utilities. Average over longer periods (e.g. 3year records).
Utility bills include the total electricity demand for the building’s technical services (in scope here) and plug loads, cooking etc (not in scope here).
Desegregate electricity demand for different end-uses with calibrated building simulations or use survey results from an energy audit.
For more information see indicator B.1.5

## Slide 12: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
The calculation steps are the following:
For each building in the neighborhood (residential and non-residential) collect /calculate :
the annual total renewable thermal energy produced on site, [kWh/a] (as described in B.1.4 – Energy from renewable sources in total thermal energy consumption)
the annual total renewable electrical energy produced on site, [kWh/a] (as described in B.1.5 – Energy from renewable sources in total electrical energy consumption)
the annual final thermal energy consumption for building operations for each energy carrier separately, [kWh/a] (as described in B.1.2 - Thermal energy consumption)
the annual final electrical energy consumption for building operations from the gird, [kWh/a] (as described in B.1.3 - Electrical energy consumption)
ASSESSMENT METHOD

## Slide 13: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
For all buildings in the neighborhood sum up:
a) the annual total renewable thermal energy per energy carrier produced on site, to calculate the aggregated renewable thermal energy per energy carrier produced on site, ERen,th, [kWh/a]
b) the annual total renewable electrical energy produced on site, to calculate the aggregated renewable electrical energy produced on site, ERen,el [kWh/a]
c) the annual final thermal energy consumption for building operations for each energy carrier, to calculate the aggregated thermal energy consumption per energy carrier, Eth [kWh/a]
d) the annual final electrical energy consumption, to calculate the aggregated electrical energy consumption, Eel [kWh/a]

## Slide 14: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Calculate the total primary energy renewable thermal energy consumption, 𝐸𝑝,Ren,th, summing up the aggregated renewable thermal energy per energy carrier (i) multiplied with the appropriate primary energy factor
Calculate the total primary renewable electrical energy consumption, 𝐸𝑝,Ren,el, summing up the aggregated electrical energy consumption multiplied with the appropriate primary energy factor
Calculate the total primary thermal energy consumption, 𝐸𝑝,th, summing up the aggregated thermal energy consumption per energy carrier (i) multiplied with the appropriate primary energy factor
Calculate the total primary electrical energy consumption, 𝐸𝑝,el, summing up the aggregated electrical energy consumption multiplied with the appropriate primary energy factor

## Slide 15: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
ASSESSMENT METHOD
Calculate the total annual primary energy from renewables, 𝐸𝑝,Ren, adding the total primary energy renewable thermal energy consumption and the total primary renewable electrical energy consumption
Calculate the total annual primary energy consumption 𝐸𝑝, adding the total primary thermal energy consumption and the total primary electrical energy consumption
Calculate the indicator’s value as the percentage ratio of total annual primary energy from on-site renewables to the sum of total annual primary energy consumption the total annual primary energy consumption from renewables
%

## Slide 16: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
RED 2018. Directive (EU) 2018/2001 of the European Parliament and of the Council of 11 December 2018 on the promotion of the use of energy from renewable sources (recast). Brussels: European Commission. http://data.europa.eu/eli/dir/2018/2001/oj
2013/114/EU: Commission Decision of 1 March 2013
EN 15603:2008 - Energy performance of buildings. Overall energy use and definition of energy ratings. Brussels: European Committee for Standardization.
EN 13790:2008 - Energy performance of buildings. Calculation of energy use for space heating and cooling. Brussels: European Committee for Standardization.
Level(s) Part 1-2 – Beta version. Brussels: European Commission. https://environment.ec.europa.eu/topics/circular-economy/levels_en

## Slide 17: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans

## Slide 18: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
REFERENCES and STANDARDS
Solar Engineering of Thermal Processes (4th ed.), John A. Duffie, William A. Beckman, 944 p., ISBN: 978-0-470-87366-3, Wiley, 2013. https://www.wiley.com/en-us/Solar+Engineering+of+Thermal+Processes%2C+4th+Edition-p-9780470873663
Solar Cooling Handbook, A Gudie to Solar Assisted Cooling and Dehumidification Processes, Hans-Martin Henning, Mario Motta, Daniel Mugnier (Editors), 368 p., ISBN 978-3990434383, Ambra Verlag, 2013.
ASHRAE GreenGuide (5th ed.), Design, Construction and Operation of Sustainable Buildings, T. Lawrence, A.K. Darwich, J.K. Means, D. Macauley (Editors), 504 p., Atlanta: ASHRAE, 2018. https://www.ashrae.org/technical-resources/bookstore/ashrae-greenguide-the-design-construction-and-operation-of-sustainable-buildings
Handbook of Energy Efficiency in Buildings (1st ed.), Umberto Desideri and Francesco Asdrubali (Editors), 836 p., ISBN 978-0128128176, Butterworth-Heinemann, 2018. https://www.elsevier.com/books/handbook-of-energy-efficiency-in-buildings/desideri/978-0-12-812817-6

## Slide 19: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXAMPLE

## Slide 20: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 20 single houses, one sports hall and one junior school. All buildings are connected to the main electricity grid and all except for the school to the central natural gas network. The school has a central biomass boiler for space heating. The sports hall and some of the houses have solar collectors for DHW, while the sports hall has PV panels integrated on its envelope to cover partially cooling and lighting demands.
Available data: The total renewable energy on-site and the total thermal and electrical energy consumption of all buildings in the neighborhood
Calculate the percentage ratio of renewable energy on-site in total
primary energy consumption (RES & conventional)

## Slide 21: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
* For single houses the consumptions are given as a total aggreggated value for all the buildings
Available data
Steps 1 -2
Calculated annual energy consumption | Sports hall | School | Single houses (20)* | Total
Thermal energy (natural gas) (kWhth) | 108100 |  | 295324 | 403424
Electrical energy from grid (kWhe) | 45564 | 51347 | 128466 | 225377
Thermal energy from RES (kWhth,RES) | 30900 | 46432 | 21411 | 98743
Electrical energy from RES (kWhth,RES) | 12605 |  |  | 12605
HVAC systems (heating, cooling, domestic hot water) | Central natural gas boiler for heating. Central HP for cooling. Solar collectors for domestic hot water. | Central biomass boiler for heating. Local HP for space cooling. Electric heaters for domestic hot water. | Central natural gas boiler for heating and domestic hot water. Local HP for space cooling. Solar collectors for domestic hot water. | 

## Slide 22: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 3
Calculate the total primary energy renewable thermal energy consumption for all energy carriers in all buildings in the neighborhood
Step 4
Calculate the total primary renewable electrical energy consumption for all the buildings in the neighborhood
Step 5
Calculate the total primary thermal energy consumption
National conversion factor
X
Fuels
52311 x 1.05 = 54927 kWhth
National conversion factor
X
Electricity
= 12605 x 2.9 = 36555 kWh
46432 x 1.00 = 46432 kWhth
Natural Gas
Biomass
+
= 101359 kWh
𝐸𝑝,th = 403424 x 1.05 = 423595 kWh
Natural Gas
Step 6
Calculate the total primary electrical energy consumption
𝐸𝑝,el = 225377 x 2.9= 653593 kWh
Electricity

## Slide 23: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
Step 7
Calculate the total annual primary energy from renewables,
𝐸𝑝,Ren = (101359 + 36555) = 137913 kWh
Step 8
Calculate the total annual primary energy consumption 𝐸𝑝
Step 9
Calculate the percentage ratio of renewable energy on-site, on total
primary energy consumption (RES & conventional)
𝐸𝑝 = (423595 + 653593) = 1077189 kWh
11.4 %
137913 kWh
1077189 + 137913 kWh
______
x
100

## Slide 24: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
EXERCISE

## Slide 25: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
In an existing neighborhood, there are 22 single houses, one kindergarten and one junior school. All buildings are connected to the main electricity grid and all of them are equipped with central boilers (natural gas or fuel oil). Domestic hot water is covered by solar collectors in some houses, in the kindergarten and in the school.
The kindergarten and some of the houses have PV panels integrated on their envelope to cover partially cooling and lighting demands.
Available data: The total renewable energy on-site and the total thermal and electrical energy consumption of all buildings in the neighborhood
Calculate the percentage ratio of renewable energy on-site in total
primary energy consumption (RES & conventional)

## Slide 26: B.3.7 – SHARE OF RENEWABLE ENERGY ON-SITE IN TOTAL PRIMARY ENERGY CONSUMPTION FOR BUILDING OPERATIONS
* For single houses the consumptions are given as a total aggreggated value for all the buildings
Available data
Steps 1 -2
Calculated annual energy consumption | kindergarten | School | Single houses (22)* | Total
Thermal energy (kWhth) | 52470 (natural gas) | 112929 (natural gas) | 382765 (fuel oil) | 
Electrical energy from grid (kWhe) | 45564 | 51347 | 128466 | 
Thermal energy from RES (kWhth,RES) | 6297 | 4616 | 32621 | 
Electrical energy from RES (kWhth,RES) | 12600 |  | 66230 | 
HVAC systems (heating, cooling, domestic hot water) | Central natural gas boiler for space heating. Local HP for space cooling. Solar collectors for domestic hot water. PV panels | Central natural gas boiler for space heating. Local HP for space cooling. Solar collectors for domestic hot water | Central boiler (fuel oil) for space heating and domestic hot water. Local HP for space cooling. Solar collectors for domestic hot water. PV panels |