## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: C.2.3– CONSUMPTION OF POTABLE WATER IN RESIDENTIAL BUILDINGS
C.2.3– CONSUMPTION OF POTABLE WATER IN RESIDENTIAL BUILDINGS | 
ISSUE | CATEGORY
C. Water | C.2 Water Consumption
Residential Buildings)
See also Β.4.3 of Building Scale

## Slide 3: C.2.3– CONSUMPTION OF POTABLE WATER IN RESIDENTIAL BUILDINGS
BACKGROUND
The Mediterranean region holds only 3% of global water resources but hosts over 50% of the world's water poor populations, around 180 million people
In the Middle East and North Africa region, 60% of the population live in areas of high or very high water-stress, compared to the global average of 35%.
Source: https://ufmsecretariat.org/wp-content/uploads/2018/01/water-report-2017.pdf
Annual natural renewable water resources per capita in the Main Mediterranean
Source: https://www.medecc.org/scientific-basis-of-water-food-energy-part-of-the-medecc-report/

## Slide 4: C.2.3– CONSUMPTION OF POTABLE WATER IN RESIDENTIAL BUILDINGS
BACKGROUND
Source: https://www.eea.europa.eu/publications/horizon-2020-mediterranean-report/file
Water Exploitation Index (WEI) for natural renewable freshwater resources in Mediterranean countries (2005–2010)

## Slide 5: C.2.3– CONSUMPTION OF POTABLE WATER IN RESIDENTIAL BUILDINGS
BACKGROUND
https://knoema.com/jgnqhdf/water-consumption-by-country
Renewable freshwater resources

## Slide 6: C.2.3– CONSUMPTION OF POTABLE WATER IN RESIDENTIAL BUILDINGS
BACKGROUND
https://knoema.com/jgnqhdf/water-consumption-by-country

## Slide 7
INDICATOR
C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
Indicator | Unit | Data source
Annual potable water consumption per occupant | l/occupant/year | Metered data
If metered data aren’t available, estimated data shall be used.
Estimated data are used for evaluating retrofit scenarios in planning and decision-making processes
The source of data must always be clearly declared.

## Slide 8: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
INTENT
Make efficient use of water resources
https://www.right2water.eu/
Right to water is an European citizens initiative launched to ensure that water remains a public service and a public good.

## Slide 9
DESCRIPTION
The indicator measures the potable water consumption of sanitary fittings/devices and water consuming appliances by residential population.
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS

## Slide 10
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
BOUNDARY & SCOPE
The assessment boundary includes all residential buildings in the neighbourhood.
The potable water consumption is calculated based on metered data from water consuming appliances and sanitary fittings in the buildings.
The scope of the indicator includes the use of potable water for:
drinking water;
water for sanitation;
domestic hot water;
water for washing machine;
water for cleaning
Not taken into account
Water consumption in the common use spaces of residential buildings
Water consumption for watering

## Slide 11
ASSESSMENT METHOD – METERED DATA
The calculation steps are the following:
For each residential building in the neighborhood collect actual data of annual potable water consumption, [l]. It is preferable to consider actual data from longer records (e.g. three year data) or at least 12 consecutive months.
For each residential building in the neighborhood calculate the average annual potable water consumption, [l]
Sum the annual potable water consumption of each building up to an aggregated annual total potable water consumption, [m3].
Estimate the total number of residential buildings’ occupants.
Calculate the indicator’s value as: annual total potable water consumption (step 3) / number of occupants (step 4), [l /occupant].
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
l /occupant

## Slide 12
ASSESSMENT METHOD – ESTIMATED DATA
The calculation steps are the following:
For each residential building in the neighborhood estimate the annual potable water consumption, [l] for the various sanitary devices/fittings (i.e. toilets, taps and showers) and water using appliances (i.e. dishwashers and washing machines). Consumption rates are determined through specific data from manufacturer specifications on labels or from data libraries. The specific usage factors as well as the annual operation of the building have to be defined by the user.
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
For each sanitary device/fitting or water using appliance:
Daily consumption (l/occupant.day) = Consumption rate (l/min)  Usage factor (min/occupant.day)
Daily consumption (l/occupant.year) = Daily consumption (l/occupant.day)  Building operation (days/year)

## Slide 13: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
ASSESSMENT METHOD – ESTIMATED DATA
Typical water consumption rates
Toilet flushing : 9 l
Bath : 150 l
Shower: 15 l/min
Washing hands, face, teeth : 10-15 l/min
Washing machine : 150 l
Dishwasher: 50 l
Washing fruits/vegetables : 15 l/min
Washing dishes 150 l/day

## Slide 14: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
ASSESSMENT METHOD – ESTIMATED DATA
Source: ANSI/ASHRAE/ICC/USGBC/IES Standard 189.1-2017
https://www.ashrae.org/technical-resources/bookstore/standard-189-1
Minimum requirements of water consumption in «Green Buildings»

## Slide 15
ASSESSMENT METHOD – ESTIMATED DATA
Sum the annual potable water consumption of each building up to an aggregated annual total potable water consumption, [l].
Estimate the total number of residential buildings’ occupants.
Calculate the indicator’s value as: annual total potable water consumption (step 2) / number of occupants (step 3), [l /occupant].
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
l /occupant

## Slide 16
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
REFERENCES and STANDARDS
Council Directive 98/83/EC on the quality of water intended for human consumption Brussels: European Council. http://data.europa.eu/eli/dir/1998/83/oj
COM(2017) 753 final 2017/0332 (COD). Proposal for a Directive of the European parliament on the quality of water intended for human consumption (recast). Brussels: European Commission. https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A52017PC0753
Directive (EU) 2020/2184 of the European parliament on the quality of water intended for human consumption (Recast). ). Brussels: European Commission. http://data.europa.eu/eli/dir/2020/2184/oj
EU Environment - Water, European Commission. https://ec.europa.eu/environment/water/index_en.htm

## Slide 17
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
REFERENCES and STANDARDS
ASHRAE Standard 189.1 - Design of High-Performance Green Buildings. https://www.ashrae.org/technical-resources/standards-and-guidelines/read-only-versions-of-ashrae-standards

## Slide 18: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
EXAMPLE

## Slide 19: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
In an existing neighborhood, there are 5 small residential buildings, 15 single houses, one office building and one junior school.
Available data: The floor areas, the number of occupants and the average annual water consumption of all buildings in the neighborhood
Calculate the annual potable water consumption.

## Slide 20
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
 | Useful internal floor area (m2) | Garden area (m2) | Occupants* | Total annual water consumption/ common spaces (m3)
Office | 1045 | 183 | 102 | 1058.8 / 164.7
School | 1847 | --- | 220 | 346.6 / ---
Single houses (15) | 1805 | 420 | 42 | 2023.8** / ---
Residential buildings (5) | 3322 | 875 | 96 | 3936.3 / 682.5
* Employees, students ή residents
** Default water consumption for garden watering: 0.6 m3/m2 garden area
Available data
For single houses and residential buildings the internal floor area and the annual water consumption are given as a total aggreggated value for all the buildings within the category
Step 1

## Slide 21
C.2.3– POTABLE WATER CONSUMPTION
IN RESIDENTIAL BUILDINGS
Single Houses: Subtract annual water consumption for garden watering from the annual total water consumption
2023.8m3 – (420m2 * 0.6 m3/m2 ) = 1771.8 m3 = 1771800 l
Residential buildings : Subtract annual water consumption for common spaces from the annual total water consumption
3936.3 m3 – 682.5 m3 = 3253.8 m3 = 3253800 l
Calculate the total potable water consumption for residential buildings (single houses & residential buildings)
1771800 l + 3253800 l = 5708.1 l = 5025600 l
Calculate the total number of residential buildings’occupants
(42+96) = 138 occupants
Calculate the annual potable water consumption per occupant
5025600 l

=
138 occupants
Step 2
Step 4
Step 5
36417.4 l/occupant
Step 3

## Slide 22: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
EXERCISE

## Slide 23: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
In an existing neighborhood, there are 22 single houses, one kindergarten and one junior school.
Available data: The floor areas, the number of occupants and the average annual water consumption of all buildings in the neighborhood
Calculate the annual potable water consumption.

## Slide 24: C.2.3– POTABLE WATER CONSUMPTION IN RESIDENTIAL BUILDINGS
Available data
 | Useful internal floor area (m2) | Garden area (m2) | Occupants* | Total annual water consumption/ common spaces (m3)
Kindergarten | 456 | 245 | 86 | 445.1 / 176.4
School | 2151 | --- | 315 | 355.6 / ---
Single houses (22) | 2530 | 748 | 67 | 3149.7** /---
For single houses the floor areas, the occupants and the annual water consumption are given as a total aggreggated value for all the buildings
* Employees, students ή residents
** Default water consumption for garden watering: 0.6 m3/m2 garden area