## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: F.2.3 – BICYCLE NETWORK
F.2.3 – BICYCLE NETWORK | 
ISSUE | CATEGORY
F. Transportation and Mobility | F.2. Green Mobility

## Slide 3: F.2.3 – BICYCLE NETWORK
BACKGROUND
The green mobility policy goal is to “reduce the environmental impact of mobility in terms of greenhouse gas (GHG) emissions, air pollution, and noise.”
The Green Mobility objective proposes three sub-goals for each of the three key dimensions— climate change mitigation, air pollution, and noise pollution.
According to UN Environment’s Global Report on walking and cycling (2016), up to 60% of city trips are made by bike in Chinese cities while in African cities the share is closer to 5%.
Switching from a car to a bicycle saves 150 g of CO2 per kilometre. Each 7 km by bicycle will save an emission of 1 kilogram of CO2 as compared to the same distance covered by car. In a five-year period, Dutch people avoided 1.41 million tonnes of CO2 each year through cycling, saving equivalent to 54.4 million trees being planted each year.
In Europe, for short trips under 5 km, the share of cycling varies from 12% (Finland) to 39% (the Netherlands). The average trip length for cycling is around 3 km in most European countries.

## Slide 4: F.2.3 – BICYCLE NETWORK
BACKGROUND
Overview of the state of EU national cycling strategies

## Slide 5: F.2.3 – BICYCLE NETWORK
BACKGROUND
Non-motorized transport (walking and bicycling) accounts for a large share of all urban trips made across the Middle East and North Africa (MENA) region.
Bicycle usage, as a daily mode of travel, in major Tunisian cities is low, 0.8% of the modal share in Sfax and less than 1% in Tunis according to the World Bank report (Source: https://houloul.org/en/2020/12/13/new-modes-of-transport-in-tunisia/)
Walking and bicycling in Cairo was estimated at 32% in 2001. Current surveys show a 52% share for non-motorized transport modes in Shebin ElKom and 31% in Fayoum. Reasons behind this high share can be estimated to be relatively short distances travelled to schools, universities, and factories, as well as the costs associated to owning a vehicle
Source: https://info.undp.org/docs/pdc/Documents/EGY/00045900_Final%20Approved%20Project%20Document%20Egypt%20Transport.pdf

## Slide 6: F.2.3 – BICYCLE NETWORK
INDICATOR
Indicator | Unit | Data source
Aggregate length of bicycle paths in the area per inhabitant. | m /inhabitant | Thematic map – Geographic Information System Or Estimation

## Slide 7: F.2.3 – BICYCLE NETWORK
INTENT
Promote cycling as an alternative to vehicle use by providing safe and efficient mobility networks.
Travelling by bicycle means less cars on the roads which reduces traffic congestion.
Efficient alternative and environmentally-friendly
modes of transport are key to not only improve
mobility but the quality of life as well.
Source: EU Cycling Strategy, European Cyclists’ Federation. https://ecf.com/eu_cycling_strategy

## Slide 8: F.2.3 – BICYCLE NETWORK
GENERAL INFORMATION
Std 189.1 Design of High-Performance Green Buildings
https://www.ashrae.org/technical-resources/standards-and-guidelines/read-only-versions-of-ashrae-standards

## Slide 9: F.2.3 – BICYCLE NETWORK
For the calculations, bicycle paths taken into account should be physically separated from traffic roads and not be part of a “shared space”
BOUNDARY & SCOPE
The assessment boundary includes the whole neighborhood.
A “shared space” is an urban design approach that minimizes the segregation between modes of road user (car, pedestrian, bicycle, etc.) in order to make safe space for every type of mobility; the shared space is to be used by anyone. This can be done through minimizing traffic signs, road surface markings, enforcing speed reduction down to 15-20 kmh.

## Slide 10: F.2.3 – BICYCLE NETWORK
The calculation steps are the following:
Estimate/Calculate the total number of inhabitants in the neighborhood
Calculate the total length of bicycle paths/lanes in the neighborhood, [m]
Calculate the indicator’s value as the ratio of total length of bicycle paths (step 2) to the total number of inhabitants (step 1) in the neighborhood, [m/inhabitant]
ASSESSMENT METHOD
m/inhabitant

## Slide 11: F.2.3 – BICYCLE NETWORK
REFERENCES and STANDARDS
Global Platform for Sustainable Cities – Urban Sustainability Framework. https://www.thegpsc.org/
Cycling, the better mode of transport,
https://www.unep.org/news-and-stories/story/cycling-better-mode-transport
European Commission, Mobility and Transport, Cycling
https://transport.ec.europa.eu/transport-themes/clean-transport-urban-transport/cycling_en
European Cyclists’ Federation, The state of national cycling strategies in Europe (2021), https://ecf.com/system/files/The_State_of_National_Cycling_Strategies_2021_final_0.pdf
Sustainable Urban Mobility in the Middle East and North Africa, https://unhabitat.org/sites/default/files/2013/06/GRHS.2013.Regional.Middle.East_.and_.North_.Africa.pdf
UNECE - Collection Methodology for Key Performance Indicators for Smart Sustainable Cities
Notes: MARINA

## Slide 12
REFERENCES and STANDARDS
https://https://road-safety.transport.ec.europa.eu/eu-road-safety-policy/priorities/safe-road-use/cyclists/walking-and-cycling-transport-modes_en
F.2.3 – BICYCLE NETWORK
Walking and cycling as transport modes

## Slide 13
REFERENCES and STANDARDS
https://www.ncl.ac.uk/media/wwwnclacuk/ceser/files/Understanding%20Cities.pdf
https://unhabitat.org/planning-and-design-for-sustainable-urban-mobility-global-report-on-human-settlements-2013/
http://www.eltis.org/discover/news/interreg-presents-good-practice-sustainable-urban-mobility-and-sumps
F.2.3 – BICYCLE NETWORK

## Slide 14: F.2.3 – BICYCLE NETWORK
EXAMPLE

## Slide 15: F.2.3 – BICYCLE NETWORK
In an existing neighborhood, the total population is 2500 inhabitants.
Using maps it was measured that there is 300m of bicycle path that were safe and separated from traffic roads.
Available data: The total population and the bicycle path length
Calculate the total length of bicycle paths in the area per inhabitant.

## Slide 16: F.2.3 – BICYCLE NETWORK
Step 1
Total population : 2500 inhabitants
Step 2
Total length of bicycle paths : 300 m
Step 3
Calculate the total length of bicycle paths per inhabitant
Total number of inhabitants
Total length of bicycle paths
300 m
2500 inhabitants
0.12 m/inhabitant

## Slide 17: F.2.3 – BICYCLE NETWORK
EXERCISE

## Slide 18: F.2.3 – BICYCLE NETWORK
In an existing neighborhood, the total population is 500 inhabitants.
There is one bicycle path separated from traffic roads that is crossing the neighborhood, with a total length of 40m, and a bicycle path of 30 m that is a part of a shared space
Calculate the total length of bicycle paths in the area per inhabitant.