## Slide 1
Training Module 4
Calculating the assessment
criteria of
SNTool – Neighbourhood Scale

## Slide 2: I.1.1 – GREENHOUSE GAS EMISSIONS
I.1.1 – GREENHOUSE GAS EMISSIONS | 
ISSUE | CATEGORY
I. CLIMATE CHANGE: Mitigation and Adaptation | I.1 Climate Change Mitigation
See also C.1.2 of Building Scale

## Slide 3: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND
-22%
-1265 mil ton CO2 eq.
-20% -40%

## Slide 4: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND
A carbon dioxide equivalent or CO2 equivalent (CO2eq) is a metric measure used to compare the emissions from various greenhouse gases on the basis of their global-warming potential (GWP), by converting the amounts of other gases to the equivalent amount of carbon dioxide with the same global warming potential.
Πηγή: IPCC

## Slide 5: I.1.1 – GREENHOUSE GAS EMISSIONS
INDICATOR
Indicator | Unit | Data source
Total amount of greenhouse gases (CO2 equivalent emissions ) generated from buildings’ operation over a calendar year per inhabitant | t CO2 eq./inhabidant | Estimation
GHG
For the calculation of the indicator only residents of the neighborhood and not working people in the area

## Slide 6: I.1.1 – GREENHOUSE GAS EMISSIONS
INTENT
Μinimise the total greenhouse gas emissions from buildings’ operations.

## Slide 7: I.1.1 – GREENHOUSE GAS EMISSIONS
DESCRIPTION
The indicator measures the contribution of the greenhouse gas (GHG) emissions associated with the building’s operational phase on the earth's global warming or climate change.
The Global Warming Potential (GWP) was developed to allow for the comparison of the impact on global warming caused by different gases (such as carbon dioxide, methane, nitrous oxide, or chlorofluorocarbons). It is a measure of how much energy the emissions of 1 ton of a gas will absorb over a given period of time, relative to the emissions of 1 ton of carbon dioxide (CO2)
A higher GWP means a larger warming effect
in that period of time (usually 100 years).

## Slide 8: I.1.1 – GREENHOUSE GAS EMISSIONS
ASSESSMENT METHOD
The calculation method for the contribution of buildings; operation to greenhouse gas emissions, is provided by the ISO Standard 14067
ISO Standard 14040 also provides a general reference
It is often referred to as carbon footprint of the buildings

## Slide 9: I.1.1 – GREENHOUSE GAS EMISSIONS
In the calculations the following energy uses should be considered:
heating,
cooling,
mechanical ventilation,
domestic hot water
lighting
auxilliaries
BOUNDARY & SCOPE
The assessment boundary includes all buildings in the neighbourhood.

## Slide 10: I.1.1 – GREENHOUSE GAS EMISSIONS
The calculation steps are the following:
For each building (residential and non-residential) in the neighborhood calculate or collect actual data for the annual amount of each fuel (e.g. liters of oil, cubic meters of natural gas), the heat/cold from district networks, or electricity consumption (kWh) for the energy uses taken into account
ASSESSMENT METHOD
Calculated data should be over a typical year, according to CEN standards that support EPBD
Actual data from monitoring or from bills / utilities, for a 3years-period.
For each building in the neighborhood calculate the average annual consumption per fuel, district heat/cold or electricity, for the energy uses taken into account

## Slide 11: I.1.1 – GREENHOUSE GAS EMISSIONS
ASSESSMENT METHOD
 | Qfuel,i = annual quantity of i-th fuel [m3/a or kg/a] Qel = annual quantity of electrical energy from the grid [kWh/a] Qdh = annual quantity of energy from district heating/cooling [kWh/a] LHVi = lower heating value of the i-th fuel [kWh/m3 or kWh/kg] kem,i = CO2 eq. emission factor of the i-th fuel [t CO2/kWh] kem,el = CO2 eq. emission factor of the electrical energy from the grid [t CO2/kWh] kem,dh = CO2 eq. emission factor of energy from district heating/cooling [t CO2/kWh]
Calculate the aggregated annual consumption per energy source (fuel, district heat/cold, electricity), for all the buildings in the neighborhood
Calculate the total emissions of CO2 eq. related to building operations, using the following formula:
Notes: MARINA

## Slide 12: I.1.1 – GREENHOUSE GAS EMISSIONS
ASSESSMENT METHOD
Calculate the current population of the neighbourhood (permanent residents)
Calculate the indicator’s value as the ratio of the total emissions of CO2 eq. related to building operations (step 4) to the total neighborhood’s population (step 5), [t CO2eq./inhabidant]
t CO2eq./inhabidant

## Slide 13: I.1.1 – GREENHOUSE GAS EMISSIONS
ISO 14067:2013 - Greenhouse gases -- Carbon footprint of products -- Requirements and guidelines for quantification and communication. Geneva: International Organization for Standardization.
ISO 14040:2006 - Environmental management -- Life cycle assessment -- Principles and framework. Geneva: International Organization for Standardization.
ISO 37120: Sustainable cities and communities - Indicators for city services and quality of life
Directive (EU) 2015/652 laying down calculation methods and reporting requirements pursuant to Directive 98/70/EC of the European Parliament and of the Council relating to the quality of petrol and diesel fuels. https://eur-lex.europa.eu/legal-content/EN/TXT/PDF/?uri=CELEX:32015L0652&from=EN
JRC: 2013. How to develop a sustainable energy action plan (SEAP) in the Southern Mediterranean Partner Countries, JRC88817. Joint Research Centre, European Commission. http://publications.jrc.ec.europa.eu/repository/handle/JRC88817
REFERENCES and STANDARDS

## Slide 14: I.1.1 – GREENHOUSE GAS EMISSIONS
EXAMPLE

## Slide 15: I.1.1 – GREENHOUSE GAS EMISSIONS
In an existing neighborhood, there are 10 small residential buildings, one office building and one junior school. All buildings are connected to the main electricity grid and most of them to the central natural gas network.
Available data: The total number of inhabitants and the average annual fuel and electrical energy consumption of all buildings in the neighborhood
Calculate the total emissions of CO2 eq. related to building operations per inhabitant.

## Slide 16: I.1.1 – GREENHOUSE GAS EMISSIONS
For residential buildings the annual consumptions are given as a total aggreggated value for all the buildings within the category
Available data
 | Office | School | Residential buildings (10)
Annual natural gas consumption (m3) | 10769 |  | 23298
Annual fuel oil consumption (lt) |  | 19105 | 
Annual electricity consumption (kWh) | 21624 | 44765 | 84882
Lower heating value of natural gas [kWh/m3] | 10.3 |  | 10.3
Lower heating value of fuel oil [kWh/lt] |  | 9.9 | 
CO2 eq. emission factor of fuels [kg CO2 eq./KWh] | 0.237 | 0.305 | 0.237
CO2 eq. emission factor of electrical energy [kg CO2 eq./KWh] | 1.167 |  | 
Total inhabitants | 500 |  | 
Steps 1,2,5

## Slide 17: I.1.1 – GREENHOUSE GAS EMISSIONS
Step 6
Calculate the total annual consumption per energy source (fuel, district heat/cold, electricity) for all the buildings in the neighborhood
Natural gas (10769 + 0 + 23298) = 34067 m3
Step 4
Calculate the total emissions of CO2 eq. related to building operations, for all the buildings in the neighborhood
Fuel oil (0 + 19105 + 0) = 19105 lt
Electricity (21624 + 44765 + 84882) = 151271 kWh
Natural gas (34067 m3 x 10.3 kWh/m3 x 0.237 kgCO2 eq./kWh) = 83161 kgCO2 eq
Fuel oil (19105 lt x 9.9 kWh/m3 x 0.305 kgCO2 eq./kWh ) = 57688 kgCO2 eq
Electricity (151271 kWh x 1.167 kgCO2 eq./kWh ) = 176533 kgCO2 eq
Total CO2 eq. emissions (83161 + 57688 + 176533) = 317382 kgCO2 eq

## Slide 18: I.1.1 – GREENHOUSE GAS EMISSIONS
Step 6
Calculate the total CO2 eq. emissions per inhabitant
Total number of inhabitants
317382 kgCO2 eq

=
Total CO2 eq. emissions
500 inhabitants
634.8
kgCO2 eq/inhabitant

## Slide 19: I.1.1 – GREENHOUSE GAS EMISSIONS
EXERCISE

## Slide 20: I.1.1 – GREENHOUSE GAS EMISSIONS
In an existing neighborhood, there are 10 small residential buildings, one office building and one hospital. All buildings are connected to the main electricity grid and most of them to the central natural gas network.
Available data: The total number of inhabitants and the average annual fuel and electrical energy consumption of all buildings in the neighborhood
Calculate the total emissions of CO2 eq. related to building operations per inhabitant.

## Slide 21: I.1.1 – GREENHOUSE GAS EMISSIONS
For residential buildings the annual consumptions are given as a total aggreggated value for all the buildings within the category
Available data
 | Office | Hospital | Residential buildings (10)
Annual natural gas consumption (m3) | 33172 |  | 20298
Annual fuel oil consumption (lt) |  | 92151 | 
Annual electricity consumption (kWh) | 102591 | 211460 | 84882
Lower heating value of natural gas [kWh/m3] | 10.3 |  | 10.3
Lower heating value of fuel oil [kWh/lt] |  | 9.9 | 
CO2 eq. emission factor of fuels [kg CO2 eq./KWh] | 0.237 | 0.305 | 0.237
CO2 eq. emission factor of electrical energy [kg CO2 eq./KWh] | 1.167 |  | 
Total inhabitants | 1000 |  | 
Steps 1,2,5