## Slide 1
Training Module 5
Calculating the assessment
criteria of
SCTool – City Scale

## Slide 2: SMC SCTool - City Scale
The purpose  to contextualize the Generic Framework, taking into account urban specific features
The result  a final assessment score, that indicates the overall sustainability performance of a city
The assessment process  Starting from a set of criteria it’s necessary to follow a mathematical procedure in three steps:
  Characterization
  Normalization
  Aggregation

## Slide 3: SMC SCTool - City Scale
Structure of SMC SCTool
10 Issues
39 Categories
99 Criteria / Indicators
10 KPIs

## Slide 4
The process is composed in three steps:
Selection of active criteria
  It’s very important to select the active criteria because they represent the stakeholders’ needs and objectives. They are the most relevant and measurable within the city specific context.
Definition of benchmarks for criteria / indicators
  A benchmark represents a reference performance, while scores define the level of performances reached by the city.
Assignment of weights to indicators, categories and issues
  The weights assignment is a participative process and it has to reflect the local priorities and policies.

## Slide 5
The sustainability score is articulated in 3 main steps:
Characterization: Neighborhood’s performance is quantified through indicators associated with each criterion
Normalization: Indicators’ values are dimensionalized and rescaled in a suitable interval, called normalization interval. The normalization consists in the assignment of a score to the indicator value.
Aggregation: Normalized scores are combined through weighted sums to produce the final sustainability score.

## Slide 6
Characterization step
Input | Output
Experimental / Design data | Indicators’ values
Normalization step
Input | Output
Indicators’ values | Normalized scores
Aggregation
Input | Output
Normalized scores | Final sustainability score
FINAL SCORE

## Slide 7
Step 1: Characterization
Set of numerical
values
representing city
performance
Assign a numerical value or a description
experimental data or design data
Define indicators
Quantitative or qualitative
Select active criteria
- KPIs are mandatory

## Slide 8
Step 2: Normalization or score assignment
Set of normalized
scores
values between
-1 and +5
HIB, LIB or Qualitative
normalization function or a qualitative description
Dimensionalization and rescaling
in a suitable interval
Indicators’ values
quantitative or qualitative

## Slide 9
Step 2: Normalization or score assignment
Normalized scores
-1
under minimum acceptable performance
minimum acceptable performance
0
slightly above minimum performance
1
substantialy above minimum performance
2
best practice
3
improvement towards excellent performance
4
excellent and ideal performance
5

## Slide 10
Step 2: Normalization or score assignment
HIB – Higher is Better
The higher the indicator value, the better the performance level
LIB – Lower is Better
The lower the indicator value, the better the performance level
Qualitative
Discrete values, describing indicator’s performance
3 main kinds of criteria / indicators
Quantitative

## Slide 11
Step 2: Normalization or score assignment
Increasing functions
Example:
Share of Renewables (%)
Length of Bicycle Paths (m/inhabitant)
Quantitative: HIB – Higher is Better

## Slide 12
Step 2: Normalization or score assignment
Quantitative : HIB – Higher is Better
Benchmark* (minimum acceptable performance and best practice)
Indicator’s value
* Benchmark is defined according to laws/regulations, technical standards, statistics data, typical performance, simulation and modelling

## Slide 13
Step 2: Normalization or score assignment
Quantitative : HIB – Higher is Better
V0 = indicator’s value for Normalized Score = 0
V5 = indicator’s value for Normalized Score = 5
Vi = indicator’s value
If Vi < V0, Normalized Score = -1
If Vi > V5, Normalized Score = 5
If V0 <= Vi <= V5, Normalized Score = = 0 + (Vi-V0) x ((5-0) / (V5-V0))
**If benchmarks are not available, they are computed starting from some reference values (two normalized scores are associated with two values and benchmarks are recovered by linear extrapolation)

## Slide 14
Step 2: Normalization or score assignment
Quantitative : HIB – Higher is Better
Example
Indicator
Share of renewables on total final thermal energy consumption of buildings (%)
Annual final thermal energy consumption of all buildings in the neighborhood (GWh) | 12.3
Annual final thermal energy generated from renewable sources in the neighborhood (GWh) | 0.42
Share of renewables on total final thermal energy consumption of buildings (%) | 3.4
Audit

## Slide 15
Step 2: Normalization or score assignment
Decreasing functions
Quantitative : LIB – Lower is Better
Example:
Thermal energy consumption for
building operations (kWh/m2)
Unemployment rate (%)

## Slide 16
Step 2: Normalization or score assignment
Benchmark* (minimum acceptable performance and best practice)
Indicator’s value
* Benchmark is defined according to laws/regulations, technical standards, statistics data, typical performance, simulation and modelling
Quantitative : LIB – Lower is Better

## Slide 17
Step 2: Normalization or score assignment
V0 = indicator’s value for Normalized Score = 0
V5 = indicator’s value for Normalized Score = 5
Vi = indicator’s value
If Vi < V5, Normalized Score = 5
If Vi > V0, Normalized Score = -1
If V5 <= Vi <= V0, Normalized Score = 0 + (Vi-V0) x ((5-0) / (V5-V0))
**If benchmarks are not available, they are computed starting from some reference values (two normalized scores are associated with two values and benchmarks are recovered by linear extrapolation)
Quantitative : LIB – Lower is Better

## Slide 18
Step 2: Normalization or score assignment
Quantitative : LIB – Lower is Better
Example
Indicator
Annual total final thermal energy consumption of buildings per total indoor useful floor area (kWh/ m2)
Annual final thermal energy consumption of all buildings in the neighborhood (kWh) | 283793
Total indoor useful floor area of all buildings in the neighborhood (m2) | 3855
Annual total final thermal energy consumption of buildings per total indoor useful floor area (kWh/ m2) | 73.6
Audit

## Slide 19
Step 2: Normalization or score assignment
Qualitative
Descriptions
Normalized Score
Discrete situations, describing indicator’s performance for each normalized score
Example:
Perceived safety of public areas for pedestrians
Community involvement in urban planning activities

## Slide 20
Step 2: Normalization or score assignment
Qualitative
Descriptions
Normalized Score
Discrete situations :
Normalized score V-1 is associated with situation -1
Normalized score V0 is associated with situation 0
Normalized score V3 is associated with situation 3
Normalized score V5 is associated with situation 5
 Neighborhood performance is defined based on comparison with all descriptions

## Slide 21
Step 2: Normalization or score assignment
Qualitative
Example
Indicator
Community involvement in urban planning activities
Audit
Minimum citizens involvement in urban planning activities

## Slide 22
Step 3: Aggregation
Final score
that represents the neighbourhood’s sustainability performance
Sum of weighted scores
for indicators, categories and issues
Assign weights and compute weighted score
for each indicator
Set of normalized scores
a score for each indicator

## Slide 23
Weighted score (WS) of each Indicator (i)
Step 3: Aggregation

## Slide 24
Weighted score (WS) of each Category (c)
Step 3: Aggregation
Weighted score (WS) of each Issue (IS)
Final score (FS) of the project
Sum of Weighted Scores of all Indicators within Category
Sum of Weighted Scores of all Categories within Issue
Sum of Weighted Scores of all Issues

## Slide 25
Indicators
Indicators
Indicators
Categories
E1
Categories
E2
Categories
E3
Issues
E
Issues
A
B
C
D
F
G
F
G
H
I
L
Final score
Step 3: Aggregation