## Slide 1
Training Module 5
Calculating the assessment
criteria of
SCTool – City Scale

## Slide 2: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
A.2.1 – AVAILABILITY OF GREEN URBAN AREAS | 
ISSUE | CATEGORY
A. Use of land | A.2. Green urban areas

## Slide 3: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
BACKGROUND
The amount of vegetated and/or natural surface cover is an indicator of how much “green” space a city has. Green or natural spaces are important to the sustainability of a city. They improve the urban climate, capture atmospheric pollutants, reduce storm runoff, reduce the “heat island” effect and improve quality of life by providing recreational spaces for urban inhabitants

## Slide 4: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
BACKGROUND
Green areas include parks, groves and green urban spaces in general.
Blue areas include rivers, lakes and large water areas in general.

## Slide 5: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
INDICATOR
Indicator | Unit | Data source
Ratio of all vegetated areas within the city boundaries in relation to the total city area | % | Urban area thematic map
Information on green areas should be obtained from municipal recreation and parks departments, planning departments, forestry departments and census. Green areas can be defined from land use/land cover maps.

## Slide 6: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
INTENT
Facilitate climate change adaptation and mitigation, to improve health and quality of life, favouring biodiversity conservation.

## Slide 7: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
Green area is broader than recreation space, and should include both public and private spaces. Green or natural spaces areas should also include green roofs.
Areas that are without green or natural surface cover are assumed to be sealed (i.e. paved or impervious).
BOUNDARY & SCOPE
The assessment boundary includes the whole city.

## Slide 8: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
The calculation steps are the following:
Calculate the total surface of the city, [m2]
Calculate the total surface of green urban areas in the city, [m2]
Calculate the indicator’s value as the percentage ratio of the total surface of green urban areas (step 2) to the total surface of the city (step 1), [%]
ASSESSMENT METHOD
%

## Slide 9: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
REFERENCES and STANDARDS
ISO 37120, Second edition 2018-07, “Sustainable cities and communities — Indicators for city services and quality of life”
IEFCA 2019 edition – Calculation Guideline
United for Smart Sustainable Cities (U4SSC) - Collection Methodology for Key Performance Indicators for Smart Sustainable Cities
Guidelines on best practice to limit, mitigate or compensate soil sealing, Luxembourg: Publications Office of the European Union, 2012. https://ec.europa.eu/environment/soil/pdf/guidelines/pub/soil_en.pdf
https://unhabitat.org/books/urban-planning-for-city-leaders/
https://www.ncl.ac.uk/media/wwwnclacuk/ceser/files/Understanding%20Cities.pdf
Notes: MARINA

## Slide 10: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
EXAMPLE

## Slide 11: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
In a small existing city, of total surface area of 13 square kilometers, 9.5 square kilometers are covered by public and private sealed areas (i.e. paved or impervious).
Calculate the percentage ratio of all vegetated areas within the city boundaries in relation to the total city area .

## Slide 12: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
Step 1
Step 2
Step 3
Calculate the total area of green areas
(13000000 - 9500000) = 3500000 m2
Calculate the percentage ratio of the total surface of green urban areas to the total surface area of the city
3500000 m2
13000000 m2
27 %
100
Total surface: 13000000 m2

## Slide 13: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
EXERCISE

## Slide 14: A.2.1 – AVAILABILITY OF GREEN URBAN AREAS
Calculate the percentage ratio of all vegetated areas within the city boundaries in relation to the total city area .
A small existing city has α total surface area of 608.5 square kilometers (km²). Public and private green and natural areas cover 202.1 km².