## Slide 1
Training Module 5
Calculating the assessment
criteria of
SCTool – City Scale

## Slide 2: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES | 
ISSUE | CATEGORY
B. Energy | B.3. Renewable energy
Solar energy Biomass energy Thermal heat from the air-ground-water Geothermal energy

## Slide 3: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
BACKGROUND – Share of renewable in final energy consumption
Spain
Italy
Greece
Source IEA Data Services. https://www.iea.org/data-and-statistics
Europe

## Slide 4: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
BACKGROUND - Share of renewable in final energy consumption
Jordan
Lebanon
Source IEA Data Services. https://www.iea.org/data-and-statistics
Middle East

## Slide 5: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
BACKGROUND - Total final energy consumption by sector
Tunisia
Source IEA Data Services. https://www.iea.org/data-and-statistics
Africa

## Slide 6: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
INDICATOR
Indicator | Unit | Data source
Share of renewable energy in final energy consumption | % | Estimated or metered data
Data should be gathered from electricity and fuel distributors. Electricity consumption statistics are typically collected in categories of residential, industrial, transportation, commercial and other sector.
If metered data aren’t available, estimated data shall be used.
Estimated data are used for evaluating retrofit scenarios in planning and decision-making processes
The source of data must always be clearly declared.

## Slide 7: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
INTENT
Maximize the use of renewable energy sources.
RED: Renewable Energy Directive 2018/2001
New package of 8 different legislative proposals for
«Clean Energy for All Europeans package»
https://ec.europa.eu/energy/en/topics/energy-strategy-and-energy-union/clean-energy-all-europeans
Ground source
Water source
Wood chips
Wood pellets

## Slide 8: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
Renewable energy sources include geothermal, solar, wind, hydro, tide and wave energy, combustibles and biofuels such as biomass.
Total renewable energy consumption includes both thermal and electrical energy from all sectors : residential, commercial, industrial, transportation and other.
BOUNDARY & SCOPE
The assessment boundary includes the whole city.

## Slide 9: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
The calculation steps are the following:
Calculate the total final energy consumption of the city (RES & conventional), [MWh]
Calculate the total consumption of end-use energy generated from renewable sources within the city, [MWh]
Calculate the indicator’s value as the percentage ratio of total consumption of end-use energy generated from renewable sources (step 2) to the total final energy consumption of the city (step 1), [%]
ASSESSMENT METHOD
Total energy consumption include all fuel types for all sectors.
End-use sectors include residential, commercial, industrial, transportation and other. Commercial ranges from commerce to administration (public buildings), financial and real estate activities, services to business, personal services, education, health and social services. “Other sector” includes sectors such as agriculture that are not explicitly stated. Categories of fuel types include electricity, coal, fuel oil, natural gas, gasoline, diesel, biomass, biofuels and other
%

## Slide 10: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
REFERENCES and STANDARDS
ISO 37120, Second edition 2018-07, “Sustainable cities and communities — Indicators for city services and quality of life”
United for Smart Sustainable Cities (U4SSC) - Collection Methodology for Key Performance Indicators for Smart Sustainable Cities
Solar Engineering of Thermal Processes (4th ed.), John A. Duffie, William A. Beckman, 944 p., ISBN: 978-0-470-87366-3, Wiley, 2013. https://www.wiley.com/en-us/Solar+Engineering+of+Thermal+Processes%2C+4th+Edition-p-9780470873663
Solar Cooling Handbook, A Gudie to Solar Assisted Cooling and Dehumidification Processes, Hans-Martin Henning, Mario Motta, Daniel Mugnier (Editors), 368 p., ISBN 978-3990434383, Ambra Verlag, 2013.
ASHRAE GreenGuide (5th ed.), Design, Construction and Operation of Sustainable Buildings, T. Lawrence, A.K. Darwich, J.K. Means, D. Macauley (Editors), 504 p., Atlanta: ASHRAE, 2018. https://www.ashrae.org/technical-resources/bookstore/ashrae-greenguide-the-design-construction-and-operation-of-sustainable-buildings
Handbook of Energy Efficiency in Buildings (1st ed.), Umberto Desideri and Francesco Asdrubali (Editors), 836 p., ISBN 978-0128128176, Butterworth-Heinemann, 2018. https://www.elsevier.com/books/handbook-of-energy-efficiency-in-buildings/desideri/978-0-12-812817-6
Notes: MARINA

## Slide 11: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
EXAMPLE

## Slide 12: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
A small city has total surface area of 13.1 square kilometers and 72500 citizens. The final energy consumption from conventional and renewable sources is available for all sectors.
Calculate the percentage ratio of the total consumption of end-use energy generated from renewable sources to the total final energy consumption of the city (RES & conventional).

## Slide 13: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
 | Consumption (MWh) |  |  | 
 | Conventional |  |  | RES
 | Electricity | Thermal Energy | Gasoline | 
Residential buildings | 117272 | 217107 |  | 50157
Non-Residential buildings | 150430 | 111470 |  | 52380
Public vehicles +transportation |  | 6065 | 312 | 319
Private vehicles |  | 12506 | 463888 | 
Public lighting | 14576 |  |  | 3644
Step 1
Available data

## Slide 14: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
Step 1
Step 2
Step 3
Calculate the total consumption of energy generated from renewable sources within the city
(50157 + 52380 + 319 + 3644) = 106500 MWh
Calculate the percentage ratio of the total consumption of energy generated from renewable sources to the total final energy consumption of the city (RES & conventional)
106500 MWh
1200125 MWh
9 %
100
Calculate the total final energy consumption of the city (conventional & RES)
(334379 + 50157 + 261900 + 52380 + 6377 + 319 + 476394
14576 + 3644) = 1200125 MWh

## Slide 15: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
EXERCISE

## Slide 16: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
Calculate the percentage ratio of the total consumption of end-use energy generated from renewable sources to the total final energy consumption of the city (RES & conventional). .
A small city has total surface area of 10.4 square kilometers and 44500 citizens. The final energy consumption from conventional and renewable sources is available for all sectors. In the public sector 20% of the consumed electricity in from RES. In Non residential buildings 12% of the consumed electricity is from RES, while 15% of the thermal energy in residential buildings is from RES.

## Slide 17: B.3.1 – FINAL ENERGY DERIVED FROM RENEWABLE SOURCES
Available data
 | Final Consumption (MWh) |  | 
 | Electricity | Fuel Oil | Gasoline
Public buildings & infrastructures | 2470 | 845 | 
Residential buildings | 86984 | 58049 | 
Non-Residential buildings | 65042 | 3149 | 
Public vehicles |  | 1902 | 147
Private & Commercial vehicles |  | 101654 | 141702
Public transport |  | 107 | 
Public lighting | 4654 |  |