## Slide 1
Training Module 5
Calculating the assessment
criteria of
SCTool – City Scale

## Slide 2: D.2.2– SOLID WASTE RECYCLING
D.2.2–SOLID WASTE RECYCLING | 
ISSUE | CATEGORY
D. Solid Waste | D.2 Solid Waste Management
See also D.2.2 of Neighborhood Scale

## Slide 3: D.2.2– SOLID WASTE RECYCLING
BACKGROUND
Waste represents an enormous loss of resources in the form of both materials and energy. Municipal solid waste management, i.e. its collection, treatment and disposal, is of the first priorities for countries.
Municipal Solid Waste is generated by households, commercial and business establishments, institutions (e.g. schools, hospitals), public spaces (e.g. parks, streets) and construction sites. Generally, it is non-hazardous waste composed of food waste, garden waste, paper and cardboard, wood, textiles, nappies (disposable diapers), rubber and leather, plastics, metal, glass, construction and demolition waste etc.
The priority is to minimize this waste, recycle as much as possible and properly treat the small remaining amounts.
Source: https://www.enicbcmed.eu/sites/default/files/2021-03/MEDINA_designed_guidebook_EN_0.pdf

## Slide 4: D.2.2– SOLID WASTE RECYCLING
BACKGROUND - EUROPEAN LIST OF MUNICIPAL WASTE
Source: http://data.europa.eu/eli/dec/2014/955/oj

## Slide 5: D.2.2– SOLID WASTE RECYCLING
BACKGROUND - RECYCLING SIGNS
The Green Dot does not necessarily mean that the packaging is recyclable, will be recycled or has been recycled. It signifies that the producer has made a financial contribution towards the recovery and recycling of packaging in Europe.
Plastic resin codes identify the type of plastic resin used to make the item by providing a 'Resin Identification Code'.
1 - PET, used for drinks bottles and some food packaging: Widely recycled
2 - HDPE, used for cleaning product bottles, milk cartons, etc: Widely recycled
3 - PVC, used for car parts, window fittings, etc: Not easily recyclable
4 - LDPE, used for plastic bags and wrapping, etc: Recycle at specialist points
5 - PP, used for some tubs and trays etc: Widely recycled
6 - PS, used for takeaway boxes, disposable cutlery, etc: Not easily recyclable
7 - Other, used for crisp packets, rice packets etc: Recycle at specialist points
The Mobius Loop indicates that an object is capable of being recycled but not that it will necessarily be accepted in all recycling collection systems or that it has been recycled. Sometimes this symbol is used with a percentage figure in the middle to explain that the packaging contains x% of recycled material.
Glass. Recycle the glass container (bottles, jars, non-food bottles)
Recyclable aluminium. Indicates that the item is made from recyclable aluminium.
Paper, card and wood. Identifies wood-based products from well managed forests independently certified in accordance with the rules of the FSC.
Waste electricals. Explains that you should not place electrical items in your waste bin.
Tidyman. It doesn't relate to recycling but is a reminder to be a good citizen, disposing of the item in the most appropriate manner

## Slide 6: D.2.2– SOLID WASTE RECYCLING
BACKGROUND
Chart: Municipal waste generated per person
| Croatia | Cyprus | France | Greece | Italy | Malta | Slovenia | Spain | Bosnia and Herzegovina | Montenegro | Turkey | Algeria | Egypt | Israel | Jordan | Lebanon | Morocco | Palestine | Tunisia | EU Mediterranean | West Balkans and Turkey | ENP-South
 | 387 | 617 | 509 | 482 | 488 | 600 | 432 | 435 | 349 | 551 | 405 | 258 | 252 | 615 | 420 | 459 | 209 | 365 | 221
Source: Horizon 2020 Mediterranean report
Toward shared environmental information systems
EEA-UNEP/MAP joint report

## Slide 7: D.2.2– SOLID WASTE RECYCLING
BACKGROUND
Chart: Municipal waste recycled
| Croatia | Cyprus | France | Greece | Italy | Malta | Slovenia | Spain | Bosnia and Herzegovina | Montenegro | Turkey | Algeria | Egypt | Israel | Jordan | Lebanon | Morocco | Palestine | Tunisia | EU Mediterranean | West Balkans and Turkey | ENP-South
 | 16 | 18 | 39 | 19 | 42 | 11 | 36 | 33 | 0 | 8 | 1 | 7 | 2.5 | 13 | 10 | 8 | 10 | 2 | 10
Source: Horizon 2020 Mediterranean report
Toward shared environmental information systems
EEA-UNEP/MAP joint report

## Slide 8
INDICATOR
D.2.2– SOLID WASTE RECYCLING
Indicator | Unit | Data source
Total amount of solid waste that is recycled divided by the total amount of solid waste produced in the city | % | Metered data

## Slide 9: D.2.2– SOLID WASTE RECYCLING
INTENT
Promote and develop sustainable waste management

## Slide 10
D.2.2– SOLID WASTE RECYCLING
BOUNDARY & SCOPE
The boundary is the whole city.
Municipal Solid Waste is non-hazardous waste composed of food waste, garden waste, paper and cardboard, wood, textiles, nappies (disposable diapers), rubber and leather, plastics, metal, glass, and refuse (i.e. ash, dirt and dust).

## Slide 11
ASSESSMENT METHOD
The calculation steps are the following:
Calculate the annual total amount of the city’s solid waste that is recycled, [t]. Use data from the most recent complete year
Calculate the annual total amount of solid waste produced in the city, [t]
Calculate the indicator’s value as the percentage ratio of annual total amount of the city’s solid waste that is recycled (step 1) to the annual total amount of solid waste produced in the city (step 2), [%]
D.2.2– SOLID WASTE RECYCLING
%

## Slide 12
D.2.2– SOLID WASTE RECYCLING
REFERENCES and STANDARDS
ISO 37120, Second edition 2018-07, “Sustainable cities and communities — Indicators for city services and quality of life”
United for Smart Sustainable Cities (U4SSC) - Collection Methodology for Key Performance Indicators for Smart Sustainable Cities
Directive (Eu) 2018/851 of the European Parliament and of the Council of 30 May 2018 on Waste http://data.europa.eu/eli/dir/2018/851/oj, amending Directive 2008/98/EC http://data.europa.eu/eli/dir/2008/98/oj
2014/955/ΕΕ - List of Waste referred to in Article 7 of Directive 2008/98/EC http://data.europa.eu/eli/dec/2014/955/oj
UN HABITANT - SOLID WASTE MANAGEMENT IN CITIES https://unhabitat.org/sites/default/files/2019/02/Indicator-11.6.1-Training-Module_Solid-waste-in-cities_23-03-2018.pdf

## Slide 13: D.2.2– SOLID WASTE RECYCLING
EXAMPLE

## Slide 14: D.2.2– SOLID WASTE RECYCLING
A small city, with a total population of 81350 inhabitants, generates annually about 27400 t of municipal waste.
The total amount of municipal waste that are annually collected in the recycling points is 1936 t.
.
Calculate the percentage of solid waste that is collected and recycled.

## Slide 15
D.2.2– SOLID WASTE RECYCLING
Total annual amount of solid waste produced in the city = 27400 t
Step 1
Step 2
Step 3
Total annual amount of recycled solid waste = 1936 t
Calculate the percentage of solid waste that is recycled
1936 t
27400 t
7.1 %
100

## Slide 16: D.2.2– SOLID WASTE RECYCLING
EXERCISE

## Slide 17: D.2.2– SOLID WASTE RECYCLING
A small city generates annually about 28000 t of municipal waste. The annually collected recycled materials from the various recycling bins are : paper 6100 t, plastic 3800 t, aluminum 1000t and glass 1200 t.
Calculate the percentage of solid waste that is collected and recycled