## Slide 1
Training Module 5
Calculating the assessment
criteria of
SCTool – City Scale

## Slide 2: I.1.1 – GREENHOUSE GAS EMISSIONS
I.1.1 – GREENHOUSE GAS EMISSIONS | 
ISSUE | CATEGORY
I. CLIMATE CHANGE: Mitigation and Adaptation | I.1 Climate Change Mitigation
See also I.1.1 of Neighborhood Scale

## Slide 3: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND
The greenhouse gas emissions from all activities within the city are an indicator of the adverse contribution the city is making to climate change.
The Global Warming Potential (GWP) was developed to allow for the comparison of the impact on global warming caused by different gases (such as carbon dioxide, methane, nitrous oxide, or chlorofluorocarbons). It is a measure of how much energy the emissions of 1 ton of a gas will absorb over a given period of time, relative to the emissions of 1 ton of carbon dioxide (CO2)
A higher GWP means a larger warming effect
in that period of time (usually 100 years).

## Slide 4: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND
A carbon dioxide equivalent or CO2 equivalent (CO2-eq) is a metric measure used to compare the emissions from various greenhouse gases on the basis of their global-warming potential (GWP), by converting the amounts of other gases to the equivalent amount of carbon dioxide with the same global warming potential.
Source: IPCC

## Slide 5: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND
-22%
-1265 mil ton CO2 eq.
-20% -40%

## Slide 6: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND – Total GHG emissions (kt of CO2eq)
Source: The World Bank. World Development Indicators https://databank.worldbank.org/reports.aspx?source=2&series=EN.ATM.GHGT.KT.CE&country=MEA
Europe

## Slide 7: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND – Total GHG emissions (kt of CO2eq)
Source: The World Bank. World Development Indicators https://databank.worldbank.org/reports.aspx?source=2&series=EN.ATM.GHGT.KT.CE&country=MEA
Middle East & North Africa

## Slide 8: I.1.1 – GREENHOUSE GAS EMISSIONS
BACKGROUND – Total GHG emissions (kt of CO2eq)
Source: The World Bank. World Development Indicators https://databank.worldbank.org/reports.aspx?source=2&series=EN.ATM.GHGT.KT.CE&country=MEA
Italy
Greece
Spain
Jordan
Lebanon
Tunisia

## Slide 9: I.1.1 – GREENHOUSE GAS EMISSIONS
INDICATOR
Indicator | Unit | Data source
Total amount of greenhouse gases (equivalent carbon dioxide units) generated over a calendar year for all sectors, divided by the current city population | t CO2 eq./inhabidant | Estimation
GHG
Greenhouse gas emissions from all activities within the city, including indirect emissions outside city boundaries

## Slide 10: I.1.1 – GREENHOUSE GAS EMISSIONS
INTENT
Minimise the total greenhouse gas emissions from all activities within a city

## Slide 11: I.1.1 – GREENHOUSE GAS EMISSIONS
End-use sectors include :
residential
commercial
industrial
transportation
other
BOUNDARY & SCOPE
The assessment boundary includes the whole city as well as indirect emissions outside city boundaries.

## Slide 12: I.1.1 – GREENHOUSE GAS EMISSIONS
The calculation steps are the following:
Calculate the total annual final energy consumption per energy source, by all activities within the city, [MWh]
Calculate the total amount of greenhouse gases generated over a calendar year by all activities within the city, including indirect emissions outside city boundaries, using national global warming potential for each energy source, [t CO2 eq]
Calculate the total population of the city, [inhabitants]
Calculate the indicator’s value as the ratio of the total amount of greenhouse gases (step 2) to the total population of the city (step 3), [t CO2eq /inhabitant]
ASSESSMENT METHOD
t CO2eq./inhabidant

## Slide 13: I.1.1 – GREENHOUSE GAS EMISSIONS
ISO 37120, Second edition 2018-07, “Sustainable cities and communities — Indicators for city services and quality of life”
United for Smart Sustainable Cities (U4SSC) - Collection Methodology for Key Performance Indicators for Smart Sustainable Cities
ISO 14067:2013 - Greenhouse gases -- Carbon footprint of products -- Requirements and guidelines for quantification and communication. Geneva: International Organization for Standardization.
ISO 14040:2006 - Environmental management -- Life cycle assessment -- Principles and framework. Geneva: International Organization for Standardization.
Directive (EU) 2015/652 laying down calculation methods and reporting requirements pursuant to Directive 98/70/EC of the European Parliament and of the Council relating to the quality of petrol and diesel fuels. https://eur-lex.europa.eu/legal-content/EL/TXT/PDF/?uri=CELEX:32015L0652&from=EN
REFERENCES and STANDARDS

## Slide 14: I.1.1 – GREENHOUSE GAS EMISSIONS
IPCC: 2014. Fifth Assessment Report of the Intergovernmental Panel on Climate Change. Geneva, Switzerland. https://www.ipcc.ch/report/ar5/syr/
JRC: 2013. How to develop a sustainable energy action plan (SEAP) in the Southern Mediterranean Partner Countries, JRC88817. Joint Research Centre, European Commission. http://publications.jrc.ec.europa.eu/repository/handle/JRC88817
REFERENCES and STANDARDS

## Slide 15: I.1.1 – GREENHOUSE GAS EMISSIONS
EXAMPLE

## Slide 16: I.1.1 – GREENHOUSE GAS EMISSIONS
A small city has total surface area of 13.1 square kilometers and 72500 citizens. The energy consumption for all sectors is available per energy source
Calculate the total emissions of CO2 eq. of the city per inhabitant.

## Slide 17: I.1.1 – GREENHOUSE GAS EMISSIONS
Available data
Step 1
 | Consumption (MWh) |  |  | 
 | Electricity | Fuel Oil | Natural gas | Gasoline
Public buildings | 2457.4 |  | 3423.2 | 
Schools | 947.2 |  | 1887.8 | 
Nurseries | 216.0 | 278.99 |  | 
Residential buildings | 119664.5 | 154224 | 110646.9 | 
Non-Residential buildings | 184417.3 | 21096 | 99556.56 | 
Public vehicles |  | 2276.7 | 725.4 | 440.7
Private vehicles |  | 12506 |  | 463888
Public transport |  | 3152.94 | 100.4 | 
Public lighting | 18219.5 |  |  | 
Total | 325921.9 | 193534.6 | 216340.3 | 464328.7

## Slide 18: I.1.1 – GREENHOUSE GAS EMISSIONS
Step 2
Calculate the total emissions of CO2 eq. per energy source
Natural gas [(216340.3 MWh x 237 kgCO2 eq./MWh )/1000000] = 51.3 tCO2 eq
Step 3
Total population of the the city : 72500 inhabitants
Fuel oil [(193534.6 MWh x 305 kgCO2 eq./MWh )/1000000] = 59.0 tCO2eq
Gasoline [(464328.7 MWh x 299 kgCO2 eq./MWh )/1000000] = 138.8 tCO2eq
Electricity [(325921.9 MWh x 1167 kgCO2 eq./MWh )/1000000] = 380.4 tCO2eq
Step 4
Calculate the total CO2 eq. emissions per inhabitant
Total number of inhabitants
629.5 tCO2 eq

=
Total CO2 eq. emissions
72500 inhabitants
0.009 tCO2 eq/inhabitant
Total = 629.5 tCO2 q

## Slide 19: I.1.1 – GREENHOUSE GAS EMISSIONS
EXERCISE

## Slide 20: I.1.1 – GREENHOUSE GAS EMISSIONS
A small city has total surface area of 10.4 square kilometers and 44500 citizens. The final energy consumption for all sectors is available per energy source
Calculate the total emissions of CO2 eq. of the city per inhabitant.

## Slide 21: I.1.1 – GREENHOUSE GAS EMISSIONS
Available data
 | Consumption (MWh) |  |  | 
 | Electricity | Fuel Oil | Natural gas | Gasoline
Public buildings & infrastructures | 2470 | 207 | 638 | 
Residential buildings | 86984 | 34878 | 23171 | 
Non-Residential buildings | 65042 | 3149 |  | 
Public vehicles |  | 1902 |  | 147
Private & Commercial vehicles |  | 101654 |  | 141702
Public transport |  | 107 |  | 
Public lighting | 4654 |  |  | 
Step 1