## Slide 1
Training Module 6
Case Studies Presentation:
IRBID - Jordan

## Slide 2
Al Nuzha Neighborhood- Greater Irbid Municipality
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
Greater Irbid Municipality/ German Jordanian University

## Slide 3
Climate Conditions
Overview and Key Characteristics of the Pilot
3
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
The climate is classified as Mediterranean semi-arid
Hot and dry summer seasons
Cold and wet winter seasons
climate data |  |  |  |  |  |  |  |  |  |  |  |  | 
month | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Year
mean high °C | 12.7 | 13.9 | 17.6 | 23.3 | 27.9 | 30.9 | 32.5 | 32.7 | 30.8 | 26.8 | 20.1 | 14.6 | 23.7
daily mean °C | 8.5 | 9.4 | 12.4 | 17.1 | 21.4 | 24.6 | 26.5 | 26.6 | 24.6 | 21.0 | 15.0 | 10.2 | 18.1
mean low °C | 4.2 | 4.8 | 7.2 | 10.9 | 14.8 | 18.3 | 20.5 | 20.4 | 18.3 | 15.1 | 9.8 | 5.8 | 12.5

## Slide 4
Overview and Key Characteristics of the Pilot
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities

## Slide 5
Total Study area : 0.96 km2
Residential land use prevails as the dominant land use in the study area.
There is a scarcity of green areas within the study area, represented by just a single parcel accounting for less than 1% of the total area.
The built-up area constitutes 83% of the total study area.
The study area is surrounded by four vital roads:
King Abdullah II street
Makkah Al Mukarrmah street
Baghdad street
Ratib al Batayenah street
Overview and Key Characteristics of the Pilot
5
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities

## Slide 6
Urban Area
6
Sustainable MED Cities
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION

## Slide 7
Urban Area
7
Sustainable MED Cities
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION

## Slide 8
Public Building
8
Sustainable MED Cities
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Level of degradation of the building | Average
Owner | Irbid Chamber of Commerce
Year of construction | 1998
Number of levels above earth | 4
Number of levels underground | 1
Lighting System | LED+ Fluorescent tube+ Halogen lamp
Average U value | 0.57 W/m^2 K for walls
Number of occupants | 1000 visitors + 60 Workers

## Slide 9
Residential Building
9
Sustainable MED Cities
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Level of degradation of the building | The building is recently built with average standards , limestone facades with glass façade windows
Owner | Multi family ownership
Year of construction | 2010
Building method | Stone and Concrete structure
Number of levels above earth | 4
Number of levels underground | 1
Number of occupants | 9 households

## Slide 10
Weaknesses Identified and Objectives to Achieve
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities

## Slide 11
Availability and accessibility of green urban areas.
Green zones density and green areas ratio to neighborhood population.
Total final electrical energy consumption for building/ residential building operations
Total primary energy demand for building operations
Share of renewable energy on-site, relative to total final thermal energy, electric energy , and energy consumption for building operations.
Weaknesses Identified - Al Nuzha Neighborhood
11
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities

## Slide 12
Public Building Weaknesses identified/ Objectives to achieve
12
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
Public Buildings Primary energy consumption
Delivered thermal and electrical energy consumption
Energy from renewable sources in total thermal energy consumption
Embodied non-renewable primary energy
Electrical peak demand for building operations.
Recycled materials
Potable water consumption for irrigation
Heat island effect
Shading of building envelope by vegetation
GHG gas emissions during operation
Decrease primary energy consumption, & lower the urban heat island effect.
Increase the dependency on renewable energy in electrical generation and thermal energy generation.
Conserve the environment by using less resources and less raw material and encourage the purchase of locally produced products.
Increase comfort and wellbeing for the occupant.
The foundation for creating local and national database platforms, facilitating informed decision-making and long-term planning for energy management

## Slide 13
Residential Buildings
Residential Building Weaknesses identified/ Objectives to achieve
13
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
Embodied non-renewable primary energy
Electrical peak demand for building operations.
Recycled materials
Total water consumption
Potable water consumption for irrigation
Heat island effect
Shading of building envelope by vegetation
Creating a welcoming ambiance, boosting space utilization, and fostering community engagement.
Substantial reduction in operational costs for long-term financial benefits.
Reducing dependence on fossil fuels and lowering carbon dioxide (CO2) and greenhouse gas (GHG) emissions.
Decrease the dependence on potable water for irrigation, contributing to water resource conservation, and reducing stormwater runoff.

## Slide 14
Scenario Developed
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
Global 1 (SN Smart Energy - SB (A: PUBLIC) active - SB (B: RESIDENTIAL) passive)

## Slide 15
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
15
Neighborhood Scenarios

## Slide 16
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
16
Building 1 Scenarios: Public Building

## Slide 17
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
17
Building 2 Scenarios: Residential Building

## Slide 18
Scenario Developed
18
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
The Smart Energy Scenario towards Future is a comprehensive plan that promotes renewable energy to tackle climate issues and reduce carbon emissions. incorporating technological advancement, community involvement, and green practices to effectively tackle climate change and contribute towards creating sustainable and livable neighborhoods.The scenario outlines several initiatives with a total budget of 8.22 Million Euros , including :
The use of land and biodiversity to increase energy storage and efficiency.
Implementing renewable energy sources such as EV batteries, EV motors, solar PV, and battery storage will provide affordable access to energy and promote clean and renewable energy sources.
- Improving energy efficiency savings by adopting green technology and insulation enforcement, funding energy storage projects, building a secure energy supply chain and encouraging the production of critical minerals.
- Water conservation through technology advancements, strategic planning and the use of artificial intelligence (AI).

## Slide 19
Scenario Developed
19
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
Public Buildings – Active The application of active systems to improve energy efficiency and energy consumptions on most levels, including changing active mechanical and lighting systems and control devices and updating energy consuming appliances, in addition to introducing some renewable systems that could contribute to lowering energy consumption and increase the building’s adaptation to climate change.
Residential Buildings – Passive The application of passive systems to improve energy efficiency and energy consumption on most levels, including changing glazing systems, addition of insulation to avoid thermal bridges, and introducing shading devices. In addition to introducing some changes in the exposed surface materials that could contribute to lowering energy consumption and increase the building’s adaptation to climate change.

## Slide 20
Participatory Approach
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities

## Slide 21
Participatory approach
21
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
LPC meetings brought together individuals from various sectors and entities, contributing to the formulation of policy direction in the project. This included representatives who played a key role in shaping the project's trajectory, including professionals from :
GIM Department Heads
Irbid Electricity Company
Irbid Public Works Directorate
National Building Council
Royal Scientific Society
Jordan Engineers Association
Academic Professionals

## Slide 22
Lessons Learned and Future Perspectives
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities

## Slide 23
Lessons Learned and Future Perspectives
23
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
Considering more residential and public buildings and other types, sizes, and ages of buildings in order to get more comprehensive insights on the sustainable building system.
Enhancing community engagement: Arranging for using an online virtual platform (e.g., adhocracy) in order to enhance the cocreation process and reach the target respondents more easily and be more inclusive in the cocreation process.
Arranging with the main partner (i.e., the municipality) to include more stakeholders (i.e., a number of experts with different backgrounds) in order to enrich the outcomes through selecting useful indicators and designing the retrofitting scenarios and interventions.

## Slide 24
Lessons Learned and Future Perspectives
24
TRAINING MODULE 6 – PILOT CASE STUDIES PRESENTATION
Sustainable MED Cities
4. Adopting an adaptive governance: to respond to changing circumstances and feedback from the community that are vital for the success of sustainable projects.
5. Employing a measuring and monitoring system: to implement a robust monitoring and evaluation system that helps track progress in order to identify areas for improvement and ensure accountability in achieving sustainability goals.
6. Policy alignment: to align local policies with broader regional and national sustainability goals. This is critical for creating a cohesive and interconnected network of sustainable cities.